## Slide 1: Lecture 20
Chemical Reaction Engineering (CRE) is the field that studies the rates and mechanisms of chemical reactions and the design of the reactors in which they take place.

## Slide 2: Last Lecture Energy Balance Fundamentals
Substituting for

## Slide 3: Web Lecture 20 Class Lecture 16-Thursday
Reactors with Heat Exchange
User friendly Energy Balance Derivations
  Adiabatic
  Heat Exchange Constant Ta
  Heat Exchange Variable Ta Co-current
  Heat Exchange Variable Ta Counter Current

## Slide 4: Adiabatic Operation CSTR
The feed consists of both - Inerts I and Species A with the ratio of inerts I to the species A being 2 to 1.
Elementary liquid phase reaction carried out in a CSTR

## Slide 5: Adiabatic Operation CSTR
Assuming the reaction is irreversible for CSTR, A  B, (KC = 0) what reactor volume is necessary to achieve 80% conversion?
If the exiting temperature to the reactor is 360K, what is the corresponding reactor volume?
Make a Levenspiel Plot and then determine the PFR reactor volume for 60% conversion and 95% conversion. Compare with the CSTR volumes at these conversions.
Now assume the reaction is reversible, make a plot of the equilibrium conversion as a function of temperature between 290K and 400K.

## Slide 6: CSTR: Adiabatic Example
1) Mole Balances:
(exothermic)

## Slide 7: CSTR: Adiabatic Example
2) Rate Laws:
3) Stoichiometry:

## Slide 8: CSTR: Adiabatic Example
4) Energy Balance
Adiabatic, ∆Cp=0

## Slide 9: CSTR: Adiabatic Example
Irreversible for Parts (a) through (c)
(a) Given X = 0.8, find T and V
(if reversible)

## Slide 10: CSTR: Adiabatic Example
Given X, Calculate T and V

## Slide 11: CSTR: Adiabatic Example
(b)
(if reversible)
Given T, Calculate X and V

## Slide 12: CSTR: Adiabatic Example
(c) Levenspiel Plot

## Slide 13: CSTR: Adiabatic Example
(c) Levenspiel Plot

## Slide 14: CSTR: Adiabatic Example
CSTR X = 0.95 T = 395 K
CSTR X = 0.6 T = 360 K

## Slide 15: CSTR: Adiabatic Example
PFR X = 0.6
PFR X = 0.95

## Slide 16: CSTR: Adiabatic Example - Summary
CSTR | X = 0.6 | T = 360 | V = 2.05 dm3
PFR | X = 0.6 | Texit = 360 | V = 5.28 dm3
CSTR | X = 0.95 | T = 395 | V = 7.59 dm3
PFR | X = 0.95 | Texit = 395 | V = 6.62 dm3

## Slide 17: Energy Balance in terms of Enthalpy

## Slide 18: PFR Heat Effects

## Slide 19: PFR Heat Effects
Need to determine Ta

## Slide 20
Heat Exchange:
Need to determine Ta

## Slide 21: Heat Exchange Example: Case 1 - Adiabatic
Energy Balance:
Adiabatic (Ua=0) and ΔCP=0

## Slide 22: User Friendly Equations
Constant Ta e.g., Ta = 300K
B. Variable Ta Co-Current
C. Variable Ta Counter Current
Guess Ta at V = 0 to match Ta0 = Ta0 at exit, i.e., V = Vf

## Slide 23
Coolant Balance:
In - Out + Heat Added = 0
Heat Exchanger Energy Balance
Variable Ta Co-current

## Slide 24: Heat Exchanger Energy Balance Variable Ta Co-current
In - Out + Heat Added = 0

## Slide 25: Heat Exchanger – Example Case 1 – Constant Ta
Elementary liquid phase reaction carried out in a PFR
The feed consists of both inerts I and species A with the ratio of inerts to the species A being 2 to 1.
FA0
FI
Ta
Heat Exchange Fluid
T

## Slide 26: Heat Exchanger – Example Case 1 – Constant Ta
1) Mole Balance:
2) Rate Laws:

## Slide 27: Heat Exchanger – Example Case 1 – Constant Ta
3) Stoichiometry:
4) Heat Effects:

## Slide 28: Heat Exchanger – Example Case 1 – Constant Ta
Parameters:

## Slide 29: PFR Heat Effects
Heat removed
Heat generated

## Slide 30: Heat Exchanger – Example Case 2 – Adiabatic
Energy Balance:
Adiabatic and ΔCP=0
Ua=0
Additional Parameters (17A) & (17B)
Mole Balance:

## Slide 31: Adiabatic PFR

## Slide 32: Example: Adiabatic
Find conversion, Xeq and T as a function of reactor volume
V
rate
V
T
V
X
X
Xeq

## Slide 33: Heat Exchange
Need to determine Ta

## Slide 34: User Friendly Equations
A. Constant Ta (17B) Ta = 300K
Additional Parameters (18B – (20B):
B. Variable Ta Co-Current
C. Variable Ta Countercurrent
Guess Ta at V = 0 to match Ta0 = Ta0 at exit, i.e., V = Vf

## Slide 35: Heat Exchange Energy Balance Variable Ta Co-current
Coolant balance:
In - Out + Heat Added = 0
All equations can be used from before except Ta parameter, use differential Ta instead, adding mC and CPC

## Slide 36: Heat Exchange Energy Balance Variable Ta Co-current
In - Out + Heat Added = 0
All equations can be used from before except dTa/dV which must be changed to a negative. To arrive at the correct integration we must guess the Ta value at V=0, integrate and see if Ta0 matches; if not, re-guess the value for Ta at V=0

## Slide 37: Derive the user-friendly Energy Balance for a PBR
Differentiating with respect to W:

## Slide 38: Derive the user-friendly Energy Balance for a PBR
Mole Balance on species i:
Enthalpy for species i:

## Slide 39: Derive the user-friendly Energy Balance for a PBR
Differentiating with respect to W:

## Slide 40: Derive the user-friendly Energy Balance for a PBR
Final Form of the Differential Equations in Terms of Conversion:
A:

## Slide 41: Derive the user-friendly Energy Balance for a PBR
Final form of terms of Molar Flow Rate:
B:

## Slide 42: Reversible Reactions
The rate law for this reaction will follow an elementary rate law.
Where Ke is the concentration equilibrium constant. We know from Le Chaltlier’s law that if the reaction is exothermic, Ke will decrease as the temperature is increased and the reaction will be shifted back to the left. If the reaction is endothermic and the temperature is increased, Ke will increase and the reaction will shift to the right.

## Slide 43: Reversible Reactions
Van’t Hoff Equation:

## Slide 44: Reversible Reactions
For the special case of ΔCP=0
Integrating the Van’t Hoff Equation gives:

## Slide 45: Reversible Reactions
endothermic reaction
exothermic reaction
KP
T
endothermic reaction
exothermic reaction
Xe
T

## Slide 46: End of Lecture 20