## Slide 1: Lecture 1
Chemical Reaction Engineering (CRE) is the field that studies the rates and mechanisms of chemical reactions and the design of the reactors in which they take place.

## Slide 2: Lecture 1
Introduction
Definitions
General Mole Balance Equation
  Batch (BR)
  Continuously Stirred Tank Reactor (CSTR)
  Plug Flow Reactor (PFR)
  Packed Bed Reactor (PBR)
Chapter 1

## Slide 3: Chemical Reaction Engineering
Chemical reaction engineering is at the heart of virtually every chemical process. It separates the chemical engineer from other engineers.
Industries that Draw Heavily on Chemical Reaction Engineering (CRE) are:
CPI (Chemical Process Industries)
Examples like Dow, DuPont, Amoco, Chevron
Chapter 1

## Slide 4
Chapter 1

## Slide 5
Chemical Plant for Ethylene Glycol (Ch. 5)
Smog (Ch. 1)
Plant Safety
(Ch. 11,12,13)
Lubricant Design (Ch. 9)
Cobra Bites
(Ch. 8 DVD-ROM)
Oil Recovery (Ch. 7)
Wetlands (Ch. 7 DVD-ROM)
Hippo Digestion (Ch. 2)
Chapter 1

## Slide 6: Materials on the Web and CD-ROM
http://www.umich.edu/~elements/6e

## Slide 7: Let’s Begin CRE
Chemical Reaction Engineering (CRE) is the field that studies the rates and mechanisms of chemical reactions and the design of the reactors in which they take place.
Chapter 1

## Slide 8: Chemical Identity
A chemical species is said to have reacted when it has lost its chemical identity.
The identity of a chemical species is determined by the kind, number, and configuration of that species’ atoms.
Chapter 1

## Slide 9: Chemical Identity
A chemical species is said to have reacted when it has lost its chemical identity.
There are three ways for a species to loose its identity:
1. Decomposition CH3CH3  H2 + H2C=CH2
2. Combination N2 + O2  2 NO
3. Isomerization C2H5CH=CH2  CH2=C(CH3)2
Chapter 1

## Slide 10: Reaction Rate
The reaction rate is the rate at which a species looses its chemical identity per unit volume.
The rate of a reaction (mol/dm3/s) can be expressed as either:
  The rate of Disappearance of reactant: -rA
              or as
  The rate of Formation (Generation) of product: rP
Chapter 1

## Slide 11: Reaction Rate
Consider the isomerization
A  B
rA = the rate of formation of species A per unit volume
-rA = the rate of a disappearance of species A per unit volume
rB = the rate of formation of species B per unit volume
Chapter 1

## Slide 12: Reaction Rate
EXAMPLE: AB
  If Species B is being formed at a rate of
  0.2 moles per decimeter cubed per second, i.e.,
  rB = 0.2 mole/dm3/s
Then A is disappearing at the same rate:
-rA= 0.2 mole/dm3/s
The rate of formation (generation of A) is:
  rA= -0.2 mole/dm3/s
Chapter 1

## Slide 13: Reaction Rate
For a catalytic reaction we refer to –rA’ , which is the rate of disappearance of species A on a per mass of catalyst basis. (mol/gcat/s)
NOTE: dCA/dt is not the rate of reaction
Chapter 1

## Slide 14: Reaction Rate
Consider species j:
rj is the rate of formation of species j per unit volume [e.g. mol/dm3s]
rj is a function of concentration, temperature, pressure, and the type of catalyst (if any)
rj is independent of the type of reaction system (batch, plug flow, etc.)
rj is an algebraic equation, not a differential equation
(e.g. -rA = kCA or -rA = kCA2)
Chapter 1

## Slide 15: General Mole Balances
Building Block 1:
Fj0
Fj
Gj
System Volume, V
Chapter 1

## Slide 16: General Mole Balances
Building Block 1:
If spatially uniform:
If NOT spatially uniform:
Chapter 1

## Slide 17: General Mole Balances
Building Block 1:
Take limit
Chapter 1

## Slide 18: General Mole Balances
Building Block 1:
General Mole Balance on System Volume V
FA0
FA
GA
System Volume, V
Chapter 1

## Slide 19: Batch Reactor - Mole Balances
19
Batch
Well-Mixed
Chapter 1

## Slide 20: Batch Reactor - Mole Balances
Integrating
Time necessary to reduce the number of moles of A from NA0 to NA.
when
Chapter 1

## Slide 21: Batch Reactor - Mole Balances
NA
t
Chapter 1

## Slide 22: CSTR - Mole Balances
Steady State
CSTR
Chapter 1

## Slide 23: CSTR - Mole Balances
Well Mixed
CSTR volume necessary to reduce the molar flow rate from FA0 to FA.
Chapter 1

## Slide 24: Plug Flow Reactor - Mole Balances
Chapter 1

## Slide 25: Plug Flow Reactor - Mole Balances
Chapter 1

## Slide 26: Plug Flow Reactor - Mole Balances
Rearrange and take limit as ΔV0
This is the volume necessary to reduce the entering molar flow rate (mol/s) from FA0 to the exit molar flow rate of FA.
Chapter 1

## Slide 27: Plug Flow Reactor - Mole Balances
Steady State
PFR
Chapter 1

## Slide 28: Plug Flow Reactor - Mole Balances
Differientiate with respect to V
The integral form is:
This is the volume necessary to reduce the entering molar flow rate (mol/s) from FA0 to the exit molar flow rate of FA.
Alternative Derivation
Chapter 1

## Slide 29: Packed Bed Reactor - Mole Balances
Steady State
PBR
Chapter 1

## Slide 30: Packed Bed Reactor - Mole Balances
Rearrange:
PBR catalyst weight necessary to reduce the entering molar flow rate FA0 to molar flow rate FA.
The integral form to find the catalyst weight is:
Chapter 1

## Slide 31: Reactor Mole Balances Summary
Reactor | Differential | Algebraic | Integral
The GMBE applied to the four major reactor types
(and the general reaction AB)
CSTR
Batch
NA
t
PFR
FA
V
PBR
FA
W
Chapter 1

## Slide 32: Reactors with Heat Effects
Propylene glycol is produced by the hydrolysis of propylene oxide:
EXAMPLE: Production of Propylene Glycol in an Adiabatic CSTR
Chapter 11
Fast Forward to the 10th Week of the Course

## Slide 33
What are the exit conversion X and exit temperature T?
Solution
Let the reaction be represented by
A+BC
v0
Propylene Glycol
Chapter 11
Fast Forward to the 10th Week of the Course

## Slide 34
Chapter 11

## Slide 35
Chapter 11

## Slide 36
Chapter 11
Parameter Evaluation (CA0, i, ): The total liquid volumetric flow rate entering the reactor is

## Slide 37
Chapter 11
Evaluate mole balance terms: The conversion calculated from the mole balance, XMB, is found form Equation (E8-8.5).

## Slide 38
Chapter 11

## Slide 39
Evaluate energy balance terms
Chapter 11

## Slide 40
Chapter 11

## Slide 41
Chapter 11

## Slide 42: Analysis
We have applied our CRE algorithm to calculate the Conversion (X=0.84) and Temperature (T=614 °R) in a 300 gallon CSTR operated adiabatically.
X=0.84
T=614 °R
T=535 °R
A+BC
Chapter 11

## Slide 43: Keeping Up
Algorithm

## Slide 44: Separations
These topics do not build upon one another.
Filtration
Distillation
Adsorption
Algorithm

## Slide 45: Reaction Engineering
Mole Balance
Rate Laws
Stoichiometry
These topics build upon one another.
Algorithm

## Slide 46
Mole Balance
Rate Laws
Stoichiometry
Isothermal Design
Heat Effects
CRE Algorithm
Algorithm

## Slide 47
Mole Balance
Be careful not to cut corners on any of the
CRE building blocks while learning this material!
Rate Laws
Algorithm

## Slide 48
Mole Balance
Rate Laws
Stoichiometry
Isothermal Design
Heat Effects
Otherwise, your Algorithm becomes unstable.
Algorithm

## Slide 49: End of Lecture 1

## Slide 50: Supplemental Slides Additional Applications of CRE

## Slide 51: Supplemental Slides Additional Applications of CRE

## Slide 52: Supplemental Slides Additional Applications of CRE

## Slide 53: Supplemental Slides Additional Applications of CRE
Hippo Digestion (Ch. 2)

## Slide 54: Supplemental Slides Additional Applications of CRE

## Slide 55: Supplemental Slides Additional Applications of CRE

## Slide 56
Smog (Ch. 1)
Supplemental Slides Additional Applications of CRE

## Slide 57
Chemical Plant for Ethylene Glycol (Ch. 5)
Supplemental Slides Additional Applications of CRE

## Slide 58
Oil Recovery (Ch. 7)
Wetlands (Ch. 7 DVD-ROM)
Supplemental Slides Additional Applications of CRE

## Slide 59
Cobra Bites
(Ch. 8 DVD-ROM)
Supplemental Slides Additional Applications of CRE

## Slide 60
Lubricant Design (Ch. 9)
Supplemental Slides Additional Applications of CRE

## Slide 61
Plant Safety
(Ch. 11,12,13)
Supplemental Slides Additional Applications of CRE