## Slide 1: Review: Nonelementary Reaction Kinetics
Nonelementary reaction kinetics
  No direct correspondence between reaction order and stoichiometry
  Result of multiple elementary reaction steps and reactive intermediates (an intermediate so reactive it is consumed as fast as it is formed)
How do we determine the reaction mechanism?
Postulate a reaction mechanism that is a series of elementary reactions
Derive a rate equation for the postulated mechanism
Determine whether the rate eq for the postulated mechanism consistent with the experimental results. If it is, you’re done. If they are not consistent, go back to step 1.

## Slide 2: Review: Postulating a Reaction Mechanism Based on an Experimentally Observed Rate Law
If CB appears in the denominator of the experimentally observed rate law, then one elementary reaction step is probably:
where A* is a reactive intermediate
If the denominator contains a constant (by itself, not multiplied by a concentration), then one reaction step is probably:
If the numerator contains a species concentration, then one rxn step is probably:
Derive a rate equation for the postulated mechanism and check if it describes the experimentally observed rate equation
This will definitely be on quiz 3!

## Slide 3: Review: Deriving a Rate Equation for a Postulated Mechanism
Write rate equation for postulated mechanism
2) For concentrations of reactive intermediates CI* that appear in the rate equation –rA
a) Write out the rate equation for reactive intermediates rI*
b) Apply Pseudo-Steady State Hypothesis, which states that the net formation of reactive intermediates is zero (rI*=0)
c) Solve for CI* in terms of measurable species
d) Substitute the new expression for CI* in terms of measurable species back into -rA
3) Rearrange –rA to check if it matches the experimentally observed rate equation

## Slide 4: Review: Free Radical Polymerizations
M
M
M
M
M
M
M-M-M
n
monomer
polymer
1. Initiation:
2. Propagation:
3. Chain transfer:
4a. Termination by addition:
Initiator (I) decomposes to 2 free radicals
Radical (1)
Chain elongation, new monomers add to chain
“Live” polymer chain transfers radical to monomer. Polymer chain is no longer reactive (dead). Can also transfer to solvent or other species
4b. Termination by disproportionation:

## Slide 5: Review: PSSH Applied to Thermal Cracking of Ethane
The thermal decomposition of ethane to ethylene, methane, butane and
hydrogen is believed to proceed in the following sequence:
Initiation:
Propagation:
Termination:
(a) Use the PSSH to derive a rate law for the rate of formation of ethylene
(b) Compare the PSSH solution in Part (a) to that obtained by solving the complete set
of ODE mole balance

## Slide 6: L10b: Bioreactors
Enzymes: Protein catalyst that execute complex biochemical reactions- all synthetic and degradative reactions in living organisms!
Increases the rate of reaction without undergoing permanent chemical change – not used up (consumed) by the reaction
  Substrate: the reactant that the enzyme acts on
Today’s goals:
  Predict rates of enzyme-catalyzed reactions
  Determine effect of chemical inhibitors on rxn rate
  Develop mathematical expression based on fundamental steps of rxn
  Apply model to cell growth

## Slide 7: Enzymes Increase Reaction Rate
Transition state, G‡
Activation energy for catalyzed rxn
Activation energy for uncatalyzed reaction
Enzymes do NOT change DG
Effects the reaction rate (kinetics), NOT equilibrium (thermo)
Lower activation energy ΔG‡ increases reaction rate, reach equilibrium faster
ΔG is unchanged, so ratio of products to reactants at equilibrium is the same
k1,cat>k1,uncat
DG‡ determines rxn rate
DG‡ = -RT ln(k)
Enzymes change DG‡
Thermodynamic:
DG determines equilibrium
DG = -RT ln(K)
Enzymes do NOT change DG

## Slide 8: Michaelis-Menten (M-M) Equation
[rP]
Vmax: maximum reaction rate, further increases in substrate, S, no longer increase the reaction velocity, v
Empirically found the Michaelis-Menten equation:
Where Vmax depends on the amount of enzyme
Km = substrate concentration where reaction velocity v = Vmax/2
[S] = substrate concentration [P]: product concentration
v = reaction velocity = rP = -rS

## Slide 9: Rate Equation for Enzymatic Reaction
Goal: derive this experimentally determined reaction rate
We cannot measure CES, so we need to get CES in terms of species we can measure. Start by writing the rate equation for CES :
The free enzyme concentration CE is also difficult to measure. Use the mass balance to get CE in terms of CES and CE0.
E: enzyme S: substrate
ES: enzyme-substrate complex
Substitute into rate eq for CE:
Notes: Participation question: connect inability to measure CES with reactive intermediate from the last lecture.

## Slide 10: CES in Measurable Quantities
Pseudo-steady state assumption: ES is a reactive intermediate, so
Now solve for CES
Multiply out and rearrange
Bring CES to left side of equation
Factor out CES
Divide by quantity in bracket
Divide top & bottom by k1
Plug this expression for CES into dCP/dt

## Slide 11: Derivation of the M-M Equation
E: enzyme S: substrate
ES: enzyme-substrate complex
Plug this expression for CES into dCP/dt
Compare to experimentally observed rate eq:
Vmax occurs when enzyme is fully saturated with S (in ES form)
When CS>>Km, then:
When CS<<Km, then:

## Slide 12: Complications with Measuring Rates with the M-M Equation
In practice, Vmax can be difficult to estimate using the MM equation. Everyone reported different values of Vmax.
Since a solution with infinite concentration of substrate is impossible to make, a different equation was needed.

## Slide 13: Lineweaver-Burk Equation
Lineweaver & Burk inverted the MM equation
By plotting 1/ v vs 1/CS,
a linear plot is obtained:
Slope = Km/Vmax
y-intercept = 1/Vmax
x-intercept= -1/Km

## Slide 14: Types of Reversible Inhibition
Binds to active site & blocks substrate binding
Reduces the CEnzyme available for binding
Competitive
inhibitor
Substrate
1. Competitive:
Inhibitor binds to some other site
Does not affect substrate binding
K’m
K’m
KI
KI
Substrate
2. Noncompetitive
I is the inhibitor

## Slide 15: 1. Competitive Inhibition
Chart: CS (mM)
| 0 | 0.25 | 0.5 | 1 | 2 | 3 | 5 | 10 | 15 | 20 | 30 | 100
v | 0 | 1.7 | 3 | 5 | 7.3 | 8.6 | 10.1 | 11.6 | 12.4 | 12.6 | 13 | 13.5
inhibited | 0 | 0.13911 | 0.27543 | 0.54001 | 1.0391 | 1.5016 | 2.3323 | 3.986 | 5.2197 | 6.1753 | 7.5593 | 11.0155
Uninhibited reaction
Chart: 1/CS (mmol)-1
| -0.65400000000000125 | 4 | 2 | 1 | 0.5 | 0.33333333333333331 | 0.2 | 0.1 | 6.666666666666668E-2 | 0.05 | 3.333333333333334E-2 | 1.0000000000000005E-2
v | 0 | 0.58824 | 0.33333 | 0.2 | 0.13699 | 0.11628 | 0.09901 | 0.086207 | 0.080645 | 0.079365 | 0.076923 | 0.074074
inhibited reaction | 0 | 7.1883 | 3.6307 | 1.8518 | 0.96241 | 0.66594 | 0.42876 | 0.25088 | 0.19158 | 0.16193 | 0.13229 | 0.090781
Slope = Km/Vmax y-int = 1/Vmax x-int= -1/Km
Can be overcome by high substrate concentration
Substrate and inhibitor
compete for same site
Km, app >Km
Vmax, app =Vmax
Competitive inhibition
No inhibition
Km observed w/ competitive inhibitor
Will reach Vmax of uninhibited rxn at high CS

## Slide 16: 2. Noncompetitive Inhibition
substrate and inhibitor bind different sites
Vmax, app < Vmax
Km, app = Km
higher CI
No I
CI
Vmax
Vmax,app
Vmax,app
CS
Km
rP
Increasing
CI
Competitive inhibition
No inhibition
Vmax observed w/ noncompetitive inhibitor

## Slide 17
E
S
substrate & inhibitor bind different sites but I only binds after S is bound
I
1/CS
1/rp
3. Uncompetitive Inhibition
Vmax, app < Vmax
Km, app <Km
Notes: For Lineweaver-Burk Plot, Both Km, apparent and Vm, apparent are smaller than Vmax and Km without inhibitor. Therefore both the y-intercept and x-intercept values change. However, the factor from the inhibitor cancels out, so the slope is Km/Vm.
E-H: the slope, Km, app, is decreasing as inhibitor increases and the y-intercept, Vmax, app, also decreases as the inhibitor increases.

## Slide 18: Batch Bioreactor or Fermentor
S
S
S
S
C
C
C
C
S
Batch Reactor
In a reactor with substrate at concentration CS0 and CC =0 add cells at concentration CC0 at t = 0 add no more S or cells after t = 0 monitor CS and CC with time
well stirred
reaction limited
C
S
C represents
cell mass
(biomass)
S
time
S0
t=0 s

## Slide 19: Kinetics of Microbial Growth (Batch or Semi-Batch)
Region 1: Lag phase
  microbes are adjusting to the new substrate
Region 2: Exponential growth phase
  microbes have acclimated to the conditions
Region 3: Stationary phase
  limiting substrate or oxygen limits the growth rate
Region 4: Death phase
  substrate supply is exhausted
CC,max
Log CC
CC0

## Slide 20: Quantifying Growth Kinetics
Relationship of the specific growth rate to substrate concentration exhibits the form of saturation kinetics
Assume a single chemical species, S, is growth-rate limiting
Apply Michaelis-Menten kinetics to cellular system→ called the Monod equation
mmax is the maximum specific growth rate when S>>Ks
CS is the substrate concentration
CC is the cell concentration
Ks is the saturation constant or half-velocity constant. Equals the rate-limiting substrate concentration, S, when the specific growth rate is ½ the maximum
Semi-empirical, experimental data fits to equation, assumes that a single enzymatic reaction, and therefore substrate conversion by that enzyme, limits the growth-rate

## Slide 21: Monod Model (1942) – Nobel Prize
Chart: CS
| 0 | 0.5 | 1 | 2 | 3 | 4 | 5 | 10 | 20 | 30 | 40 | 50 | 75 | 100
 | 0 | 1.1111 | 2 | 3.3333 | 4.2857 | 5 | 5.5556 | 7.1429 | 8.3333 | 9 | 9.45 | 9.7 | 9.9 | 10
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
 | 5 | 5 | 5 | 5 | 5
 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
First-order kinetics:
Zero-order kinetics:

## Slide 22: Mass Balance on Cell Growth with Products
Overall balance for cells growing on carbohydrate with products:
CHmOn + a O2 + b NH3 → c CHaObNd + d CHxOyNz + e H2O + f CO2
Carbohydrate
(can be any organic material)
Nitrogen source
Cell material
(biomass)
Individual elemental balances:
Carbon: 1 = c + d + f
Hydrogen: m + 3b = ca + dx + 2e
Oxygen: n + 2a = cb + dy + e + 2f
Nitrogen: b = cd + dz
Product

## Slide 23: Yield Coefficients
cell mass formed
substrate consumed
Cell yield for substrate:
Cell yield for O2:
Product yield for substrate:
cell mass formed
oxygen consumed
substrate consumed
product mass formed