## Slide 1: Review: Rate Equation for Enzymatic Reaction
experimentally determined reaction rate
E: enzyme S: substrate
ES: enzyme-substrate complex
Where:

## Slide 2: Review: Lineweaver-Burk Equation
Lineweaver & Burk: inverted the MM equation
By plotting 1/ V vs 1/CS,
a linear plot is obtained:
Slope = Km/Vmax
y-intercept = 1/Vmax
x-intercept= -1/Km

## Slide 3: Review: Competitive Inhibition
Chart: 1/CS (mmol)-1
| -0.65400000000000225 | 4 | 2 | 1 | 0.5 | 0.33333333333333331 | 0.2 | 0.1 | 6.6666666666666693E-2 | 5.0000000000000024E-2 | 3.3333333333333354E-2 | 1.0000000000000007E-2
v | 0 | 0.58824 | 0.33333 | 0.2 | 0.13699 | 0.11628 | 0.09901 | 0.086207 | 0.080645 | 0.079365 | 0.076923 | 0.074074
inhibited reaction | 0 | 7.1883 | 3.6307 | 1.8518 | 0.96241 | 0.66594 | 0.42876 | 0.25088 | 0.19158 | 0.16193 | 0.13229 | 0.090781
Slope = Km/Vmax y-int = 1/Vmax
x-int= -1/Km
Can be overcome by high substrate concentration
Substrate and inhibitor
compete for same site
Km, app >Km
Vmax, app =Vmax

## Slide 4: Review: Noncompetitive Inhibition
Vmax, app < Vmax
Km, app = Km
substrate and inhibitor bind different sites
higher CI
No I
CI
Vmax
Vmax,app
Vmax,app
CS
Km
rP
Increasing
CI

## Slide 5: Review: Uncompetitive Inhibition
substrate & inhibitor bind different sites but I only binds after S is bound
1/CS
1/v
Vmax, app < Vmax
Km, app <Km
No rxn
Notes: For Lineweaver-Burk Plot, Both Km, apparent and Vm, apparent are smaller than Vmax and Km without inhibitor. Therefore both the y-intercept and x-intercept values change. However, the factor from the inhibitor cancels out, so the slope is Km/Vm.
E-H: the slope, Km, app, is decreasing as inhibitor increases and the y-intercept, Vmax, app, also decreases as the inhibitor increases.

## Slide 6: Review: Kinetics of Microbial Growth (Batch or Semi-Batch)
Region 1: Lag phase
  microbes are adjusting to the new substrate
Region 2: Exponential growth phase
  microbes have acclimated to the conditions
Region 3: Stationary phase
  limiting substrate or oxygen limits the growth rate
Region 4: Death phase
  substrate supply is exhausted
CC,max
Log CC
CC0

## Slide 7: Review: Quantifying Growth Kinetics
Relationship of the specific growth rate to substrate concentration exhibits the form of saturation kinetics
Assume a single chemical species, S, is growth-rate limiting
Apply Michaelis-Menten kinetics to cells→ called the Monod equation:
mmax is the maximum specific growth rate when S>>Ks
CS is the substrate concentration
CC is the cell concentration
Ks is the saturation constant or half-velocity constant. Equals the rate-limiting substrate concentration, S, when the specific growth rate is ½ the maximum
Semi-empirical, experimental data fits to equation
Assumes that a single enzymatic reaction, and therefore substrate conversion by that enzyme, limits the growth-rate

## Slide 8: Review: Monod Model
Chart: S
| 0 | 0.5 | 1 | 2 | 3 | 4 | 5 | 10 | 20 | 30 | 40 | 50 | 75 | 100
 | 0 | 1.1111 | 2 | 3.3333 | 4.2857 | 5 | 5.5556 | 7.1429 | 8.3333 | 9 | 9.45 | 9.7 | 9.9 | 10
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
 | 5 | 5 | 5 | 5 | 5
 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
First-order kinetics:
Zero-order kinetics:

## Slide 9: L11: Thermochemistry for Nonisothermal Reactor Design
The major difference between the design of isothermal and non-isothermal reactors is the evaluation of the design equation
  What do we do when the temperature varies along the length of a PFR or when heat is removed from a CSTR?
  Today we will start nonisothermal reactor design by reviewing energy balances
  Monday we will use the energy balance to design nonisothermal steady-state reactors
Nonisothermal
Energy balance

## Slide 10: Why do we need to balance energy?
FA
XA = 0.7
Mole balance:
Rate law:
Stoichiometry:
Arrhenius Equation
Need relationships:
X T V
Consider an exothermic, liquid-phase reaction operated adiabatically in a PFR (adiabatic operation- temperature increases down length of PFR):
FA0
We can get them from the energy balance

## Slide 11: Clicker Question
    The concentration of a reactant in the feed stream (inlet) will be greatly influenced by temperature when the reactant is
      a gas
      a liquid
      a solid
      either a gas or a liquid
      extremely viscous
Gas phase:
Liquid& solid phase:
Hints:

## Slide 12: Thermodynamics in a Closed System
First law of Thermodynamics
  Closed system: no mass crosses the system’s boundaries
dÊ: change in total energy of the system
dQ: heat flow to system
dW: work done by system on the surroundings
Q
W

## Slide 13: Thermodynamics in an Open System
Ẇ
Fin
Hin
Fout
Hout
Open system: continuous flow system, mass crosses the system’s boundaries
Mass flow can add or remove energy
Energy balance on system:
Rate of accum of energy in system
work done by system
energy added to sys. by mass flow in
energy leaving sys. by mass flow out
Heat in
=
-
+
-
Let’s look at these terms individually

## Slide 14: The Work Term, Ẇ
Work term is separated into “flow work” and “other work”.
  Flow work: work required to get the mass into and out of system
  Other work includes shaft work (e.g., stirrer or turbine)
other work (shaft work)
P : pressure
Ẇ: Rate of work done by the system on the surroundings
Flow work
Plug in:
Accum of energy in system
Other work
Energy & work added by flow in
Energy & work removed by flow out
Heat in
=
-
+
-

## Slide 15: The Energy Term, Ei
Accum of energy in system
Other work
Energy & work added by flow in
Energy & work removed by flow out
Heat in
=
-
+
-
Internal energy
Kinetic energy
Potential energy
Electric, magnetic, light, etc.
Usually:
Plug in Ui for Ei:
Internal energy is major contributor to energy term

## Slide 16: Total Energy Balance
Recall eq for enthalpy, a function of T
unit : (cal / mole)
Steady state:
Accumulation = 0 = in - out + flow in – flow out

## Slide 17: In Terms of Conversion:
If XA0=0, then:
Steady state:
Total energy balance (TEB)
Relates temperature to XA
Multiply out:
Must use this equation if a phase change occurs

## Slide 18: What is (Hi0 – Hi)?
When NO phase change occurs & heat capacity is constant:
Enthalpy of formation of i at reference temp (TR) of 25 °C
What is the heat of reaction for species i (Hi)?
Change in enthalpy due to heating from TR to rxn temp T

## Slide 19: What is ΔHRX(T)?
How do we calculate ΔHRX(T), which is the heat of reaction at temperature T?
For the generic reaction:

## Slide 20: Example: Calculation of ΔHRX(T)
For the reaction N2 (g) + 3H2 (g) → 2NH3 (g), calculate the heat of reaction at 150 °C in kcal/mol of N2 reacted.
Extra info:

## Slide 21: Example: Calculation of ΔHRX(T)
For the reaction N2 (g) + 3H2 (g) → 2NH3 (g), calculate the heat of reaction at 150 °C in kcal/mol of N2 reacted.
Extra info:
Convert T and TR to Kelvins

## Slide 22: Example: Calculation of ΔHRX(T)
For the reaction N2 (g) + 3H2 (g) → 2NH3 (g), calculate the heat of reaction at 150 °C in kJ/mol of H2 reacted.
Extra info:
Convert kcal to kJ
Put in terms of moles H2 reacted

## Slide 23: Q and Hi in Terms of T
Ignore enthalpy of mixing (usually an acceptable assumption)
Look up enthalpy of formation, Hi◦(TR) in a thermo table, where the reference temperature TR is usually 25◦C
Compute Hi(T) using heat capacity and heats of vaporization/melting
Phase change at Tm (solid to liquid):
Solid at TR
For Tm < T < Tb
←boiling
If constant of average heat capacities are used, then:
For Tm < T < Tb
melting

## Slide 24: Insert ΔHRX(T) & (Hi0 – Hi) into EB
Example calculations of ∆H°RX(TR) & ΔCp are shown on the previous slides
If the feed does not contain the products C or D, then:
(Ti0 – T) = - (T – Ti0)

## Slide 25: Clicker Question
    If the reactor is at a steady state, which term in this equation would be zero?
      dEsys/dt
      Ẇ
      FA0
      ∆CP
Accum of energy in system
Other work
Energy & work added by flow in
Energy & work removed by flow out
Heat in
=
-
+
-
At the steady state:

## Slide 26: How do we Handle Q in a CSTR?
CSTR with a heat exchanger, perfectly mixed inside and outside of reactor
T, X
FA0
T, X
Ta
Ta
The heat flow to the reactor is in terms of:
Overall heat-transfer coefficient, U
Heat-exchange area, A
Difference between the ambient temperature in the heat jacket, Ta, and rxn temperature, T

## Slide 27: Tubular Reactors (PFR/PBR):
Integrate the heat flux equation along the length of the reactor to obtain the total heat added to the reactor :
Heat transfer to a perfectly mixed PFR in a jacket
a: heat-exchange area per unit volume of reactor
For a tubular reactor of diameter D, a = 4 / D
For a jacketed PBR (perfectly mixed in jacket):
Heat transfer to a PBR