## Slide 1: Review: Thermochemistry for Nonisothermal Reactor Design
FA
XA = 0.7
Mole balance:
Rate law:
Stoichiometry:
Arrhenius Equation
Need relationships:
X T V
Consider an exothermic, liquid-phase reaction operated adiabatically in a PFR (adiabatic operation- temperature increases down length of PFR):
FA0
The energy balance provides this relationship

## Slide 2: Review: Terms in Energy Balance
Rate of accum of energy in system
Rate of work done by syst
energy added to syst by mass flow in
energy leaving syst by mass flow out
Heat in
=
-
+
-
WS: shaft work
P : pressure
Flow work
Internal energy is major contributor to energy term
Steady state:
Accum of energy in system
shaft work
Energy & work added by flow in
Energy & work removed by flow out
Heat in
=0=
-
+
-

## Slide 3: Review: Relate T to Conversion
If XA0=0, then:
Steady state:
Total energy balance (TEB)
0 at steady state
Multiply out:
Accum of energy in system
shaft work
Energy & work added by flow in
Energy & work removed by flow out
Heat in
=
-
+
-

## Slide 4: Review: Q in a CSTR
CSTR with a heat exchanger, perfectly mixed inside and outside of reactor
T, X
FA0
T, X
Ta
Ta
The heat flow to the reactor is in terms of:
Overall heat-transfer coefficient, U
Heat-exchange area, A
Difference between the ambient temperature in the heat jacket, Ta, and rxn temperature, T

## Slide 5: Review: Tubular Reactors (PFR/PBR):
Integrate the heat flux equation along the length of the reactor to obtain the total heat added to the reactor :
Heat transfer to a perfectly mixed PFR in a jacket
a: heat-exchange area per unit volume of reactor
For a tubular reactor of diameter D, a = 4 / D
For a jacketed PBR (perfectly mixed in jacket):
Heat transfer to a PBR

## Slide 6: L12: Nonisothermal Reactor Design
Steady–state total energy balance (TEB):
At a particular temperature:
For a SS nonisotherm flow reactor:
Goal: Use TEB to design nonisothermal steady-state reactors
Needs to be “simplified” before we can apply it to reactor design
Constant (average) heat capacities :
Substitute
(Hi – Hi0) = - (Hi – Hi0)

## Slide 7: Relating DHRX(T) to DH◦RX(TR) and Overall Change in Heat Capacity
Only considering constant (average) heat capacities:
T = reaction temp Ti0 = initial (feed) temp TR= reference temp

## Slide 8: Solving TEB for Conversion
Rearrange to isolate terms with XA on one side of eq:
Solve for XA:
Plug in Q for the specific type of reactor, and solve this eq simultaneously with design equation
Always start with this TEB:

## Slide 9: Solving TEB for XA for an Adiabatic Rxn
Rearrange:
    Which term in this equation is zero because we’re solving for an adiabatic reaction?
      dEsys/dt
      Ẇ
      FA0
      None of the above
When the reaction is adiabatic (Q=0):

## Slide 10: Solving TEB for XA for an Adiabatic Rxn
When shaft work can be neglected (Ẇ=0) and the reaction is adiabatic (Q=0):
Rearrange:
Solve for XA:
T = reaction temp Ti0 = initial (feed) temperature TR= reference temp
Solve this eq simultaneously with design equation
Design eqs do not change, except k will be a function of T

## Slide 11: Nonisothermal Adiabatic Operation
Constant or mean heat capacities
For a system with no shaft work ( ) & adiabatic operation ( ):
Usually,
Xenergy balance
Temperature
CSTR, PFR, PBR, Batch
Adiabatic exothermic reactions

## Slide 12: Nonisothermal CSTR
Design equation (From mass balance) :
Energy balance:
Coupled
With the exception of processes involving highly viscous materials,
the work done by the stirrer can be neglected (i.e. )
With heat exchanger:

## Slide 13: Application to CSTR
Solve TEB for T at the exit (Texit = Tinside reactor)
Calculate k = Ae-E/RT where T was calculated in step a
Plug the k calculated in step b into the design equation to calculate VCSTR
Case 1: Given FA0, CA0, A, E, Cpi, H°I, and XA, calculate T & V
Solve TEB for T as a function of XA
Solve CSTR design equation for XA as a function of T (plug in k = Ae-E/RT )
Plot XA,EB vs T & XA,MB vs T on the same graph. The intersection of these 2 lines is the conditions (T and XA) that satisfies the energy & mass balance
Case 2: Given FA0, CA0, A, E, Cpi, H°I, and V, calculate T & XA
XA,EB = conversion determined from the TEB equation
XA,MB = conversion determined using the design equation
XA
T
XA,EB
XA,MB
XA,exit
Texit
Intersection is T and XA that satisfies both equations

## Slide 14: Application to a Steady-State PFR
PFR
FA0
FA
distance
T
XA
Negligible shaft work (ẆS=0) and adiabatic (Q=0)
Use TEB to construct a table of T as a function of XA
Use k = Ae-E/RT to obtain k as a function of XA
Use stoichiometry to obtain –rA as a function of XA
Calculate:

## Slide 15
A first order reaction A(l) → B(l) is to be carried out adiabatically in a CSTR. Given A, E, T0, u0, CA0, and FA0, find the reactor volume that produces a conversion XA. The heat capacities of A & B are approximately equal, & ẆS=0.
a) Solve TEB for T:
Multiply out
Factor out T
Plug in values (∆Cp, ∆H°RX(TR), Cp,i) given in problem statement (look them up if necessary) & solve
Temp when specified XA is reached
0
0
Isolate T

## Slide 16
A first order reaction A(l) → B(l) is to be carried out adiabatically in a CSTR. Given A, E, T0, u0, CA0, and FA0, find the reactor volume that produces a conversion XA. The heat capacities of A & B are approximately equal, & ẆS=0.
a) Solve TEB for T of reaction when the specified XA is reached:
Calculate k = Ae-E/RT where T was calculated in step (a)
Look up E in a thermo book
Plug the k calculated for the reaction’s temperature when the specified XA is reached (in step b) into the design equation to calculate VCSTR

## Slide 17
Now, the first order reaction A(l) → B(l) is carried out adiabatically with and inlet temp of 300 K, CPA = 50 cal/mol∙K, and the heat of reaction = -20,000 cal/mol. Assume ẆS=0. The energy balance is:
From thermodynamics
XEB
T
From energy balance
0
0

## Slide 18
The irreversible, elementary liquid-phase reaction 2A → B is carried out adiabatically in a flow reactor with ẆS=0 and without a pressure drop. The feed contains equal molar amounts of A and an inert liquid (I). The feed enters the reactor at 294 K with u0 = 5 dm3/s and CA0= 1 mol/dm3. What would be the temperature inside of a steady-state CSTR that achieved XA= 0.8? Extra info:
E = 10,000 cal/mol CpA= 15 cal/mol•K CpB= 30 cal/mol•K CpI = 15 cal/mol•K ∆HA°(TR) = -20 kcal/mol ∆ HB°(TR) = -50 kcal/mol ∆HI°(TR) = -15 kcal/mol
k = 0.02 dm3/mol•s at 350 K
Start with SS EB & solve for T:
Multiply out brackets & bring terms containing T to 1 side

## Slide 19
The irreversible, elementary liquid-phase reaction 2A → B is carried out adiabatically in a flow reactor with ẆS=0 and without a pressure drop. The feed contains equal molar amounts of A and an inert liquid (I). The feed enters the reactor at 294 K with u0 = 5 dm3/s and CA0= 1 mol/dm3. What would be the temperature inside of a steady-state CSTR that achieved XA= 0.8? Extra info:
E = 10,000 cal/mol CpA= 15 cal/mol•K CpB= 30 cal/mol•K CpI = 15 cal/mol•K ∆HA°(TR) = -20 kcal/mol ∆ HB°(TR) = -50 kcal/mol ∆HI°(TR) = -15 kcal/mol
k = 0.02 dm3/mol•s at 350 K
Start with SS EB & solve for T:

## Slide 20
The irreversible, elementary liquid-phase reaction 2A → B is carried out adiabatically in a flow reactor with ẆS=0 and without a pressure drop. The feed contains equal molar amounts of A and an inert liquid (I). The feed enters the reactor at 294 K with u0 = 5 dm3/s and CA0= 1 mol/dm3. What would be the temperature inside of a steady-state CSTR that achieved XA= 0.8? Extra info:
E = 10,000 cal/mol CpA= 15 cal/mol•K CpB= 30 cal/mol•K CpI = 15 cal/mol•K ∆HA°(TR) = -20 kcal/mol ∆ HB°(TR) = -50 kcal/mol ∆HI°(TR) = -15 kcal/mol
k = 0.02 dm3/mol•s at 350 K
Start with SS EB & solve for T:

## Slide 21
The irreversible, elementary liquid-phase reaction 2A → B is carried out adiabatically in a flow reactor with ẆS=0 and without a pressure drop. The feed contains equal molar amounts of A and an inert liquid (I). The feed enters the reactor at 294 K with u0 = 5 dm3/s and CA0= 1 mol/dm3. What would be volume of the steady-state CSTR that achieves XA= 0.8? Extra info:
E = 10,000 cal/mol CpA= 15 cal/mol•K CpB= 30 cal/mol•K CpI = 15 cal/mol•K ∆HA°(TR) = -20 kcal/mol ∆ HB°(TR) = -50 kcal/mol ∆HI°(TR) = -15 kcal/mol
k = 0.02 dm3/mol•s at 350 K
Solve the CSTR design eq for V at XA = 0.8 & T = 427.3K:

## Slide 22
The irreversible, elementary liquid-phase reaction 2A → B is carried out adiabatically in a flow reactor with ẆS=0 and without a pressure drop. The feed contains equal molar amounts of A and an inert liquid (I). The feed enters the reactor at 294 K with u0 = 5 dm3/s and CA0= 1 mol/dm3. Use the 2-point rule to numerically calculate the PFR volume required to achieve XA=0.8? Extra info:
E = 10,000 cal/mol CpA= 15 cal/mol•K CpB= 30 cal/mol•K CpI = 15 cal/mol•K ∆HA°(TR) = -20 kcal/mol ∆ HB°(TR) = -50 kcal/mol ∆HI°(TR) = -15 kcal/mol
k = 0.02 dm3/mol•s at 350 K
Use the energy balance to construct table of T as a function of XA
For each XA , calculate k, -rA and FA0/-rA
Use numeric evaluation to calculate VPFR
XA | T(K) | k(dm3/mol•s) | -rA(mol/dm3•s) | FA0/-rA(dm3)
0 | 294* |  |  | 
0.8 | 427.3* | 0.2696* |  | 
*Calculated in CSTR portion of this problem
0.00129
0.00129
0.010784

## Slide 23
The irreversible, elementary liquid-phase reaction 2A → B is carried out adiabatically in a flow reactor with ẆS=0 and without a pressure drop. The feed contains equal molar amounts of A and an inert liquid (I). The feed enters the reactor at 294 K with u0 = 5 dm3/s and CA0= 1 mol/dm3. Use the 2-point rule to numerically calculate the PFR volume required to achieve XA=0.8? Extra info:
E = 10,000 cal/mol CpA= 15 cal/mol•K CpB= 30 cal/mol•K CpI = 15 cal/mol•K ∆HA°(TR) = -20 kcal/mol ∆ HB°(TR) = -50 kcal/mol ∆HI°(TR) = -15 kcal/mol
k = 0.02 dm3/mol•s at 350 K
Use the energy balance to construct table of T as a function of XA
For each XA , calculate k, -rA and FA0/-rA
Use numeric evaluation to calculate VPFR
XA | T(K) | k(dm3/mol•s) | -rA(mol/dm3•s) | FA0/-rA(dm3)
0 | 294 | 0.00129 | 0.00129 | 
0.8 | 427.3 | 0.2696 | 0.010784 | 
3876
463.6

## Slide 24
The irreversible, elementary liquid-phase reaction 2A → B is carried out adiabatically in a flow reactor with ẆS=0 and without a pressure drop. The feed contains equal molar amounts of A and an inert liquid (I). The feed enters the reactor at 294 K with u0 = 5 dm3/s and CA0= 1 mol/dm3. Use the 2-point rule to numerically calculate the PFR volume required to achieve XA=0.8? Extra info:
E = 10,000 cal/mol CpA= 15 cal/mol•K CpB= 30 cal/mol•K CpI = 15 cal/mol•K ∆HA°(TR) = -20 kcal/mol ∆ HB°(TR) = -50 kcal/mol ∆HI°(TR) = -15 kcal/mol
k = 0.02 dm3/mol•s at 350 K
Use the energy balance to construct table of T as a function of XA
For each XA , calculate k, -rA and FA0/-rA
Use numeric evaluation to calculate VPFR
XA | T(K) | k(dm3/mol•s) | -rA(mol/dm3•s) | FA0/-rA(dm3)
0 | 294 | 0.00129 | 0.00129 | 3876
0.8 | 427.3 | 0.2696 | 0.010784 | 463.6