## Slide 1: Review: Nonideal Flow & Reactor Design
Real CSTRs
  Relatively high reactant conc at entrance
  Relatively low conc in stagnant regions, called dead zones (corners & behind baffles)
Dead Zone
Dead Zone
Short Circuiting
Real PBRs
fluid velocity profiles, turbulent mixing, & molecular diffusion cause molecules to move at varying speeds & directions
channeling
Dead zones
Goal: mathematically describe non-ideal flow and solve design problems for reactors with nonideal flow

## Slide 2: Residence Time Distribution (RTD)
RTD is experimentally determined by injecting an inert “tracer” at t=0 and measuring the tracer concentration C(t) at exit as a function of time
RTD ≡ E(t) ≡ “residence time distribution” function
RTD describes the amount of time molecules have spent in the reactor
Measurement of RTD
↑
Pulse injection
↓
Detection
Reactor
X
C(t)
The C curve
t
Fraction of material leaving reactor that has been inside reactor for a time between t1 & t2
E(t)=0 for t<0 since no fluid can exit before it enters
E(t)≥0 for t>0 since mass fractions are always positive

## Slide 3
t
E(t)

t
E(t)
t
E(t)

Nearly ideal PFR
Nearly ideal CSTR
PBR with dead zones
t
E(t)
CSTR with dead zones
The fraction of the exit stream that has resided in the reactor for a period of time shorter than a given value t:
F(t) is a cumulative distribution function
40
0.8
80% of the molecules spend 40 min or less in the reactor
Nice multiple choice question

## Slide 4: Review: Mean Residence Time, tm
For an ideal reactor, the space time  is defined as V/u0
The mean residence time tm is equal to  in either ideal or nonideal reactors
By calculating tm, the reactor V can be determined from a tracer experiment
The spread of the distribution (variance):
Space time t and mean residence time tm would be equal if the following two conditions are satisfied:
  No density change
  No backmixing
In practical reactors the above two may not be valid, hence there will be a difference between them

## Slide 5: Review: Complete Segregation Model
  Flow is visualized in the form of globules
  Each globule consists of molecules of the same residence time
  Different globules have different residence times
  No interaction/mixing between different globules
Mixing of different ‘age groups’ at the last possible moment
The mean conversion is the average conversion of the various globules in the exit stream:
Conversion achieved after spending time tj in the reactor
Fraction of globules that spend between tj and tj + Dt in the reactor
XA(t) is from the batch reactor design equation

## Slide 6: Review: Maximum Mixedness Model
In a PFR: as soon as the fluid enters the reactor, it is completely mixed radially with the other fluid already in the reactor. Like a PFR with side entrances, where each entrance port creates a new residence time:
 +Dl
  0
V = 0
V = V0
: time it takes for fluid to move from a particular point to end of the reactor
u0
u0E(l)Dl: Volumetric flow rate of fluid fed into side ports of reactor in interval between  +  & 
Volumetric flow rate of fluid fed to reactor at :
Volume of fluid with life expectancy between  +  & :
u(l): volumetric flow rate at l, = flow that entered at l+Dl plus what entered through the sides
fraction of effluent that in reactor for less than time t
 ∞


## Slide 7
t min | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 12 | 14
C g/m3 | 0 | 1 | 5 | 8 | 10 | 8 | 6 | 4 | 3 | 2.2 | 1.5 | 0.6 | 0
E(t) | 0 | 0.02 | 0.1 | 0.16 | 0.2 | 0.16 | 0.12 | 0.08 | 0.06 | 0.044 | 0.03 | 0.012 | 0
For a pulse tracer expt, the effluent concentration C(t) & RTD function E(t) are given
in the table below. The irreversible, liquid-phase, nonelementary rxn A+B→C+D, -rA=kCACB2 will be carried out isothermally at 320K in this reactor. Calculate the conversion for (1) an ideal PFR and (2) for the complete segregation model.
CA0=CB0=0.0313 mol/L & k=176 L2/mol2·min at 320K

## Slide 8
t min | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 12 | 14
C g/m3 | 0 | 1 | 5 | 8 | 10 | 8 | 6 | 4 | 3 | 2.2 | 1.5 | 0.6 | 0
E(t) | 0 | 0.02 | 0.1 | 0.16 | 0.2 | 0.16 | 0.12 | 0.08 | 0.06 | 0.044 | 0.03 | 0.012 | 0
Start with PFR design eq & see how far can we get:
For a pulse tracer expt, the effluent concentration C(t) & RTD function E(t) are given
in the table below. The irreversible, liquid-phase, nonelementary rxn A+B→C+D, -rA=kCACB2 will be carried out isothermally at 320K in this reactor. Calculate the conversion for (1) an ideal PFR and (2) for the complete segregation model.
CA0=CB0=0.0313 mol/L & k=176 L2/mol2·min at 320K
Get like terms together & integrate

## Slide 9
t min | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 12 | 14
C g/m3 | 0 | 1 | 5 | 8 | 10 | 8 | 6 | 4 | 3 | 2.2 | 1.5 | 0.6 | 0
E(t) | 0 | 0.02 | 0.1 | 0.16 | 0.2 | 0.16 | 0.12 | 0.08 | 0.06 | 0.044 | 0.03 | 0.012 | 0
For a pulse tracer expt, the effluent concentration C(t) & RTD function E(t) are given
in the table below. The irreversible, liquid-phase, nonelementary rxn A+B→C+D, -rA=kCACB2 will be carried out isothermally at 320K in this reactor. Calculate the conversion for (1) an ideal PFR and (2) for the complete segregation model.
CA0=CB0=0.0313 mol/L & k=176 L2/mol2·min at 320K
How do we determine t?
For an ideal reactor, t = tm
Use numerical method to determine tm:
t min | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 12 | 14
C g/m3 | 0 | 1 | 5 | 8 | 10 | 8 | 6 | 4 | 3 | 2.2 | 1.5 | 0.6 | 0
E(t) | 0 | 0.02 | 0.1 | 0.16 | 0.2 | 0.16 | 0.12 | 0.08 | 0.06 | 0.044 | 0.03 | 0.012 | 0
t*E(t) | 0 | 0.02 | 0.2 | 0.48 | 0.8 | 0.8 | 0.72 | 0.56 | 0.48 | 0.396 | 0.3 | 0.144 | 0

## Slide 10
t min | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 12 | 14
C g/m3 | 0 | 1 | 5 | 8 | 10 | 8 | 6 | 4 | 3 | 2.2 | 1.5 | 0.6 | 0
E(t) | 0 | 0.02 | 0.1 | 0.16 | 0.2 | 0.16 | 0.12 | 0.08 | 0.06 | 0.044 | 0.03 | 0.012 | 0
For a pulse tracer expt, the effluent concentration C(t) & RTD function E(t) are given
in the table below. The irreversible, liquid-phase, nonelementary rxn A+B→C+D, -rA=kCACB2 will be carried out isothermally at 320K in this reactor. Calculate the conversion for (1) an ideal PFR and (2) for the complete segregation model.
CA0=CB0=0.0313 mol/L & k=176 L2/mol2·min at 320K
t min | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 12 | 14
C g/m3 | 0 | 1 | 5 | 8 | 10 | 8 | 6 | 4 | 3 | 2.2 | 1.5 | 0.6 | 0
E(t) | 0 | 0.02 | 0.1 | 0.16 | 0.2 | 0.16 | 0.12 | 0.08 | 0.06 | 0.044 | 0.03 | 0.012 | 0
t*E(t) | 0 | 0.02 | 0.2 | 0.48 | 0.8 | 0.8 | 0.72 | 0.56 | 0.48 | 0.396 | 0.3 | 0.144 | 0
For an ideal PFR reactor, t = tm

## Slide 11
t min | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 12 | 14
C g/m3 | 0 | 1 | 5 | 8 | 10 | 8 | 6 | 4 | 3 | 2.2 | 1.5 | 0.6 | 0
E(t) | 0 | 0.02 | 0.1 | 0.16 | 0.2 | 0.16 | 0.12 | 0.08 | 0.06 | 0.044 | 0.03 | 0.012 | 0
Segregation model:
XA(t) is from batch reactor design eq
For a pulse tracer expt, the effluent concentration C(t) & RTD function E(t) are given
in the table below. The irreversible, liquid-phase, nonelementary rxn A+B→C+D, -rA=kCACB2 will be carried out isothermally at 320K in this reactor. Calculate the conversion for an ideal PFR, the complete segregation model and maximum mixedness model. CA0=CB0=0.0313 mol/L & k=176 L2/mol2·min at 320K
Numerical method
Solve batch reactor design equation to determine eq for XA
Determine XA for each time
Use numerical methods to determine ¯X A
Polymath Method
Use batch reactor design equation to find eq for XA
Use Polymath polynomial curve fitting to find equation for E(t)
Use Polymath to determine ¯X A

## Slide 12
t min | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 12 | 14
C g/m3 | 0 | 1 | 5 | 8 | 10 | 8 | 6 | 4 | 3 | 2.2 | 1.5 | 0.6 | 0
E(t) | 0 | 0.02 | 0.1 | 0.16 | 0.2 | 0.16 | 0.12 | 0.08 | 0.06 | 0.044 | 0.03 | 0.012 | 0
Segregation model:
XA(t) is from batch reactor design eq
Batch design eq:
Stoichiometry:
For a pulse tracer expt, the effluent concentration C(t) & RTD function E(t) are given
in the table below. The irreversible, liquid-phase, nonelementary rxn A+B→C+D, -rA=kCACB2 will be carried out isothermally at 320K in this reactor. Calculate the conversion for an ideal PFR, the complete segregation model and maximum mixedness model. CA0=CB0=0.0313 mol/L & k=176 L2/mol2·min at 320K

## Slide 13
Segregation model:
Numerical method
t min | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 12 | 14
C g/m3 | 0 | 1 | 5 | 8 | 10 | 8 | 6 | 4 | 3 | 2.2 | 1.5 | 0.6 | 0
E(t) | 0 | 0.02 | 0.1 | 0.16 | 0.2 | 0.16 | 0.12 | 0.08 | 0.06 | 0.044 | 0.03 | 0.012 | 0
XA |  |  |  |  |  |  |  |  |  |  |  |  | 
Plug in each t & solve
For a pulse tracer expt, the effluent concentration C(t) & RTD function E(t) are given
in the table below. The irreversible, liquid-phase, nonelementary rxn A+B→C+D, -rA=kCACB2 will be carried out isothermally at 320K in this reactor. Calculate the conversion for an ideal PFR, the complete segregation model and maximum mixedness model. CA0=CB0=0.0313 mol/L & k=176 L2/mol2·min at 320K

## Slide 14
t min | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 12 | 14
C g/m3 | 0 | 1 | 5 | 8 | 10 | 8 | 6 | 4 | 3 | 2.2 | 1.5 | 0.6 | 0
E(t) | 0 | 0.02 | 0.1 | 0.16 | 0.2 | 0.16 | 0.12 | 0.08 | 0.06 | 0.044 | 0.03 | 0.012 | 0
XA | 0 | 0.137 | 0.23 | 0.298 | 0.35 | 0.39 | 0.428 | 0.458 | 0.483 | 0.505 | 0.525 | 0.558 | 0.585
Segregation model:
Numerical method
For a pulse tracer expt, the effluent concentration C(t) & RTD function E(t) are given
in the table below. The irreversible, liquid-phase, nonelementary rxn A+B→C+D, -rA=kCACB2 will be carried out isothermally at 320K in this reactor. Calculate the conversion for an ideal PFR, the complete segregation model and maximum mixedness model. CA0=CB0=0.0313 mol/L & k=176 L2/mol2·min at 320K

## Slide 15
t min | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 12 | 14
C g/m3 | 0 | 1 | 5 | 8 | 10 | 8 | 6 | 4 | 3 | 2.2 | 1.5 | 0.6 | 0
E(t) | 0 | 0.02 | 0.1 | 0.16 | 0.2 | 0.16 | 0.12 | 0.08 | 0.06 | 0.044 | 0.03 | 0.012 | 0
XA | 0 | 0.137 | 0.23 | 0.298 | 0.35 | 0.39 | 0.428 | 0.458 | 0.483 | 0.505 | 0.525 | 0.558 | 0.585
Segregation model:
Numerical method
For a pulse tracer expt, the effluent concentration C(t) & RTD function E(t) are given
in the table below. The irreversible, liquid-phase, nonelementary rxn A+B→C+D, -rA=kCACB2 will be carried out isothermally at 320K in this reactor. Calculate the conversion for an ideal PFR, the complete segregation model and maximum mixedness model. CA0=CB0=0.0313 mol/L & k=176 L2/mol2·min at 320K

## Slide 16
t min | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 12 | 14
C g/m3 | 0 | 1 | 5 | 8 | 10 | 8 | 6 | 4 | 3 | 2.2 | 1.5 | 0.6 | 0
E(t) | 0 | 0.02 | 0.1 | 0.16 | 0.2 | 0.16 | 0.12 | 0.08 | 0.06 | 0.044 | 0.03 | 0.012 | 0
XA | 0 | 0.137 | 0.23 | 0.298 | 0.35 | 0.39 | 0.428 | 0.458 | 0.483 | 0.505 | 0.525 | 0.558 | 0.585
Alternative approach: segregation model by Polymath:
CB0=0.0313
k=176
Need an equation for E(t)
Use Polymath to fit the E(t) vs t data in the table to a polynomial
For a pulse tracer expt, the effluent concentration C(t) & RTD function E(t) are given
in the table below. The irreversible, liquid-phase, nonelementary rxn A+B→C+D, -rA=kCACB2 will be carried out isothermally at 320K in this reactor. Calculate the conversion for an ideal PFR, the complete segregation model and maximum mixedness model. CA0=CB0=0.0313 mol/L & k=176 L2/mol2·min at 320K

## Slide 17
time
E(t)
E(t) = 0 at t=0
Gave best fit
Model: C02= a1*C01 + a2*C01^2 + a3*C01^3 + a4*C01^4
Final Equation: E= 0.0889237*t -0.0157181*t2 + 0.0007926*t3 – 8.63E-6*t4
a1=0.0889237
a2= -0.0157181
a3= 0.0007926
a4= -8.63E-06
For the irreversible, liquid-phase, nonelementary rxn A+B→C+D, -rA=kCACB2
Calculate the XA using the complete segregation model using Polymath

## Slide 18
A+B→C+D
-rA=kCACB2
Complete segregation model by Polymath
Segregation model by Polymath:

## Slide 19
t min | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 12 | 14
C g/m3 | 0 | 1 | 5 | 8 | 10 | 8 | 6 | 4 | 3 | 2.2 | 1.5 | 0.6 | 0
E(t) | 0 | 0.02 | 0.1 | 0.16 | 0.2 | 0.16 | 0.12 | 0.08 | 0.06 | 0.044 | 0.03 | 0.012 | 0
Maximum mixedness model:
l=time
Polymath cannot solve because l→0 (needs to increase)
Substitute l for z, where z=T̅-l where T̅=longest time interval (14 min)
E must be in terms of T̅-z. Since T̅-z=l & l=t, simply substitute l for t
E(l)= 0.0889237*l-0.0157181*l2 + 0.0007926*l3 – 8.63E-6*l4
F(l) is a cumulative distribution function
For a pulse tracer expt, the effluent concentration C(t) & RTD function E(t) are given
in the table below. The irreversible, liquid-phase, nonelementary rxn A+B→C+D, -rA=kCACB2 will be carried out isothermally at 320K in this reactor. Calculate the conversion for an ideal PFR, the complete segregation model and maximum mixedness model. CA0=CB0=0.0313 mol/L & k=176 L2/mol2·min at 320K

## Slide 20
Maximum Mixedness Model, nonelementary reaction A+B→C+D
-rA=kCACB2
Eq for E describes RTD function only on interval t= 0 to 14 minutes, otherwise E=0
Denominator cannot = 0
XA, maximum mixedness = 0.347

## Slide 21
t min | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 12 | 14
C g/m3 | 0 | 1 | 5 | 8 | 10 | 8 | 6 | 4 | 3 | 2.2 | 1.5 | 0.6 | 0
E(t) | 0 | 0.02 | 0.1 | 0.16 | 0.2 | 0.16 | 0.12 | 0.08 | 0.06 | 0.044 | 0.03 | 0.012 | 0
For a pulse tracer expt, C(t) & E(t) are given in the table below. The irreversible, liquid-phase, nonelementary rxn A+B→C+D, -rA=kCACB2 will be carried out in this reactor. Calculate the conversion for the complete segregation model under adiabatic conditions with T0= 288K, CA0=CB0=0.0313 mol/L, k=176 L2/mol2·min at 320K, DH°RX=-40000 cal/mol, E/R =3600K, CPA=CPB=20cal/mol·K & CPC=CPD=30 cal/mol·K
Polymath eqs for segregation model:
E(t)= 0.0889237*t -0.0157181*t2 + 0.0007926*t3 – 8.63E-6*t4
Express k as function of T:
Need equations from energy balance. For adiabatic operation:

## Slide 22
t min | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 12 | 14
C g/m3 | 0 | 1 | 5 | 8 | 10 | 8 | 6 | 4 | 3 | 2.2 | 1.5 | 0.6 | 0
E(t) | 0 | 0.02 | 0.1 | 0.16 | 0.2 | 0.16 | 0.12 | 0.08 | 0.06 | 0.044 | 0.03 | 0.012 | 0
For a pulse tracer expt, C(t) & E(t) are given in the table below. The irreversible, liquid-phase, nonelementary rxn A+B→C+D, -rA=kCACB2 will be carried out in this reactor. Calculate the conversion for the complete segregation model under adiabatic conditions with T0= 288K, CA0=CB0=0.0313 mol/L, k=176 L2/mol2·min at 320K, DH°RX=-40000 cal/mol, E/R =3600K, CPA=CPB=20cal/mol·K & CPC=CPD=30 cal/mol·K
Energy balance for adiabatic operation:
E(t)= 0.0889237*t -0.0157181*t2 + 0.0007926*t3 – 8.63E-6*t4
Not zero!

## Slide 23
Segregation model, adiabatic operation, nonelementary reaction kinetics
A+B→C+D
-rA=kCACB2

## Slide 24
The following slides show how the same problem would be solved and the solutions would differ if the reaction rate was still -rA=kCACB2 but the reaction was instead elementary: A+2B→C+D
These slides may be provided as an extra example problem that the students may study on there own if time does not permit doing it in class.

## Slide 25
t min | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 12 | 14
C g/m3 | 0 | 1 | 5 | 8 | 10 | 8 | 6 | 4 | 3 | 2.2 | 1.5 | 0.6 | 0
E(t) | 0 | 0.02 | 0.1 | 0.16 | 0.2 | 0.16 | 0.12 | 0.08 | 0.06 | 0.044 | 0.03 | 0.012 | 0
Start with PFR design eq & see how far can we get:
For a pulse tracer expt, the effluent concentration C(t) & RTD function E(t) are given
in the table below. The irreversible, liquid-phase, elementary rxn A+2B→C+D, -rA=kCACB2 will be carried out isothermally at 320K in this reactor. Calculate the conversion for an ideal PFR, the complete segregation model and maximum mixedness model. CA0=CB0=0.0313 mol/L & k=176 L2/mol2·min at 320K
Could solve with Polymath if we knew the value of t
CB0 = 0.0313
k = 0.0313

## Slide 26
t min | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 12 | 14
C g/m3 | 0 | 1 | 5 | 8 | 10 | 8 | 6 | 4 | 3 | 2.2 | 1.5 | 0.6 | 0
E(t) | 0 | 0.02 | 0.1 | 0.16 | 0.2 | 0.16 | 0.12 | 0.08 | 0.06 | 0.044 | 0.03 | 0.012 | 0
For a pulse tracer expt, the effluent concentration C(t) & RTD function E(t) are given
in the table below. The irreversible, liquid-phase, elementary rxn A+2B→C+D, -rA=kCACB2 will be carried out isothermally at 320K in this reactor. Calculate the conversion for an ideal PFR, the complete segregation model and maximum mixedness model. CA0=CB0=0.0313 mol/L & k=176 L2/mol2·min at 320K
How do we determine t?
For an ideal reactor, t = tm
Use numerical method to determine tm:
t min | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 12 | 14
C g/m3 | 0 | 1 | 5 | 8 | 10 | 8 | 6 | 4 | 3 | 2.2 | 1.5 | 0.6 | 0
E(t) | 0 | 0.02 | 0.1 | 0.16 | 0.2 | 0.16 | 0.12 | 0.08 | 0.06 | 0.044 | 0.03 | 0.012 | 0
t*E(t) | 0 | 0.02 | 0.2 | 0.48 | 0.8 | 0.8 | 0.72 | 0.56 | 0.48 | 0.396 | 0.3 | 0.144 | 0

## Slide 27
t min | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 12 | 14
C g/m3 | 0 | 1 | 5 | 8 | 10 | 8 | 6 | 4 | 3 | 2.2 | 1.5 | 0.6 | 0
E(t) | 0 | 0.02 | 0.1 | 0.16 | 0.2 | 0.16 | 0.12 | 0.08 | 0.06 | 0.044 | 0.03 | 0.012 | 0
For a pulse tracer expt, the effluent concentration C(t) & RTD function E(t) are given
in the table below. The irreversible, liquid-phase, elementary rxn A+2B→C+D, -rA=kCACB2 will be carried out isothermally at 320K in this reactor. Calculate the conversion for an ideal PFR, the complete segregation model and maximum mixedness model. CA0=CB0=0.0313 mol/L & k=176 L2/mol2·min at 320K
t min | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 12 | 14
C g/m3 | 0 | 1 | 5 | 8 | 10 | 8 | 6 | 4 | 3 | 2.2 | 1.5 | 0.6 | 0
E(t) | 0 | 0.02 | 0.1 | 0.16 | 0.2 | 0.16 | 0.12 | 0.08 | 0.06 | 0.044 | 0.03 | 0.012 | 0
t*E(t) | 0 | 0.02 | 0.2 | 0.48 | 0.8 | 0.8 | 0.72 | 0.56 | 0.48 | 0.396 | 0.3 | 0.144 | 0
For an ideal reactor, t = tm
Final XA corresponds to t=5.15 min

## Slide 28
t min | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 12 | 14
C g/m3 | 0 | 1 | 5 | 8 | 10 | 8 | 6 | 4 | 3 | 2.2 | 1.5 | 0.6 | 0
E(t) | 0 | 0.02 | 0.1 | 0.16 | 0.2 | 0.16 | 0.12 | 0.08 | 0.06 | 0.044 | 0.03 | 0.012 | 0
XA(t) is from batch reactor design eq
Batch reactor design eq:
Stoichiometry:
For a pulse tracer expt, the effluent concentration C(t) & RTD function E(t) are given
in the table below. The irreversible, liquid-phase, elementary rxn A+2B→C+D, -rA=kCACB2 will be carried out isothermally at 320K in this reactor. Calculate the conversion for an ideal PFR, the complete segregation model and maximum mixedness model. CA0=CB0=0.0313 mol/L & k=176 L2/mol2·min at 320K
CB0=0.0313
k=176
Best-fit polynomial line for E(t) vs t calculated by Polymath (slide 19)
Segregation model with Polymath:
E(t)= 0.0889237*t -0.0157181*t2 + 0.0007926*t3 – 8.63E-6*t4

## Slide 29
Segregation model, isothermal operation, elementary rxn: A+2B→C+D

## Slide 30
t min | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 12 | 14
C g/m3 | 0 | 1 | 5 | 8 | 10 | 8 | 6 | 4 | 3 | 2.2 | 1.5 | 0.6 | 0
E(t) | 0 | 0.02 | 0.1 | 0.16 | 0.2 | 0.16 | 0.12 | 0.08 | 0.06 | 0.044 | 0.03 | 0.012 | 0
Maximum mixedness model:
For a pulse tracer expt, the effluent concentration C(t) & RTD function E(t) are given
in the table below. The irreversible, liquid-phase, elementary rxn A+2B→C+D, -rA=kCACB2 will be carried out isothermally at 320K in this reactor. Calculate the conversion for an ideal PFR, the complete segregation model and maximum mixedness model. CA0=CB0=0.0313 mol/L & k=176 L2/mol2·min at 320K
l=time
Polymath cannot solve because l→0 (must increase)
Substitute l for z, where z=T̅-l where T̅=longest time interval (14 min)
E must be in terms of T̅-z. Since T̅-z=l & l=t, simply substitute l for t
E(l)= 0.0889237*l-0.0157181*l2 + 0.0007926*l3 – 8.63E-6*l4

## Slide 31
Maximum Mixedness Model, elementary reaction A+2B→C+D, -rA=kCACB2
Eq for E describes RTD function only on interval t= 0 to 14 minutes, otherwise E=0
Denominator cannot = 0
XA, maximum mixedness = 0.25

## Slide 32
t min | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 12 | 14
C g/m3 | 0 | 1 | 5 | 8 | 10 | 8 | 6 | 4 | 3 | 2.2 | 1.5 | 0.6 | 0
E(t) | 0 | 0.02 | 0.1 | 0.16 | 0.2 | 0.16 | 0.12 | 0.08 | 0.06 | 0.044 | 0.03 | 0.012 | 0
For a pulse tracer expt, C(t) & E(t) are given in the table below. The irreversible, liquid-phase, elementary rxn A+2B→C+D, -rA=kCACB2 will be carried out in this reactor. Calculate the conversion for the complete segregation model under adiabatic conditions with T0= 288K, CA0=CB0=0.0313 mol/L, k=176 L2/mol2·min at 320K, DH°RX=-40000 cal/mol, E/R =3600K, CPA=CPB=20cal/mol·K & CPC=CPD=30 cal/mol·K
Polymath eqs for segregation model:
E(t)= 0.0889237*t -0.0157181*t2 + 0.0007926*t3 – 8.63E-6*t4
Express k as function of T:
Need equations from energy balance. For adiabatic operation:

## Slide 33
t min | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 12 | 14
C g/m3 | 0 | 1 | 5 | 8 | 10 | 8 | 6 | 4 | 3 | 2.2 | 1.5 | 0.6 | 0
E(t) | 0 | 0.02 | 0.1 | 0.16 | 0.2 | 0.16 | 0.12 | 0.08 | 0.06 | 0.044 | 0.03 | 0.012 | 0
For a pulse tracer expt, C(t) & E(t) are given in the table below. The irreversible, liquid-phase, elementary rxn A+2B→C+D, -rA=kCACB2 will be carried out in this reactor. Calculate the conversion for the complete segregation model under adiabatic conditions with T0= 288K, CA0=CB0=0.0313 mol/L, k=176 L2/mol2·min at 320K, DH°RX=-40000 cal/mol, E/R =3600K, CPA=CPB=20cal/mol·K & CPC=CPD=30 cal/mol·K
Adiabatic EB:
E(t)= 0.0889237*t -0.0157181*t2 + 0.0007926*t3 – 8.63E-6*t4

## Slide 34
Segregation model, adiabatic operation, elementary reaction kinetics
A+2B→C+D
-rA=kCACB2
X̅A = 0.50
Why so much lower than before?
Because B is completely consumed by XA=0.5