## Slide 1: Review: Batch Reactor Basic Molar Balance
Rate of generation of reactant A in reactor due to rxn
Rate of accumulation of
reactant A in reactor
=
No material enters or leaves the reactor
In ideal reactor, composition and temperature are spatially uniform (i.e. perfect mixing)
No flow in or out of reactor. Fj0 and Fj = 0.
Batch Reactor Design Equation
Ideal Batch Reactor Design Equation
Ideal (perfectly mixed) reactor: spatially uniform temp, conc, & reaction rate

## Slide 2: Review: CSTR Basic Molar Balance
Accumulation = In - Out + Generation
by rxn
0 = Fj0 - Fj +
No spatial variation:
Continuously add reactants and remove products
In an ideal reactor, composition and temperature are spatially uniform (i.e. perfect mixing)
At steady state- no accumulation
Fj0
Fj
Ideal Steady State CSTR Design Equation:
in terms of concentration
in terms of flow
 (upsilon)

## Slide 3: Review: Molar Balance – PFR
ΔV
FA0
FA
Fj0
Fj
+
-
=
Ideal SS PFR Design Eq.
Flow reactor operated at steady state (no accumulation per Δ)
Composition of fluid varies down length of reactor (material balance for differential element of volume DV

## Slide 4: Review: Molar Balance- Packed Bed Reactor (PBR)
Heterogeneous rxn: reaction occurs at catalyst particle surface
Concentration gradient of reactant and product change down length of the reactor
Rxn rate based on the mass of catalyst W, not reactor volume V
Similar to PFR, but expressed in terms of catalyst weight instead of reactor volume
Units for the rate of a homogeneous rxn (rj) :
Units for the rate of a catalytic rxn (rj’) :
So in terms of catalyst weight instead of reactor volume:

## Slide 5: L3: Conversion and Reactors in Series
FA0 X0
FA1, X1
V1
V2
FA2
X2
FA0 X0
FA1, X1
V1
V2
FA2, X2
VCSTR1
VPFR2
Chart: XA
| 0 | 0.1 | 0.2 | 0.4 | 0.60000000000000064 | 0.70000000000000062 | 0.8
 | 0.89 | 1.08 | 1.33 | 2.05 | 3.56 | 5.06 | 8

## Slide 6: Conversion, XA
Conversion is convenient for relating: rj, V, υ, Nj, Fj, and Cj
Choose limiting reactant A as basis of calculation and normalize:
BATCH
SYSTEM:
“Moles A fed” is the amount of A at the start of the reactor (t=0)
FLOW
SYSTEM:
“Moles A fed” is the amount of A entering the reactor
Usually pick the basis to be the limiting reagent

## Slide 7: Conversion Example
A + 2B → 2C
Start with 1 mole of A & 1 mole of B
If A is the basis and at the end we have:
1 mole A, 1 mole B ↔ XA = 0/1 = 0 (no reaction)
½ mole A, 0 mole B ↔ XA = 0.5/1 = 1/2
0 mole A, -1 mole B ↔ XA = 1/1 = 1 (complete reaction)
Not possible!
The correct approach is to take B as the basis because B is the limiting reagent
At the end we have:
1 mole A, 1 mole B ↔ XB = 0/1 = 0 (no reaction)
½ mole A, 0 mole B ↔ XB = 1/1 = 1 (complete reaction)

## Slide 8: Expressing other Components in Terms of Conversion of A (XA)
BATCH
SYSTEM:
Longer reactant is in reactor, more reactant is converted to product (until reactant is consumed or the reaction reaches equilibrium)
∴ Conversion (Xj) is a function of time (t) in the batch reactor
Moles A in reactor at time t
=
Moles A fed
-
Moles A consumed
reactant
product

## Slide 9: Expressing other Components in Terms of Conversion of A (XA)
nj≡ stoichiometric coefficient; positive for products, negative for reactants
Total moles in reactor at time t
=
Total moles fed
+
total moles products formed minus reactants consumed

## Slide 10: Batch Reactor Design Equation with Xj
In terms of A:
Ideal Batch Reactor Design Eq:
Want to determine how long to leave reactants in reactor to achieve a desired value for the conversion
←Substitute into batch reactor design eq
Ideal Batch Reactor Design Eq with Xj:
→ take derivative of “NA” equation w/ respect to time

## Slide 11: Flow and Conversion
Molar flow rate that A leaves the reactor
=
Molar flow rate A is fed to reactor
-
Molar rate A is consumed in reactor
FLOW
SYSTEM:
For a given flow rate, the larger the reactor, the more time it takes the reactant to pass through the reactor, the more time to react
∴ Conversion (Xj) is a function of reactor volume (V)

## Slide 12: CSTR Design Equation & Xj
Ideal SS CSTR:
Substitute for FA
Ideal CSTR design eq in terms of XA
V ≡ CSTR volume required to achieve a specified conversion
Note: XA and –rA are evaluated at the exit of the CSTR

## Slide 13: PFR Design Equation & Xj
Ideal SS PRF:
Want to determine the reactor volume required to achieve a desired amount of conversion
←Substitute into PFR design eq
Ideal SS PFR Design Eq with Xj:
Applies for no pressure drop down PFR!
→ take derivative of “FA“ expression with respect to volume

## Slide 14: PBR Design Equation & Xj
Ideal SS PBF:
Want to determine the weight of catalyst that is required to achieve a desired amount of conversion
←Substitute into PBR design eq
Ideal SS PBR Design Eq with Xj:
Applies for no pressure drop down PBR!
→ take derivative of FA expression with respect to W

## Slide 15: Sizing CSTRs
We can determine the volume of the CSTR required to achieve a specific conversion if we know how the reaction rate rj depends on the conversion Xj
Ideal SS CSTR design eq.
Volume is product of FA0/-rA and XA
Plot FA0/-rA vs XA (Levenspiel plot)
VCSTR is the rectangle with a base of XA,exit and a height of FA0/-rA

## Slide 16: Sizing a CSTR with a Levenspiel Plot
XA | 0 | 0.1 | 0.2 | 0.4 | 0.6 | 0.7 | 0.8
FA0/-rA | 0.89 | 1.08 | 1.33 | 2.05 | 3.56 | 5.06 | 8
Chart: XA
| 0 | 0.1 | 0.2 | 0.4 | 0.60000000000000053 | 0.70000000000000051 | 0.8
 | 0.89 | 1.08 | 1.33 | 2.05 | 3.56 | 5.06 | 8
VCSTR for XA = 0.4?
VCSTR for XA = 0.8?
Value of FA0/-rA for XA=0.4

## Slide 17: Sizing PFRs
We can determine the required volume of a PFR to achieve a specific conversion if we know how the reaction rate rj depends on the conversion Xj
Ideal PFR design eq.
Plot FA0/-rA vs XA (Experimentally determined numerical values)
VPFR is the area under the curve FA0/-rA vs XA,exit

## Slide 18: Sizing a PFR with a Levenspiel Plot
XA | 0 | 0.1 | 0.2 | 0.4 | 0.6 | 0.7 | 0.8
FA0/-rA | 0.89 | 1.08 | 1.33 | 2.05 | 3.56 | 5.06 | 8
VPFR for XA = 0.4?
We do not have an expression for –rA(XA)

## Slide 19: Sizing a PFR with a Levenspiel Plot
XA | 0 | 0.1 | 0.2 | 0.4 | 0.6 | 0.7 | 0.8
FA0/-rA | 0.89 | 1.08 | 1.33 | 2.05 | 3.56 | 5.06 | 8
VPFR for XA = 0.4?
We do not have an expression for –rA(XA)
Numerically evaluate (Appendix A.4) to estimate the area under the curve
Volume of PFR

## Slide 20: Numerical Evaluation of Integrals (A.4)
Simpson’s one-third rule (3-point):
Trapezoidal rule (2-point):
Simpson’s three-eights rule (4-point):
Simpson’s five-point quadrature :

## Slide 21: Sizing a PFR with a Levenspiel Plot
XA | 0 | 0.1 | 0.2 | 0.4 | 0.6 | 0.7 | 0.8
FA0/-rA | 0.89 | 1.08 | 1.33 | 2.05 | 3.56 | 5.06 | 8
XA | 0 | 0.1 | 0.2 | 0.4 | 0.6 | 0.7 | 0.8
FA0/-rA | 0.89 | 1.08 | 1.33 | 2.05 | 3.56 | 5.06 | 8
VPFR for XA = 0.4?
Use Simpson’s one-third rule (3-point):
= area under the curve
XA increments must be equal
0.89
1.33
2.05

## Slide 22: Reactors in Series
In practice, reactors are usually connected so the exit stream of one reactor is the feed stream for the next reactor
Conversion up to point i (no side streams):
FA0
FA1
i=1
X1
V1
V3
FA3 i=3 X3
V2
FA2
i=2
X2

## Slide 23: 2 CSTRs in Series
FA0 X0
FA1, X1
V1
V2
FA2
X2
Materials balance reactor 1:
In
Out
-
+
Gen.
=
Accum.
Need to express FA1 in terms of X1

## Slide 24: 2 CSTRs in Series
FA0 X0
FA1, X1
V1
V2
FA2
X2
Materials balance reactor 2:
In
Out
-
+
Gen.
=
Accum.
Value of FA0/-rA at X2
Materials balance reactor 1:
Need to express FA2 in terms of X2

## Slide 25: 2 CSTRs in Series
Usually for the same overall conversion, VTOTAL, 2 CSTRs IN SERIES < VSINGLE CSTR
FA0 X0
FA1, X1=0.4
V1
V2
FA2 X2=0.8
XA | 0 | 0.4 | 0.8
FA0/-rA | 0.89 | 2.05 | 8
Chart: XA
| 0 | 0.1 | 0.2 | 0.4 | 0.60000000000000064 | 0.70000000000000062 | 0.8
 | 0.89 | 1.08 | 1.33 | 2.05 | 3.56 | 5.06 | 8
VCSTR1 for XA1 = 0.4?
VCSTR2 for XA2 = 0.4 to 0.8?
VCSTR of single CSTR with XA = 0.8?
<

## Slide 26: 2 PFRs in Series
FA0, X0
FA1 X1
FA2, X2
XA | 0 | 0.2 | 0.4 | 0.6 | 0.8
FA0/-rA | 0.89 | 1.33 | 2.05 | 3.56 | 8
VPFR2 for XA2 = 0.4 to 0.8?
Same volume as 1 PFR with XA=0.8
2 PFRs in series, X1=0.4 and X2=0.8
When XA1= 0.4, VPFR1 =0.55 m3 (slide L3-20)

## Slide 27: Combinations of CSTRs & PFRs in Series
FA0 X0
FA1, X1
V1
V2
FA2, X2
VCSTR1
VPFR2
VPFR1
VCSTR2
FA0, X0
FA1 X1
V1
V2
FA2, X2
( )
VCSTR1 + VPFR2 ≠ VPFR1 + CCSTR2

## Slide 28: Reactors in Series
for any combination of PFRs & CSTRs in series
In general, 1 PFR = any number of PFRs in series
1 PFR = ∞ number of CSTRs in series
Definitions:
Space time (t): time necessary to process one reactor volume, also called mean residence time or holding time
Space velocity (SV): inverse of space time, but vo may be measured under different conditions than the space time
Liquid-hourly space velocity
Gas-hourly space velocity
u0| is the volumetric flow rate measured at specified condition