## Slide 1: Review: Heterogeneous Catalyst
We have looked at cases where
  Adsorption, surface reaction, or desorption is rate limiting
  External diffusion is rate limiting
  Internal diffusion is rate limiting
Next goal: Derive an overall rate law for heterogeneous catalyst where the rate limiting step as any of the 7 reaction steps. This new overall reaction rate would be inserted into the design equation to get W, XA, CA, etc

## Slide 2: Review: Internal Diffusion Effects in Spherical Catalyst Particles
r
R
CAs
Internal diffusion: diffusion of reactants or products from particle surface (pore mouth) to pellet interior
Concentration at the pore mouth will be higher than that inside the pore
Internal diffusion
CAb
External diffusion
Step 1) Mole balance over the shell thickness r is:
IN - OUT + GEN = ACCUM
Volume of shell
r’A: rxn rate per mass of catalyst
c: catalyst density
rm: mean radius between r and r - r
Divide by -4p/Dr & take limit as Dr →0
Differential BMB in spherical catalyst particle

## Slide 3: Review: Diffusion & Rxn in Spherical Catalyst
r
R
CAs
r+Dr
System at steady state, so EMCD: WB = -WA (otherwise A or B would accumulate)
Rate law:
Insert diffusion eq & rate eq into BMB:
Solve for CA(r) & get WAr(r) from diffusion eq

## Slide 4: Review:Dimensionless Variables
Put into dimensionless form
Boundary Conditions:
Y =1 at l=1 Y =finite at l=0
Thiele modulus for rxn of nth order ≡ fn
Subscript n = reaction order
fn is small: surface reaction is rate limiting
fn is large: internal diffusion is rate limiting
The solution for a 1st order rxn:
R
r=0
small 1
medium 1
large 1
small 1: surface rxn control, significant amount of reactant diffuses into pellet interior w/out reacting
large 1: surface rxn is rapid, reactant is consumed very closed to the external surface of pellet (A waste of precious metal inside of pellet)

## Slide 5: Review: Internal Effectiveness Factor, h
eta
f1
h
1
0.2
2
10
4
6
8
1
0.8
0.6
0.4
0.1
0.2
Internal diffusion limited
Reaction limited
Effectiveness factor vs fn
As particle diameter ↓, fn ↓, h→1, rxn is surface rxn limited
As particle diameter ↑, fn ↑, h→0, rxn is diffusion limited

## Slide 6: Review: Effectiveness Factor & Rxn Rate
surface-reaction-limited
f1 is large, diffusion-limited reaction inside the pellet (external diffusion will have a negligible effect on the overall rxn rate because internal diffusion limits the rxn rate)
Overall rate for 1st-order rxn
When internal-diffusion-limited:
To increase the overall rate of a rxn limited by internal diffusion
(1) decrease the radius R (3) increase the concentration of A
(2) increase the temperature (4) increase the internal surface area

## Slide 7: L21: Simultaneous Internal Diffusion & External Diffusion
CAb
CAs
C(r)
At steady-state: transport of reactants from bulk fluid to external catalyst surface is equal to net rate of reactant consumption in/on the pellet
Molar rate of mass transfer from bulk fluid to external surface:
molar flux
external surface area per unit reactor volume
reactor volume
This molar rate of mass transfer to surface is equal to net rxn rate on & in pellet!
Goal: Derive a new rate eq that accounts for internal & external diffusion
-r’A is a function of reactant concentration
Reactant conc is affected by internal & external diffusion
Express reactant conc in terms of diffusion-related constants & variables
→Use mole balance

## Slide 8: Basic Molar Balance at Pellet Surface
=
Flux: bulk to external surface
Actual rxn rate per unit total S.A.
External S.A.
x
ac: external surface area per reactor volume (m2/m3)
DV: reactor volume (m3)
-r’’A: rate of reaction per unit surface area (mol/m2·s)
Sa: surface area of catalyst per unit mass of catalyst (m2/g cat)
rb: bulk density, catalyst mass/ reactor volume rb=rc(1-f)
f: porosity of bed (void fraction) c: catalyst density
x
external + internal S.A.
Typically external surface area <<< internal surface area

## Slide 9: Overall Molar Rate of Reaction
Overall rxn rate = flux to surface = rxn rate on & in pellet
For external mass transport:
Since internal diffusion resistance is also significant, the reactant conc at the internal surface is lower that the reactant conc at the external surface:
where the internal effectiveness factor:
For a 1st order rxn: -r’’A=-hk1CAs
Plug flux & 1st order rxn rate back into the mass balance:
Solve mass balance for CAs

## Slide 10: Overall Effectiveness Factors
Overall rxn rate with internal & external diffusion
Finally insert CAs into –r’’A
Is this the overall rxn rate that we ALWAYS use for a surface reaction that has internal & external?
Yes, we should always use this rate equation for a surface reaction
No, we should only use this rate eq for processes that use spherical catalyst pellets
No, we should only use this rate eq for processes that that involve catalyst particles that have a constant density & even catalyst loading on the surface
(d) No, we should only use this rate eq for 1st order irreversible reactions
(e) b, c, & d

## Slide 11: Overall Effectiveness Factors
Overall rxn rate with internal & external diffusion
Remember, the internal effectiveness factor (based on CAs) is:
The overall effectiveness factor (based on CAb) is defined as:
Finally insert CAs into –r’’A
Put into design eq to account for internal & external diffusion
Omega

## Slide 12: Rxn Rate Variation vs Reactor Conditions
Type of Limitation | Variation of Reaction Rate with: |  | 
 | Superficial velocity | Particle size | Temperature
External | U1/2 | dp-3/2 | Linear
Internal | Independent | dp-1 | Exponential
Surface reaction | Independent | Independent | Exponential
External diffusion
Surface reaction -r’A=kCA
Internal diffusion

## Slide 13
Consider an isothermal catalytic reaction in a PBR where there is no pressure drop and the catalyst pellets are uniformly packed & spherical. The kinetics are 1st order, and k, all physical parameters, and the inlet conditions (pure A in feed, A→ products) are given. Derive an equation for XA, taking into account the diffusion to and within each catalyst particle, but ignore diffusion down the length of the reactor.
PBR design eq:
Rate must account for diffusion & be in terms of catalyst surface area
1. Put rate in terms of the unit surface area:
2. Account for diffusion limitations in rate eq:
3. Rate is 1st order:
4. Put into design eq:
5. Put Cab in terms of XA:
6. Integrate:

## Slide 14
Consider an isothermal catalytic reaction in a PBR where there is no pressure drop and the catalyst pellets are uniformly packed & spherical. The kinetics are 1st order, and k, all physical parameters, and the inlet conditions (pure A in feed, A→ products) are given. Derive an equation for XA, taking into account the diffusion to and within each catalyst particle, but ignore diffusion down the length of the reactor.
6. Integrate:
7. Solve for XA:

## Slide 15
For same conditions, eq derived in Fogler (12-71) for XA at end of reactor of length L is:
XA for 1st order rxn executed in an isothermal PBR packed with spherical catalyst particles with internal & external diffusion limitations
Are these equations the same?
They differ in the exponent:

## Slide 16: Review: Simultaneous Internal Diffusion & External Diffusion
CAb
CAs
C(r)
At steady-state: transport of reactants from bulk fluid to external catalyst surface is equal to net rate of reactant consumption in/on the pellet
Molar rate of mass transfer from bulk fluid to external surface:
molar flux
external surface area per unit reactor volume
reactor volume
This molar rate of mass transfer to surface is equal to net rxn rate on & in pellet!
Goal: Derive a new rate eq that accounts for internal & external diffusion
-r’A is a function of reactant concentration
Reactant conc is affected by internal & external diffusion
Express reactant conc in terms of diffusion-related constants & variables
→Use mole balance

## Slide 17: Review: Basic Molar Balance at Spherical Pellet Surface
=
Flux: bulk to external surface
Actual rxn rate per unit total S.A.
External S.A.
x
ac: external surface area per reactor volume (m2/m3)
DV: reactor volume (m3) f: porosity of bed (void fraction)
-r’’A: rate of reaction per unit surface area (mol/m2·s)
-r’A: mol/g cat∙s -rA: mol/volume∙s
Sa: surface area of catalyst per unit mass of catalyst (m2/g cat)
rb: bulk density, catalyst mass/ reactor volume rb=rc(1-f)
x
external + internal S.A.
Cancel out DV & ac ≈0 since external surface area usually <<< internal surface area (surface area of internal pores)
per mass cat→
per surface area
per volume

## Slide 18: Review: Overall Molar Rate of Reaction
For external mass transport:
Internal diffusion resistance is significant, so the reactant conc at the internal surface is lower that the reactant conc at the external surface:
h: internal effectiveness factor
For a 1st order rxn: -r’’A=-hk1CAs
Plug flux & 1st order rxn rate back into the mass balance, solve for CAs:
Insert CAs into –r’’A=hk1CAs:
Overall 1st order rxn rate with internal & external diffusion

## Slide 19: Review: Overall Effectiveness Factors
Remember, the internal effectiveness factor is based on CAs
The overall effectiveness factor is based on CAb:
Put into design eq to account for internal & external diffusion
Omega

## Slide 20: Review: Observed Rxn Rate Variation vs FT0, dp & T
Type of Limitation | Variation of Reaction Rate with: |  | 
 | Superficial velocity | Particle size | Temperature
External | U1/2 | dp-3/2 | Linear
Internal | Independent | dp-1 | Exponential
Surface reaction | Independent | Independent | Exponential
Surface reaction -r’A=kCA
External diffusion limited:
Internal diffusion limited:
Whether the rate varies when FT0 or particle size changes indicates tells us whether external diffusion, internal diffusion, or the surface rxn is limiting (slowing down) the observed rate

## Slide 21: Review: Rxn Rate Variation vs Reactor Conditions
Rate for external diff limited rxn:
Rate for surface reaction limited rxn: -r’A = kCA
Rate for internal diff limited rxn:
When the observed rate of a reaction is limited by external diffusion, internal diffusion, or the surface rxn, the observed reaction kinetics are:
kc: mass transfer coefficient DAB: diffusivity (m2/s) dp: diameter
U: free-stream velocity (m/s),  to flow rate (FT, FT0) for constant CA0
n: kinematic viscosity (m2/s); n=m/r r: fluid density (kg/m3) m: viscosity
R: radius at
particle surface
De: effective diffusivity
Whether the rate varies when FT0 (at constant CT0) or particle size changes indicates tells us whether external diffusion, internal diffusion, or the surface rxn is limiting (slowing down) the observed rate

## Slide 22: Observed Rxn Rate vs FT0, dp & T
Rate for surface reaction limited rxn: -r’A= kCA
Rate for external diff limited rxn:
dp: diameter U: free-stream velocity (m/s),  to flow rate (FT, FT0) for constant CA0
Rate for internal diff limited rxn:
R: radius at particle surface
According to these equations, if we increase the flow rate (FT0) without increasing the concentration of reactants in the feed, the observed rxn rate will increase if the rxn is limited (slowed down) by:
External diffusion
Internal diffusion
The surface reaction
Either external & internal diffusion
Any of these (external diffusion, internal diffusion, or surface reaction)
Free-stream velocity (U), which is  to flow rate for constant CA0, is only in rate eq for a external diffusion limited reaction

## Slide 23
The graph below shows the reaction rates obtained when the irreversible, liquid-
phase, catalytic reaction A→B was carried out in a PBR using the indicated catalyst dp, T, and FT0. CA0 was the same in each trial.
Chart: dp (cm)
| 0.05 | 0.1 | 0.2 | 0.6 | 0.8
FT0=4000 mol/h, T=400K | 15 | 15 | 14 | 12 | 10
FT0=4000 mol/h, T=300K | 2 | 2 | 2
FT0=3500 mol/h, T=400K | 15 | 15 | 14 | 12 | 10
FT0=3500 mol/h, T=300K | 1.9 | 1.9 | 1.9 | 1.9
FT0=1000 mol/h, T=400K | 2.5
FT0=1500 mol/h, T=400K | 4
FT0=2000 mol/h, T=400K | 8
Which, if any, of the conditions shown (flow rates, T, and dp) is the reaction limited by external diffusion?
External diffusion limits the observed rate when increasing FT0 increases –r’A
Need to find the points that have the same T and dp. If the rate increases when Fto increases, the trial at the LOWER flow rate is limited by external diffusion
Trial with T = 400K, dp= 0.8 cm & FT0= 1000 mol/h has a lower rate than the trial with T = 400K, dp= 0.8 cm & FT0= 1500 mol/h
Thus, rate is limited by external diffusion when T = 400K, dp= 0.8 cm & FT0= 1000 mol/h

## Slide 24
The graph below shows the reaction rates obtained when the irreversible, liquid-
phase, catalytic reaction A→B was carried out in a PBR using the indicated catalyst dp, T, and FT0. CA0 was the same in each trial.
Chart: dp (cm)
| 0.05 | 0.1 | 0.2 | 0.6 | 0.8
FT0=4000 mol/h, T=400K | 15 | 15 | 14 | 12 | 10
FT0=4000 mol/h, T=300K | 2 | 2 | 2
FT0=3500 mol/h, T=400K | 15 | 15 | 14 | 12 | 10
FT0=3500 mol/h, T=300K | 1.9 | 1.9 | 1.9 | 1.9
FT0=1000 mol/h, T=400K | 2.5
FT0=1500 mol/h, T=400K | 4
FT0=2000 mol/h, T=400K | 8
Which, if any, of the conditions shown (flow rates, T, and dp) is the reaction limited by external diffusion?
External diffusion limits the observed rate when increasing FT0 increases –r’A
Need to find the points that have the same T and dp. If the rate increases when Fto increases, the trial at the LOWER flow rate is limited by external diffusion
Trial with T = 400K, dp= 0.8 cm & FT0= 1500 mol/h has a lower rate than the trial with T = 400K, dp= 0.8 cm & FT0= 2000 mol/h
ext diff lim
Thus, rate is limited by external diffusion when T = 400K, dp= 0.8 cm & FT0= 1500 mol/h

## Slide 25
The graph below shows the reaction rates obtained when the irreversible, liquid-
phase, catalytic reaction A→B was carried out in a PBR using the indicated catalyst dp, T, and FT0. CA0 was the same in each trial.
Chart: dp (cm)
| 0.05 | 0.1 | 0.2 | 0.6 | 0.8
FT0=4000 mol/h, T=400K | 15 | 15 | 14 | 12 | 10
FT0=4000 mol/h, T=300K | 2 | 2 | 2
FT0=3500 mol/h, T=400K | 15 | 15 | 14 | 12 | 10
FT0=3500 mol/h, T=300K | 1.9 | 1.9 | 1.9 | 1.9
FT0=1000 mol/h, T=400K | 2.5
FT0=1500 mol/h, T=400K | 4
FT0=2000 mol/h, T=400K | 8
Which, if any, of the conditions shown (flow rates, T, and dp) is the reaction limited by external diffusion?
External diffusion limits the observed rate when increasing FT0 increases –r’A
Need to find the points that have the same T and dp. If the rate increases when Fto increases, the trial at the LOWER flow rate is limited by external diffusion
Trial with T = 400K, dp= 0.8 cm & FT0= 2000 mol/h has a lower rate than the trial with T = 400K, dp= 0.8 cm & FT0= 3500 mol/h
ext diff lim
Thus, rate is limited by external diffusion when T = 400K, dp= 0.8 cm & FT0= 2000 mol/h

## Slide 26
The graph below shows the reaction rates obtained when the irreversible, liquid-
phase, catalytic reaction A→B was carried out in a PBR using the indicated catalyst dp, T, and FT0. CA0 was the same in each trial.
Which, if any, of the conditions shown (flow rates, T, and dp) is the reaction limited by external diffusion?
External diffusion limits the observed rate when increasing FT0 increases –r’A
Need to find the points that have the same T and dp. If the rate increases when Fto increases, the trial at the LOWER flow rate is limited by external diffusion
Trial with T = 400K, dp= 0.8 cm & FT0= 3500 mol/h has the same rate as the trial with T = 400K, dp= 0.8 cm & FT0= 4000 mol/h
ext diff lim
Rate is NOT limited by external diffusion when T = 400K, dp= 0.8 cm & FT0= 3500 mol/h or T = 400K, dp= 0.8 cm & FT0= 4000 mol/h
ext diff lim
Chart: dp (cm)
| 0.05 | 0.1 | 0.2 | 0.600000000000001 | 0.8
FT0=4000 mol/h, T=400K | 15 | 15 | 14 | 12 | 10
FT0=4000 mol/h, T=300K | 2 | 2 | 2
FT0=3500 mol/h, T=400K | 15 | 15 | 14 | 12 | 10
FT0=3500 mol/h, T=300K | 1.9 | 1.9 | 1.9 | 1.9
FT0=1000 mol/h, T=400K | 2.5
FT0=1500 mol/h, T=400K | 4
FT0=2000 mol/h, T=400K | 8

## Slide 27
The graph below shows the reaction rates obtained when the irreversible, liquid-
phase, catalytic reaction A→B was carried out in a PBR using the indicated catalyst dp, T, and FT0. CA0 was the same in each trial.
Chart: dp (cm)
| 0.05 | 0.1 | 0.2 | 0.6 | 0.8
FT0=4000 mol/h, T=400K | 15 | 15 | 14 | 12 | 10
FT0=4000 mol/h, T=300K | 2 | 2 | 2
FT0=3500 mol/h, T=400K | 15 | 15 | 14 | 12 | 10
FT0=3500 mol/h, T=300K | 1.9 | 1.9 | 1.9 | 1.9
FT0=1000 mol/h, T=400K | 2.5
FT0=1500 mol/h, T=400K | 4
FT0=2000 mol/h, T=400K | 8
Which, if any, of the conditions shown (flow rates, T, and dp) is the reaction limited by external diffusion?
External diffusion limits the observed rate when increasing FT0 increases –r’A
Need to find the points that have the same T and dp. If the rate increases when Fto increases, the trial at the LOWER flow rate is limited by external diffusion
For all remaining trials, increasing FT0 does not increase the reaction rate, so no other trial conditions are external diffusion limited.
ext diff lim
ext diff lim

## Slide 28
The graph below shows the reaction rates obtained when the irreversible, liquid-
phase, catalytic reaction A→B was carried out in a PBR using the indicated catalyst dp, T, and FT0. CA0 was the same in each trial.
Chart: dp (cm)
| 0.05 | 0.1 | 0.2 | 0.6 | 0.8
FT0=4000 mol/h, T=400K | 15 | 15 | 14 | 12 | 10
FT0=4000 mol/h, T=300K | 2 | 2 | 2
FT0=3500 mol/h, T=400K | 15 | 15 | 14 | 12 | 10
FT0=3500 mol/h, T=300K | 1.9 | 1.9 | 1.9 | 1.9
FT0=1000 mol/h, T=400K | 2.5
FT0=1500 mol/h, T=400K | 4
FT0=2000 mol/h, T=400K | 8
Which, if any, of the conditions shown (flow rates, T, and dp) is the reaction limited by internal diffusion?
Internal diffusion limits the observed rate when decreasing dp increases –r’A
Need to find the points that have the same T. If the rate increases when dp decreases but does not change with FT0, the trial at the larger dp is limited by internal diffusion
Trial with T = 400K, dp= 0.8 cm & FT0= 3500 mol/h has a lower rate than the trial with T = 400K, dp= 0.6 cm & FT0= 3500 mol/h
Thus, rate is limited by internal diffusion when T = 400K, dp= 0.8 cm & FT0= 3500 mol/h
ext diff lim
ext diff lim
ext diff lim

## Slide 29
The graph below shows the reaction rates obtained when the irreversible, liquid-
phase, catalytic reaction A→B was carried out in a PBR using the indicated catalyst dp, T, and FT0. CA0 was the same in each trial.
Chart: dp (cm)
| 0.05 | 0.1 | 0.2 | 0.6 | 0.8
FT0=4000 mol/h, T=400K | 15 | 15 | 14 | 12 | 10
FT0=4000 mol/h, T=300K | 2 | 2 | 2
FT0=3500 mol/h, T=400K | 15 | 15 | 14 | 12 | 10
FT0=3500 mol/h, T=300K | 1.9 | 1.9 | 1.9 | 1.9
FT0=1000 mol/h, T=400K | 2.5
FT0=1500 mol/h, T=400K | 4
FT0=2000 mol/h, T=400K | 8
Which, if any, of the conditions shown (flow rates, T, and dp) is the reaction limited by internal diffusion?
Trial with T = 400K, dp= 0.8 cm & FT0= 4000 mol/h has a lower rate than the trial with T = 400K, dp= 0.6 cm & FT0= 4000 mol/h
Thus, rate is limited by internal diffusion when T = 400K, dp= 0.8 cm & FT0= 4000 mol/h
ext diff lim
ext diff lim
ext diff lim
int diff lim
Internal diffusion limits the observed rate when decreasing dp increases –r’A
Need to find the points that have the same T. If the rate increases when dp decreases but does not change with FT0, the trial at the larger dp is limited by internal diffusion

## Slide 30
The graph below shows the reaction rates obtained when the irreversible, liquid-
phase, catalytic reaction A→B was carried out in a PBR using the indicated catalyst dp, T, and FT0. CA0 was the same in each trial.
Chart: dp (cm)
| 0.05 | 0.1 | 0.2 | 0.6 | 0.8
FT0=4000 mol/h, T=400K | 15 | 15 | 14 | 12 | 10
FT0=4000 mol/h, T=300K | 2 | 2 | 2
FT0=3500 mol/h, T=400K | 15 | 15 | 14 | 12 | 10
FT0=3500 mol/h, T=300K | 1.9 | 1.9 | 1.9 | 1.9
FT0=1000 mol/h, T=400K | 2.5
FT0=1500 mol/h, T=400K | 4
FT0=2000 mol/h, T=400K | 8
Which, if any, of the conditions shown (flow rates, T, and dp) is the reaction limited by internal diffusion?
Trial with T = 400K, dp= 0.6 cm & FT0= 3500 mol/h has a lower rate than the trial with T = 400K, dp= 0.2 cm & FT0= 3500 mol/h
Thus, rate is limited by internal diffusion when T = 400K, dp= 0.6 cm & FT0= 3500 mol/h
ext diff lim
ext diff lim
ext diff lim
int diff lim
int diff lim
Internal diffusion limits the observed rate when decreasing dp increases –r’A
Need to find the points that have the same T. If the rate increases when dp decreases but does not change with FT0, the trial at the larger dp is limited by internal diffusion

## Slide 31
The graph below shows the reaction rates obtained when the irreversible, liquid-
phase, catalytic reaction A→B was carried out in a PBR using the indicated catalyst dp, T, and FT0. CA0 was the same in each trial.
Chart: dp (cm)
| 0.05 | 0.1 | 0.2 | 0.6 | 0.8
FT0=4000 mol/h, T=400K | 15 | 15 | 14 | 12 | 10
FT0=4000 mol/h, T=300K | 2 | 2 | 2
FT0=3500 mol/h, T=400K | 15 | 15 | 14 | 12 | 10
FT0=3500 mol/h, T=300K | 1.9 | 1.9 | 1.9 | 1.9
FT0=1000 mol/h, T=400K | 2.5
FT0=1500 mol/h, T=400K | 4
FT0=2000 mol/h, T=400K | 8
Which, if any, of the conditions shown (flow rates, T, and dp) is the reaction limited by internal diffusion?
Trial with T = 400K, dp= 0.6 cm & FT0= 4000 mol/h has a lower rate than the trial with T = 400K, dp= 0.2 cm & FT0= 4000 mol/h
Thus, rate is limited by internal diffusion when T = 400K, dp= 0.6 cm & FT0= 4000 mol/h
ext diff lim
ext diff lim
ext diff lim
int diff lim
int diff lim
Internal diffusion limits the observed rate when decreasing dp increases –r’A
Need to find the points that have the same T. If the rate increases when dp decreases but does not change with FT0, the trial at the larger dp is limited by internal diffusion

## Slide 32
The graph below shows the reaction rates obtained when the irreversible, liquid-
phase, catalytic reaction A→B was carried out in a PBR using the indicated catalyst dp, T, and FT0. CA0 was the same in each trial.
Chart: dp (cm)
| 0.05 | 0.1 | 0.2 | 0.6 | 0.8
FT0=4000 mol/h, T=400K | 15 | 15 | 14 | 12 | 10
FT0=4000 mol/h, T=300K | 2 | 2 | 2
FT0=3500 mol/h, T=400K | 15 | 15 | 14 | 12 | 10
FT0=3500 mol/h, T=300K | 1.9 | 1.9 | 1.9 | 1.9
FT0=1000 mol/h, T=400K | 2.5
FT0=1500 mol/h, T=400K | 4
FT0=2000 mol/h, T=400K | 8
Which, if any, of the conditions shown (flow rates, T, and dp) is the reaction limited by internal diffusion?
Trial with T = 400K, dp= 0.2 cm & FT0= 3500 mol/h has a lower rate than the trial with T = 400K, dp= 0.1 cm & FT0= 3500 mol/h
Thus, rate is limited by internal diffusion when T = 400K, dp= 0.2 cm & FT0= 3500 mol/h
ext diff lim
ext diff lim
ext diff lim
int diff lim
int diff lim
int diff lim
Internal diffusion limits the observed rate when decreasing dp increases –r’A
Need to find the points that have the same T. If the rate increases when dp decreases but does not change with FT0, the trial at the larger dp is limited by internal diffusion

## Slide 33
The graph below shows the reaction rates obtained when the irreversible, liquid-
phase, catalytic reaction A→B was carried out in a PBR using the indicated catalyst dp, T, and FT0. CA0 was the same in each trial.
Chart: dp (cm)
| 0.05 | 0.1 | 0.2 | 0.6 | 0.8
FT0=4000 mol/h, T=400K | 15 | 15 | 14 | 12 | 10
FT0=4000 mol/h, T=300K | 2 | 2 | 2
FT0=3500 mol/h, T=400K | 15 | 15 | 14 | 12 | 10
FT0=3500 mol/h, T=300K | 1.9 | 1.9 | 1.9 | 1.9
FT0=1000 mol/h, T=400K | 2.5
FT0=1500 mol/h, T=400K | 4
FT0=2000 mol/h, T=400K | 8
Which, if any, of the conditions shown (flow rates, T, and dp) is the reaction limited by internal diffusion?
Trial with T = 400K, dp= 0.2 cm & FT0= 4000 mol/h has a lower rate than the trial with T = 400K, dp= 0.1 cm & FT0= 4000 mol/h
Thus, rate is limited by internal diffusion when T = 400K, dp= 0.2 cm & FT0= 4000 mol/h
ext diff lim
ext diff lim
ext diff lim
int diff lim
int diff lim
int diff lim
int diff lim
Internal diffusion limits the observed rate when decreasing dp increases –r’A
Need to find the points that have the same T. If the rate increases when dp decreases but does not change with FT0, the trial at the larger dp is limited by internal diffusion

## Slide 34
The graph below shows the reaction rates obtained when the irreversible, liquid-
phase, catalytic reaction A→B was carried out in a PBR using the indicated catalyst dp, T, and FT0. CA0 was the same in each trial.
Chart: dp (cm)
| 0.05 | 0.1 | 0.2 | 0.6 | 0.8
FT0=4000 mol/h, T=400K | 15 | 15 | 14 | 12 | 10
FT0=4000 mol/h, T=300K | 2 | 2 | 2
FT0=3500 mol/h, T=400K | 15 | 15 | 14 | 12 | 10
FT0=3500 mol/h, T=300K | 1.9 | 1.9 | 1.9 | 1.9
FT0=1000 mol/h, T=400K | 2.5
FT0=1500 mol/h, T=400K | 4
FT0=2000 mol/h, T=400K | 8
Which, if any, of the conditions shown (flow rates, T, and dp) is the reaction limited by internal diffusion?
Trial with T = 400K, dp= 0.1 cm & FT0= 3500 mol/h has the SAME rate as the trial with T = 400K, dp= 0.05 cm & FT0= 3500 mol/h
Thus, rate is limited by internal diffusion when T = 400K, dp= 0.2 cm & FT0= 4000 mol/h
ext diff lim
ext diff lim
ext diff lim
int diff lim
int diff lim
int diff lim
int diff lim
Rate is NOT limited by internal diffusion when T = 400K, dp= 0.1 cm & FT0= 3500 mol/h or T = 400K, dp= 0.05 cm & FT0= 3500 mol/h
Internal diffusion limits the observed rate when decreasing dp increases –r’A
Need to find the points that have the same T. If the rate increases when dp decreases but does not change with FT0, the trial at the larger dp is limited by internal diffusion

## Slide 35
The graph below shows the reaction rates obtained when the irreversible, liquid-
phase, catalytic reaction A→B was carried out in a PBR using the indicated catalyst dp, T, and FT0. CA0 was the same in each trial.
Chart: dp (cm)
| 0.05 | 0.1 | 0.2 | 0.6 | 0.8
FT0=4000 mol/h, T=400K | 15 | 15 | 14 | 12 | 10
FT0=4000 mol/h, T=300K | 2 | 2 | 2
FT0=3500 mol/h, T=400K | 15 | 15 | 14 | 12 | 10
FT0=3500 mol/h, T=300K | 1.9 | 1.9 | 1.9 | 1.9
FT0=1000 mol/h, T=400K | 2.5
FT0=1500 mol/h, T=400K | 4
FT0=2000 mol/h, T=400K | 8
Which, if any, of the conditions shown (flow rates, T, and dp) is the reaction limited by internal diffusion?
ext diff lim
ext diff lim
ext diff lim
int diff lim
int diff lim
int diff lim
int diff lim
For all remaining trials, decreasing dp does not increase the reaction rate, so no other trial conditions are internal diffusion limited.
Internal diffusion limits the observed rate when decreasing dp increases –r’A
Need to find the points that have the same T. If the rate increases when dp decreases but does not change with FT0, the trial at the larger dp is limited by internal diffusion

## Slide 36
The graph below shows the reaction rates obtained when the irreversible, liquid-
phase, catalytic reaction A→B was carried out in a PBR using the indicated catalyst dp, T, and FT0. CA0 was the same in each trial.
Chart: dp (cm)
| 0.05 | 0.1 | 0.2 | 0.6 | 0.8
FT0=4000 mol/h, T=400K | 15 | 15 | 14 | 12 | 10
FT0=4000 mol/h, T=300K | 2 | 2 | 2
FT0=3500 mol/h, T=400K | 15 | 15 | 14 | 12 | 10
FT0=3500 mol/h, T=300K | 1.9 | 1.9 | 1.9 | 1.9
FT0=1000 mol/h, T=400K | 2.5
FT0=1500 mol/h, T=400K | 4
FT0=2000 mol/h, T=400K | 8
Which, if any, of the conditions shown (flow rates, T, and dp) is the reaction limited by the surface reaction?
The surface reaction limits the reaction rate when the observed rxn rate increases when we increase T, but it does not increase when we decrease dp or increase FT0 without increasing CT0
ext diff lim
ext diff lim
ext diff lim
int diff lim
int diff lim
int diff lim
int diff lim
For all remaining trials, neither decreasing dp nor increasing FT0 increases the reaction rate. Therefore, the surface reaction limits (slows down) the rates of the remaining trial conditions.

## Slide 37
The graph below shows the reaction rates obtained when the irreversible, liquid-
phase, catalytic reaction A→B was carried out in a PBR using the indicated catalyst dp, T, and FT0. CA0 was the same in each trial.
Chart: dp (cm)
| 0.05 | 0.1 | 0.2 | 0.6 | 0.8
FT0=4000 mol/h, T=400K | 15 | 15 | 14 | 12 | 10
FT0=4000 mol/h, T=300K | 2 | 2 | 2
FT0=3500 mol/h, T=400K | 15 | 15 | 14 | 12 | 10
FT0=3500 mol/h, T=300K | 1.9 | 1.9 | 1.9 | 1.9
FT0=1000 mol/h, T=400K | 2.5
FT0=1500 mol/h, T=400K | 4
FT0=2000 mol/h, T=400K | 8
Which, if any, of the conditions shown (flow rates, T, and dp) is the reaction limited by the surface reaction?
ext diff lim
ext diff lim
ext diff lim
int diff lim
int diff lim
int diff lim
int diff lim
For all remaining trials, neither decreasing dp nor increasing FT0 increases the reaction rate. Therefore, the surface reaction limits (slows down) the rates of the remaining trial conditions.
Surface reaction limited (SRL):
T = 400K, dp= 0.1 cm & FT0= 3500 mol/h,
SRL
T = 400K, dp= 0.05 cm & FT0= 3500 mol/h,
T = 400K, dp= 0.1 cm & FT0= 4000 mol/h,
T = 400K, dp= 0.05 cm & FT0= 4000 mol/h,
T = 300K, all dp tested, & FT0= 4000 mol/h &
T = 300K, all dp tested, & FT0= 3500 mol/h
SRL

## Slide 38
Type of Limitation | Variation of Reaction Rate with: |  | 
 | Superficial velocity | Particle size | Temperature
External | U1/2 | dp-3/2 | Linear
Internal | Independent | dp-1 | Exponential
Surface reaction | Independent | Independent | Exponential
Type of Limitation | Variation of Reaction Rate with: |  | 
 | Superficial velocity | Particle size | Temperature
External | U1/2 | dp-3/2 | Linear
Internal | Independent | dp-1 | Exponential
Surface reaction | Independent | Independent | Exponential
The catalytic reaction A→B takes place in a fixed bed reactor containing spherical porous catalyst X22. The overall rxn rates at a point in the reactor are shown in the graph below. For which, if any, of the conditions shown (flow rates and temps) is the reaction limited by external diffusion?
-r’A (mol/gcat·s)
External diffusion limited where –r’A↑ linearly when T↑
For FT0 = 10 mol/h, the rate of rxn increases approximately linearly with T over the entire temperature range- external diffusion limited at FT0 = 10 and all T
For FT0 = 100 mol/h, the rate of rxn increases ~linearly with T when T > 360K. The reaction is external diffusion limited when FT0 = 100 & T> 360K

## Slide 39
Type of Limitation | Variation of Reaction Rate with: |  | 
 | Superficial velocity | Particle size | Temperature
External | U1/2 | dp-3/2 | Linear
Internal | Independent | dp-1 | Exponential
Surface reaction | Independent | Independent | Exponential
The catalytic reaction A→B takes place in a fixed bed reactor containing spherical porous catalyst X22. The overall rxn rates at a point in the reactor are shown in the graph below. For which, if any, of the conditions shown (flow rates and temps) is the reaction limited by surface reaction rate?
-r’A (mol/gcat·s)
Type of Limitation | Variation of Reaction Rate with: |  | 
 | Superficial velocity | Particle size | Temperature
External | U1/2 | dp-3/2 | Linear
Internal | Independent | dp-1 | Exponential
Surface reaction | Independent | Independent | Exponential
Surface rxn limited when –r’Aincreases
exponentially with T↑ but independent of superficial velocity (flow!)
For conditions FT0 = 100, 1000 & 5000 mol/h at T< 360K, rxn rate is independent of FT0 but exponentially dependent on T→ surface reaction limited
Rxn rates ↑ exp with T but not FT0 for FT0 = 100, 1000 & 5000 mol/h at T< 360K
ext diff lim

## Slide 40
Type of Limitation | Variation of Reaction Rate with: |  | 
 | Superficial velocity | Particle size | Temperature
External | U1/2 | dp-3/2 | Linear
Internal | Independent | dp-1 | Exponential
Surface reaction | Independent | Independent | Exponential
The catalytic reaction A→B takes place in a fixed bed reactor containing spherical porous catalyst X22. The overall rxn rates at a point in the reactor are shown in the graph below. For which, if any, of the conditions shown (flow rates and temps) is the reaction limited by surface reaction rate?
-r’A (mol/gcat·s)
Type of Limitation | Variation of Reaction Rate with: |  | 
 | Superficial velocity | Particle size | Temperature
External | U1/2 | dp-3/2 | Linear
Internal | Independent | dp-1 | Exponential
Surface reaction | Independent | Independent | Exponential
Surface rxn limited when –r’Aincreases exponentially with T↑ but independent of velocity
For FT0 = 100, 1000 & 5000 mol/h at T< 360K → surface reaction limited
For FT0 = 1000 & 5000 mol/h at T< 366K, rxn rates ↑ exp with T but not FT0
For conditions FT0 = 1000 & 5000 mol/h at T< 366K, rxn rate is independent of FT0 but exponentially dependent on T→ surface reaction limited
ext diff lim

## Slide 41
Type of Limitation | Variation of Reaction Rate with: |  | 
 | Superficial velocity | Particle size | Temperature
External | U1/2 | dp-3/2 | Linear
Internal | Independent | dp-1 | Exponential
Surface reaction | Independent | Independent | Exponential
The catalytic reaction A→B takes place in a fixed bed reactor containing spherical porous catalyst X22. The overall rxn rates at a point in the reactor are shown in the graph below. For which, if any, of the conditions shown (flow rates and temps) is the reaction limited by internal diffusion?
-r’A (mol/gcat·s)
Type of Limitation | Variation of Reaction Rate with: |  | 
 | Superficial velocity | Particle size | Temperature
External | U1/2 | dp-3/2 | Linear
Internal | Independent | dp-1 | Exponential
Surface reaction | Independent | Independent | Exponential
Internal diffusion limited when –r’Aincreases exponentially with T↑ & is independent of velocity
For FT0 = 1000 & 5000 mol/h at T> 367K, rxn rate is roughly independent of FT0 but exponentially dependent on T. The reaction rate is internal diffusion limited at T> 370K for FT0 = 1000 & 5000 mol/h
Rxn rates ↑ exp with T but not FT0 for FT0= 1000 & 5000 mol/h at T> 367K
ext diff lim
rxn lim

## Slide 42
Type of Limitation | Variation of Reaction Rate with: |  | 
 | Superficial velocity | Particle size | Temperature
External | U1/2 | dp-3/2 | Linear
Internal | Independent | dp-1 | Exponential
Surface reaction | Independent | Independent | Exponential
The catalytic reaction A→B takes place in a fixed bed reactor containing spherical porous catalyst X22. The overall rxn rates at a point in the reactor are shown in the graph below. For which, if any, of the conditions shown (flow rates and temps) is the reaction limited by internal diffusion?
-r’A (mol/gcat·s)
Type of Limitation | Variation of Reaction Rate with: |  | 
 | Superficial velocity | Particle size | Temperature
External | U1/2 | dp-3/2 | Linear
Internal | Independent | dp-1 | Exponential
Surface reaction | Independent | Independent | Exponential
Internal diffusion limited when –r’Aincreases exponentially with T↑ & is independent of velocity
How do we know it’s not surface rxn limited at FT0=1000 & 5000 mol/h & T>367K?
As T↑, the specific rate constant k↑, the rate of the surface rxn & consumption of reactant ↑. Thus the reactant is more likely to be consumed before it reaches the core.
ext diff lim
rxn lim
int
diff lim

## Slide 43
The catalytic reaction A→B takes place in a fixed bed reactor containing spherical porous catalyst X22. The overall rxn rates at a point in the reactor are shown in the graph below. For a flow rate of 10 g mol/h, determine the overall effectiveness factor W at 360K
-r’A (mol/gcat·s)
Internal
diff limited
External diff limited
Surface rxn limited
0.26
What do we use for the rate of reaction if the interior was exposed to bulk conditions?
Use the rxn rate obtained under surface reaction limited conditions
Rxn w/out diffusion limitations
0.70

## Slide 44
The catalytic reaction A→B takes place in a fixed bed reactor containing spherical porous catalyst X22. The overall rxn rates at a point in the reactor are shown in the graph below. For FT0= 5000 g mol/h, estimate the internal effectiveness factor h at 367K
-r’A (mol/gcat·s)
Internal
diff limited
External diff limited
Surface rxn limited
1.2
What do we use for the rate of reaction if the interior was exposed to the conditions at the surface of the pellet?
Extrapolate the line for the surface reaction limited regime of the FT0 = 5000 mol/h plot to estimate the rxn rate that would be obtained without internal diffusion
Rxn w/out internal diffusion limitations
1.4

## Slide 45
XA1=0.632 for dp, z, & u0
Type of Limitation | Variation of Reaction Rate with: |  | 
 | Superficial velocity | Particle size | Temperature
External | U1/2 | dp-3/2 | Linear
Internal | Independent | dp-1 | Exponential
Surface reaction | Independent | Independent | Exponential
XA2=? for dp1/3, 1.5z1, and 4u0,1
Cl2 is removed from a waste stream by passing the effluent gas over a solid granular absorbent in a tubular PBR. Presently 63.2% is removed and the reaction is external diffusion limited. If the flow rate were increases by a factor of 4, the particle diameter were decreased by a factor of 3, and the tube length (z) were increased by 1.5x, what percentage of Cl2 would be removed (assume still external diffusion limited)? What guidelines (T, CA, u) do you propose for efficient operation of this bed?

## Slide 46
XA1=0.632 for dp, z, & u0
XA2=? for dp1/3, 1.5z1, and 4u0,1
Cl2 is removed from a waste stream by passing the effluent gas over a solid granular absorbent in a tubular PBR. Presently 63.2% is removed and the reaction is external diffusion limited. If the flow rate were increases by a factor of 4, the particle diameter were decreased by a factor of 3, and the tube length (z) were increased by 1.5x, what percentage of Cl2 would be removed (assume still external diffusion limited)? What guidelines (T, CA, u) do you propose for efficient operation of this bed?
Need to relate XA to reactor length in the presence of an external diffusion limit

## Slide 47: Review: Mass Transfer Limited Rxn in PBR
ac: external surface area of catalyst per volume of catalytic bed (m2/m3)
f: porosity of bed, void fraction dp: particle diameter (m)
r’’A: rate of generation of A per unit catalytic surface area (mol/s·m2)
A steady state mole balance on reactant A between z and z + z :
Divide out AcDz:
Take limit as Dz→0:
Put Faz and –rA’’ in terms of CA:
Axial diffusion is negligible compared to bulk flow (convection)
Substitute into the mass balance
0

## Slide 48: Review: Mass Transfer Limited Rxn in PBR (continued)
At steady-state:
Molar flux of A to particle surface = rate of disappearance of A on the surface
mass transfer coefficient kc =DAB/d (s-1) d: boundary layer thickness
CAs: concentration of A at surface CA: concentration of A in bulk
Substitute
CAs ≈ 0 in most mass transfer-limited rxns
Rearrange & integrate to find how CA and the r’’A varies with distance down reactor

## Slide 49
ac: external surface area of catalyst per catalyst bed volume
f: porosity of bed
Cl2 is removed from a waste stream by passing the effluent gas over a solid granular absorbent in a tubular PBR. Presently 63.2% is removed and the reaction is external diffusion limited. If the flow rate were increases by a factor of 4, the particle diameter were decreased by a factor of 3, and the tube length (z) were increased by 1.5x, what percentage of Cl2 would be removed (assume still external diffusion limited)? What guidelines (T, CA, u) do you propose for efficient operation of this bed?
XA1=0.632 for dp, z, & u0 XA2=? for dp1/3, 1.5z1, and 4u0,1
For an external diffusion limited rxn in a PBR, we found (L19):
In terms of XA:
Express XA at 2 reaction conditions as a ratio:
Relate U to u0 & ac to dp

## Slide 50
How are kc1 and kc2 related?
Typically the 2 is negligible so
XA1=0.632 for dp, z, & u0 XA2=? for dp1/3, 1.5z1, and 4u0,1
Cl2 is removed from a waste stream by passing the effluent gas over a solid granular absorbent in a tubular PBR. Presently 63.2% is removed and the reaction is external diffusion limited. If the flow rate were increases by a factor of 4, the particle diameter were decreased by a factor of 3, and the tube length (z) were increased by 1.5x, what percentage of Cl2 would be removed (assume still external diffusion limited)? What guidelines (T, CA, u) do you propose for efficient operation of this bed?

## Slide 51
XA1=0.632 for dp, z, & u0 XA2=? for dp1/3, 1.5z1, and 4u0,1
Cl2 is removed from a waste stream by passing the effluent gas over a solid granular absorbent in a tubular PBR. Presently 63.2% is removed and the reaction is external diffusion limited. If the flow rate were increases by a factor of 4, the particle diameter were decreased by a factor of 3, and the tube length (z) were increased by 1.5x, what percentage of Cl2 would be removed (assume still external diffusion limited)? What guidelines (T, CA, u) do you propose for efficient operation of this bed?

## Slide 52
XA1=0.632 for dp, z, & u0 XA2=? for dp1/3, 1.5z1, and 4u0,1
Cl2 is removed from a waste stream by passing the effluent gas over a solid granular absorbent in a tubular PBR. Presently 63.2% is removed and the reaction is external diffusion limited. If the flow rate were increases by a factor of 4, the particle diameter were decreased by a factor of 3, and the tube length (z) were increased by 1.5x, what percentage of Cl2 would be removed (assume still external diffusion limited)? What guidelines (T, CA, u) do you propose for efficient operation of this bed?

## Slide 53
To keep the rate of Cl2 consumption (surface reaction) faster than external diffusion (still in external diffusion limited regime), use high T
XA1=0.632 for dp, z, & u0 XA2=0.98 for dp1/3, 1.5z1, and 4u0,1
Cl2 is removed from a waste stream by passing the effluent gas over a solid granular absorbent in a tubular PBR. Presently 63.2% is removed and the reaction is external diffusion limited. If the flow rate were increases by a factor of 4, the particle diameter were decreased by a factor of 3, and the tube length (z) were increased by 1.5x, what percentage of Cl2 would be removed (assume still external diffusion limited)? What guidelines (T, CA, u) do you propose for efficient operation of this bed?
Type of Limitation | Variation of Reaction Rate with: |  | 
 | Superficial velocity | Particle size | Temperature
External | U1/2 | dp-3/2 | Linear
Internal | Independent | dp-1 | Exponential
Surface reaction | Independent | Independent | Exponential
Hint for T: The conversion of 0.98 is dependent on the reaction still being external diffusion-limited. How can we adjust the T, CA, and u to make sure that the process is not instead slowed down by the surface reaction, but without slowing down external diffusion?

## Slide 54
The mass transfer rate can be increased by increasing the concentration gradient, which is achieved by increasing the bulk concentration of A
Increasing the volumetric flow rate u0 increases the mass transfer coefficient but reduces the spacetime, and therefore XA. The process also becomes reaction limited instead of external diffusion limited. XA,mass x-fer a kc a u01/2 but XA,reaction a t a u0-1 so the increase in u0 may be offset by a reaction-limited decrease in conversion, assuming constant packed-bed properties. We would need the parameters for the reaction to evaluate whether increasing u0 is a good idea.
XA1=0.632 for dp, z, & u0 XA2=0.98 for dp1/3, 1.5z1, and 4u0,1
Cl2 is removed from a waste stream by passing the effluent gas over a solid granular absorbent in a tubular PBR. Presently 63.2% is removed and the reaction is external diffusion limited. If the flow rate were increases by a factor of 4, the particle diameter were decreased by a factor of 3, and the tube length (z) were increased by 1.5x, what percentage of Cl2 would be removed (assume still external diffusion limited)? What guidelines (T, CA, u) do you propose for efficient operation of this bed?
Hint: How does changing CA and u influence the rate of external diffusion and the surface reaction?