## Slide 1: Review: Nonideal Flow in a CSTR
Dead Zone
Ideal CSTR: uniform reactant concentration throughout the vessel
Real stirred tank
  Relatively high reactant concentration at the feed entrance
  Relatively low concentration in the stagnant regions, called dead zones (usually corners and behind baffles)
Short Circuiting
Dead Zone

## Slide 2: Review: Nonideal Flow in a PBR
Ideal plug flow reactor: all reactant and product molecules at any given axial position move at same rate in the direction of the bulk fluid flow
Real plug flow reactor: fluid velocity profiles, turbulent mixing, & molecular diffusion cause molecules to move with changing speeds and in different directions
channeling
Dead zones

## Slide 3: Review: Residence Time Distribution
RTD is experimentally determined by injecting an inert “tracer” at t=0 and measuring the tracer concentration C(t) at exit as a function of time
RTD ≡ E(t) ≡ “residence time distribution” function
RTD describes the amount of time molecules have spent in the reactor
Measurement of RTD
↑
Pulse injection
↓
Detection
Reactor
X
C(t)
C curve
t
Fraction of material leaving reactor that has been inside reactor for a time between t1 & t2
E(t)=0 for t<0 since no tracer can exit before it enters
E(t)≥0 for t>0 since mass fractions are always positive

## Slide 4
t min | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 12 | 14
C g/m3 | 0 | 1 | 5 | 8 | 10 | 8 | 6 | 4 | 3 | 2.2 | 1.5 | 0.6 | 0
A pulse of tracer was injected into a reactor, and the effluent concentration as a function of time is in the graph below. Construct a figure of C(t) & E(t) and calculate the fraction of material that spent between 3 & 6 min in the reactor
Chart: t (min)
| 0.0 | 1.0 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 9.0 | 10.0 | 12.0 | 14.0
 | 0 | 1 | 5 | 8 | 10 | 8 | 6 | 4 | 3 | 2.2 | 1.5 | 0.6 | 0
Plot C vs time:
To tabulate E(t): divide C(t) by the total area under the C(t) curve, which must be numerically evaluated as shown below:

## Slide 5
t min | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 12 | 14
C g/m3 | 0 | 1 | 5 | 8 | 10 | 8 | 6 | 4 | 3 | 2.2 | 1.5 | 0.6 | 0
A pulse of tracer was injected into a reactor, and the effluent concentration as a function of time is in the graph below. Construct a figure of C(t) & E(t) and calculate the fraction of material that spent between 3 & 6 min in the reactor
Tabulate E(t): divide C(t) by the total area under the C(t) curve:
t min | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 12 | 14
C g/m3 | 0 | 1 | 5 | 8 | 10 | 8 | 6 | 4 | 3 | 2.2 | 1.5 | 0.6 | 0
E(t) | 0 | 0.02 | 0.1 | 0.16 | 0.2 | 0.16 | 0.12 | 0.08 | 0.06 | 0.044 | 0.03 | 0.012 | 0
Plot E(t):
Chart: t (min)
| 0.0 | 1.0 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 9.0 | 10.0 | 12.0 | 14.0
 | 0 | 0.02 | 0.1 | 0.16 | 0.2 | 0.16 | 0.12 | 0.08 | 0.06 | 0.044 | 0.03 | 0.012 | 0

## Slide 6
t
E(t)

t
E(t)
t
E(t)

Nearly ideal PFR
Nearly ideal CSTR
PBR with channeling & dead zones
t
E(t)
CSTR with dead zones
40
t (min)
F(t)
0.8
80% of the molecules spend 40 min or less in the reactor
F(t)=fraction of effluent in the reactor less for than time t
Review: RTD Profiles & Cum RTD Function F(t)

## Slide 7: Review: Relationship between E & F
F(t) = fraction of effluent that has been in the reactor for less than time t
E(t)= Fraction of material leaving reactor that was inside for a time between t1 & t2

## Slide 8: Review: Mean Residence Time, tm
For an ideal reactor, the space time  is defined as V/u0
The mean residence time tm is equal to in either ideal or nonideal reactors
By calculating tm, the reactor V can be determined from a tracer experiment
The spread of the distribution (variance):
Space time t and mean residence time tm would be equal if the following two conditions are satisfied:
  No density change
  No backmixing
In practical reactors the above two may not be valid, hence there will be a difference between them

## Slide 9: Significance of Mixing
RTD provides information on how long material has been in the reactor
RTD does not provide information about the exchange of matter within the reactor (i.e., mixing)!
For a 1st order reaction:
Concentration does not affect the rate of conversion, so RTD is sufficient to predict conversion
But concentration does affect conversion in higher order reactions, so we need to know the degree of mixing in the reactor
Macromixing: produces a distribution of residence times without specifying how molecules of different age encounter each other and are distributed inside of the reactor
Micromixing: describes how molecules of different residence time encounter each other in the reactor

## Slide 10: Quality of Mixing
RTDs alone are not sufficient to determine reactor performance
Quality of mixing is also required
Goal: use RTD and micromixing models to predict conversion in real reactors
2 Extremes of Fluid Mixing
Maximum mixedness: molecules are free to move anywhere, like a microfluid. This is the extreme case of early mixing

## Slide 11: Quality of Mixing
RTDs alone are not sufficient to determine reactor performance
Quality of mixing is also required
Goal: use RTD and micromixing models to predict conversion in real reactors
2 Extremes of Fluid Mixing
Complete segregation: molecules of a given age do not mix with other globules. This is the extreme case of late mixing
Maximum mixedness: molecules are free to move anywhere, like a microfluid. This is the extreme case of early mixing

## Slide 12: Complete Segregation Model
  Flow is visualized in the form of globules
  Each globule consists of molecules of the same residence time
  Different globules have different residence times
  No interaction/mixing between different globules
Mixing of different ‘age groups’ at the last possible moment
The mean conversion is the average conversion of the various globules in the exit stream:
Conversion achieved after spending time tj in the reactor
Fraction of globules that spend between tj and tj + Dt in the reactor
XA(t) is from the batch reactor design equation
Notes: Can we make a model where the time in the reactor is dictated by a gaussian distribution, and the conversion follows a first order reaction?

## Slide 13: Complete Segregation Example
First order reaction, A→Products
Batch reactor design equation:
To compute conversion for a reaction with a 1st order rxn and complete segregation, insert E(t) from tracer experiment and XA(t) from batch reactor design equation into:
& integrate
Notes: Can we make a model where the time in the reactor is dictated by a gaussian distribution, and the conversion follows a first order reaction?

## Slide 14: Maximum Mixedness Model
In a PFR: as soon as the fluid enters the reactor, it is completely mixed radially with the other fluid already in the reactor. Like a PFR with side entrances, where each entrance port creates a new residence time:
 +Dl
  0
V = 0
V = V0
: time it takes for fluid to move from a particular point to end of the reactor
u0
u0E(l)Dl: Volumetric flow rate of fluid fed into side ports of reactor in interval between  +  & 
Volumetric flow rate of fluid fed to reactor at :
Volume of fluid with life expectancy between  +  & :
u(l): volumetric flow rate at l, = flow that entered at l+Dl plus what entered through the sides
fraction of effluent in reactor for less than time t
 ∞


## Slide 15: Maximum Mixedness & Polymath
Also need to replace l because Polymath cannot calculate as l gets smaller
E(t) must be specified
Often it is an expression that fits the experimental data
2 curves, one on the increasing side, and a second for the decreasing side
Use the IF function to specify which E is used when
E
t
E1
E2
Note that the sign on each term changes
Mole balance on A gives:
fraction of effluent in reactor for less than time t
residence time distribution function
See section 13.8 in book

## Slide 16: Review: Nonideal Flow & Reactor Design
Real CSTRs
  Relatively high reactant conc at entrance
  Relatively low conc in stagnant regions, called dead zones (corners & behind baffles)
Dead Zone
Dead Zone
Short Circuiting
Real PBRs
fluid velocity profiles, turbulent mixing, & molecular diffusion cause molecules to move at varying speeds & directions
channeling
Dead zones
Goal: mathematically describe non-ideal flow and solve design problems for reactors with nonideal flow

## Slide 17: Residence Time Distribution (RTD)
RTD is experimentally determined by injecting an inert “tracer” at t=0 and measuring the tracer concentration C(t) at exit as a function of time
RTD ≡ E(t) ≡ “residence time distribution” function
RTD describes the amount of time molecules have spent in the reactor
Measurement of RTD
↑
Pulse injection
↓
Detection
Reactor
X
C(t)
The C curve
t
Fraction of material leaving reactor that has been inside reactor for a time between t1 & t2
E(t)=0 for t<0 since no fluid can exit before it enters
E(t)≥0 for t>0 since mass fractions are always positive

## Slide 18
t
E(t)

t
E(t)
t
E(t)

Nearly ideal PFR
Nearly ideal CSTR
PBR with dead zones
t
E(t)
CSTR with dead zones
The fraction of the exit stream that has resided in the reactor for a period of time shorter than a given value t:
F(t) is a cumulative distribution function
40
0.8
80% of the molecules spend 40 min or less in the reactor
Nice multiple choice question

## Slide 19: Review: Mean Residence Time, tm
For an ideal reactor, the space time  is defined as V/u0
The mean residence time tm is equal to  in either ideal or nonideal reactors
By calculating tm, the reactor V can be determined from a tracer experiment
The spread of the distribution (variance):
Space time t and mean residence time tm would be equal if the following two conditions are satisfied:
  No density change
  No backmixing
In practical reactors the above two may not be valid, hence there will be a difference between them

## Slide 20: Review: Complete Segregation Model
  Flow is visualized in the form of globules
  Each globule consists of molecules of the same residence time
  Different globules have different residence times
  No interaction/mixing between different globules
Mixing of different ‘age groups’ at the last possible moment
The mean conversion is the average conversion of the various globules in the exit stream:
Conversion achieved after spending time tj in the reactor
Fraction of globules that spend between tj and tj + Dt in the reactor
XA(t) is from the batch reactor design equation

## Slide 21: Review: Maximum Mixedness Model
In a PFR: as soon as the fluid enters the reactor, it is completely mixed radially with the other fluid already in the reactor. Like a PFR with side entrances, where each entrance port creates a new residence time:
 +Dl
  0
V = 0
V = V0
: time it takes for fluid to move from a particular point to end of the reactor
u0
u0E(l)Dl: Volumetric flow rate of fluid fed into side ports of reactor in interval between  +  & 
Volumetric flow rate of fluid fed to reactor at :
Volume of fluid with life expectancy between  +  & :
u(l): volumetric flow rate at l, = flow that entered at l+Dl plus what entered through the sides
fraction of effluent that in reactor for less than time t
 ∞


## Slide 22
t min | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 12 | 14
C g/m3 | 0 | 1 | 5 | 8 | 10 | 8 | 6 | 4 | 3 | 2.2 | 1.5 | 0.6 | 0
E(t) | 0 | 0.02 | 0.1 | 0.16 | 0.2 | 0.16 | 0.12 | 0.08 | 0.06 | 0.044 | 0.03 | 0.012 | 0
For a pulse tracer expt, the effluent concentration C(t) & RTD function E(t) are given
in the table below. The irreversible, liquid-phase, nonelementary rxn A+B→C+D, -rA=kCACB2 will be carried out isothermally at 320K in this reactor. Calculate the conversion for (1) an ideal PFR and (2) for the complete segregation model.
CA0=CB0=0.0313 mol/L & k=176 L2/mol2·min at 320K

## Slide 23
t min | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 12 | 14
C g/m3 | 0 | 1 | 5 | 8 | 10 | 8 | 6 | 4 | 3 | 2.2 | 1.5 | 0.6 | 0
E(t) | 0 | 0.02 | 0.1 | 0.16 | 0.2 | 0.16 | 0.12 | 0.08 | 0.06 | 0.044 | 0.03 | 0.012 | 0
Start with PFR design eq & see how far can we get:
For a pulse tracer expt, the effluent concentration C(t) & RTD function E(t) are given
in the table below. The irreversible, liquid-phase, nonelementary rxn A+B→C+D, -rA=kCACB2 will be carried out isothermally at 320K in this reactor. Calculate the conversion for (1) an ideal PFR and (2) for the complete segregation model.
CA0=CB0=0.0313 mol/L & k=176 L2/mol2·min at 320K
Get like terms together & integrate

## Slide 24
t min | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 12 | 14
C g/m3 | 0 | 1 | 5 | 8 | 10 | 8 | 6 | 4 | 3 | 2.2 | 1.5 | 0.6 | 0
E(t) | 0 | 0.02 | 0.1 | 0.16 | 0.2 | 0.16 | 0.12 | 0.08 | 0.06 | 0.044 | 0.03 | 0.012 | 0
For a pulse tracer expt, the effluent concentration C(t) & RTD function E(t) are given
in the table below. The irreversible, liquid-phase, nonelementary rxn A+B→C+D, -rA=kCACB2 will be carried out isothermally at 320K in this reactor. Calculate the conversion for (1) an ideal PFR and (2) for the complete segregation model.
CA0=CB0=0.0313 mol/L & k=176 L2/mol2·min at 320K
How do we determine t?
For an ideal reactor, t = tm
Use numerical method to determine tm:
t min | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 12 | 14
C g/m3 | 0 | 1 | 5 | 8 | 10 | 8 | 6 | 4 | 3 | 2.2 | 1.5 | 0.6 | 0
E(t) | 0 | 0.02 | 0.1 | 0.16 | 0.2 | 0.16 | 0.12 | 0.08 | 0.06 | 0.044 | 0.03 | 0.012 | 0
t*E(t) | 0 | 0.02 | 0.2 | 0.48 | 0.8 | 0.8 | 0.72 | 0.56 | 0.48 | 0.396 | 0.3 | 0.144 | 0

## Slide 25
t min | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 12 | 14
C g/m3 | 0 | 1 | 5 | 8 | 10 | 8 | 6 | 4 | 3 | 2.2 | 1.5 | 0.6 | 0
E(t) | 0 | 0.02 | 0.1 | 0.16 | 0.2 | 0.16 | 0.12 | 0.08 | 0.06 | 0.044 | 0.03 | 0.012 | 0
For a pulse tracer expt, the effluent concentration C(t) & RTD function E(t) are given
in the table below. The irreversible, liquid-phase, nonelementary rxn A+B→C+D, -rA=kCACB2 will be carried out isothermally at 320K in this reactor. Calculate the conversion for (1) an ideal PFR and (2) for the complete segregation model.
CA0=CB0=0.0313 mol/L & k=176 L2/mol2·min at 320K
t min | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 12 | 14
C g/m3 | 0 | 1 | 5 | 8 | 10 | 8 | 6 | 4 | 3 | 2.2 | 1.5 | 0.6 | 0
E(t) | 0 | 0.02 | 0.1 | 0.16 | 0.2 | 0.16 | 0.12 | 0.08 | 0.06 | 0.044 | 0.03 | 0.012 | 0
t*E(t) | 0 | 0.02 | 0.2 | 0.48 | 0.8 | 0.8 | 0.72 | 0.56 | 0.48 | 0.396 | 0.3 | 0.144 | 0
For an ideal PFR reactor, t = tm

## Slide 26
t min | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 12 | 14
C g/m3 | 0 | 1 | 5 | 8 | 10 | 8 | 6 | 4 | 3 | 2.2 | 1.5 | 0.6 | 0
E(t) | 0 | 0.02 | 0.1 | 0.16 | 0.2 | 0.16 | 0.12 | 0.08 | 0.06 | 0.044 | 0.03 | 0.012 | 0
Segregation model:
XA(t) is from batch reactor design eq
For a pulse tracer expt, the effluent concentration C(t) & RTD function E(t) are given
in the table below. The irreversible, liquid-phase, nonelementary rxn A+B→C+D, -rA=kCACB2 will be carried out isothermally at 320K in this reactor. Calculate the conversion for an ideal PFR, the complete segregation model and maximum mixedness model. CA0=CB0=0.0313 mol/L & k=176 L2/mol2·min at 320K
Numerical method
Solve batch reactor design equation to determine eq for XA
Determine XA for each time
Use numerical methods to determine ¯X A
Polymath Method
Use batch reactor design equation to find eq for XA
Use Polymath polynomial curve fitting to find equation for E(t)
Use Polymath to determine ¯X A

## Slide 27
t min | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 12 | 14
C g/m3 | 0 | 1 | 5 | 8 | 10 | 8 | 6 | 4 | 3 | 2.2 | 1.5 | 0.6 | 0
E(t) | 0 | 0.02 | 0.1 | 0.16 | 0.2 | 0.16 | 0.12 | 0.08 | 0.06 | 0.044 | 0.03 | 0.012 | 0
Segregation model:
XA(t) is from batch reactor design eq
Batch design eq:
Stoichiometry:
For a pulse tracer expt, the effluent concentration C(t) & RTD function E(t) are given
in the table below. The irreversible, liquid-phase, nonelementary rxn A+B→C+D, -rA=kCACB2 will be carried out isothermally at 320K in this reactor. Calculate the conversion for an ideal PFR, the complete segregation model and maximum mixedness model. CA0=CB0=0.0313 mol/L & k=176 L2/mol2·min at 320K

## Slide 28
Segregation model:
Numerical method
t min | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 12 | 14
C g/m3 | 0 | 1 | 5 | 8 | 10 | 8 | 6 | 4 | 3 | 2.2 | 1.5 | 0.6 | 0
E(t) | 0 | 0.02 | 0.1 | 0.16 | 0.2 | 0.16 | 0.12 | 0.08 | 0.06 | 0.044 | 0.03 | 0.012 | 0
XA |  |  |  |  |  |  |  |  |  |  |  |  | 
Plug in each t & solve
For a pulse tracer expt, the effluent concentration C(t) & RTD function E(t) are given
in the table below. The irreversible, liquid-phase, nonelementary rxn A+B→C+D, -rA=kCACB2 will be carried out isothermally at 320K in this reactor. Calculate the conversion for an ideal PFR, the complete segregation model and maximum mixedness model. CA0=CB0=0.0313 mol/L & k=176 L2/mol2·min at 320K

## Slide 29
t min | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 12 | 14
C g/m3 | 0 | 1 | 5 | 8 | 10 | 8 | 6 | 4 | 3 | 2.2 | 1.5 | 0.6 | 0
E(t) | 0 | 0.02 | 0.1 | 0.16 | 0.2 | 0.16 | 0.12 | 0.08 | 0.06 | 0.044 | 0.03 | 0.012 | 0
XA | 0 | 0.137 | 0.23 | 0.298 | 0.35 | 0.39 | 0.428 | 0.458 | 0.483 | 0.505 | 0.525 | 0.558 | 0.585
Segregation model:
Numerical method
For a pulse tracer expt, the effluent concentration C(t) & RTD function E(t) are given
in the table below. The irreversible, liquid-phase, nonelementary rxn A+B→C+D, -rA=kCACB2 will be carried out isothermally at 320K in this reactor. Calculate the conversion for an ideal PFR, the complete segregation model and maximum mixedness model. CA0=CB0=0.0313 mol/L & k=176 L2/mol2·min at 320K

## Slide 30
t min | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 12 | 14
C g/m3 | 0 | 1 | 5 | 8 | 10 | 8 | 6 | 4 | 3 | 2.2 | 1.5 | 0.6 | 0
E(t) | 0 | 0.02 | 0.1 | 0.16 | 0.2 | 0.16 | 0.12 | 0.08 | 0.06 | 0.044 | 0.03 | 0.012 | 0
XA | 0 | 0.137 | 0.23 | 0.298 | 0.35 | 0.39 | 0.428 | 0.458 | 0.483 | 0.505 | 0.525 | 0.558 | 0.585
Segregation model:
Numerical method
For a pulse tracer expt, the effluent concentration C(t) & RTD function E(t) are given
in the table below. The irreversible, liquid-phase, nonelementary rxn A+B→C+D, -rA=kCACB2 will be carried out isothermally at 320K in this reactor. Calculate the conversion for an ideal PFR, the complete segregation model and maximum mixedness model. CA0=CB0=0.0313 mol/L & k=176 L2/mol2·min at 320K

## Slide 31
t min | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 12 | 14
C g/m3 | 0 | 1 | 5 | 8 | 10 | 8 | 6 | 4 | 3 | 2.2 | 1.5 | 0.6 | 0
E(t) | 0 | 0.02 | 0.1 | 0.16 | 0.2 | 0.16 | 0.12 | 0.08 | 0.06 | 0.044 | 0.03 | 0.012 | 0
XA | 0 | 0.137 | 0.23 | 0.298 | 0.35 | 0.39 | 0.428 | 0.458 | 0.483 | 0.505 | 0.525 | 0.558 | 0.585
Alternative approach: segregation model by Polymath:
CB0=0.0313
k=176
Need an equation for E(t)
Use Polymath to fit the E(t) vs t data in the table to a polynomial
For a pulse tracer expt, the effluent concentration C(t) & RTD function E(t) are given
in the table below. The irreversible, liquid-phase, nonelementary rxn A+B→C+D, -rA=kCACB2 will be carried out isothermally at 320K in this reactor. Calculate the conversion for an ideal PFR, the complete segregation model and maximum mixedness model. CA0=CB0=0.0313 mol/L & k=176 L2/mol2·min at 320K

## Slide 32
time
E(t)
E(t) = 0 at t=0
Gave best fit
Model: C02= a1*C01 + a2*C01^2 + a3*C01^3 + a4*C01^4
Final Equation: E= 0.0889237*t -0.0157181*t2 + 0.0007926*t3 – 8.63E-6*t4
a1=0.0889237
a2= -0.0157181
a3= 0.0007926
a4= -8.63E-06
For the irreversible, liquid-phase, nonelementary rxn A+B→C+D, -rA=kCACB2
Calculate the XA using the complete segregation model using Polymath

## Slide 33
A+B→C+D
-rA=kCACB2
Complete segregation model by Polymath
Segregation model by Polymath:

## Slide 34
t min | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 12 | 14
C g/m3 | 0 | 1 | 5 | 8 | 10 | 8 | 6 | 4 | 3 | 2.2 | 1.5 | 0.6 | 0
E(t) | 0 | 0.02 | 0.1 | 0.16 | 0.2 | 0.16 | 0.12 | 0.08 | 0.06 | 0.044 | 0.03 | 0.012 | 0
Maximum mixedness model:
l=time
Polymath cannot solve because l→0 (needs to increase)
Substitute l for z, where z=T̅-l where T̅=longest time interval (14 min)
E must be in terms of T̅-z. Since T̅-z=l & l=t, simply substitute l for t
E(l)= 0.0889237*l-0.0157181*l2 + 0.0007926*l3 – 8.63E-6*l4
F(l) is a cumulative distribution function
For a pulse tracer expt, the effluent concentration C(t) & RTD function E(t) are given
in the table below. The irreversible, liquid-phase, nonelementary rxn A+B→C+D, -rA=kCACB2 will be carried out isothermally at 320K in this reactor. Calculate the conversion for an ideal PFR, the complete segregation model and maximum mixedness model. CA0=CB0=0.0313 mol/L & k=176 L2/mol2·min at 320K

## Slide 35
Maximum Mixedness Model, nonelementary reaction A+B→C+D
-rA=kCACB2
Eq for E describes RTD function only on interval t= 0 to 14 minutes, otherwise E=0
Denominator cannot = 0
XA, maximum mixedness = 0.347

## Slide 36
t min | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 12 | 14
C g/m3 | 0 | 1 | 5 | 8 | 10 | 8 | 6 | 4 | 3 | 2.2 | 1.5 | 0.6 | 0
E(t) | 0 | 0.02 | 0.1 | 0.16 | 0.2 | 0.16 | 0.12 | 0.08 | 0.06 | 0.044 | 0.03 | 0.012 | 0
For a pulse tracer expt, C(t) & E(t) are given in the table below. The irreversible, liquid-phase, nonelementary rxn A+B→C+D, -rA=kCACB2 will be carried out in this reactor. Calculate the conversion for the complete segregation model under adiabatic conditions with T0= 288K, CA0=CB0=0.0313 mol/L, k=176 L2/mol2·min at 320K, DH°RX=-40000 cal/mol, E/R =3600K, CPA=CPB=20cal/mol·K & CPC=CPD=30 cal/mol·K
Polymath eqs for segregation model:
E(t)= 0.0889237*t -0.0157181*t2 + 0.0007926*t3 – 8.63E-6*t4
Express k as function of T:
Need equations from energy balance. For adiabatic operation:

## Slide 37
t min | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 12 | 14
C g/m3 | 0 | 1 | 5 | 8 | 10 | 8 | 6 | 4 | 3 | 2.2 | 1.5 | 0.6 | 0
E(t) | 0 | 0.02 | 0.1 | 0.16 | 0.2 | 0.16 | 0.12 | 0.08 | 0.06 | 0.044 | 0.03 | 0.012 | 0
For a pulse tracer expt, C(t) & E(t) are given in the table below. The irreversible, liquid-phase, nonelementary rxn A+B→C+D, -rA=kCACB2 will be carried out in this reactor. Calculate the conversion for the complete segregation model under adiabatic conditions with T0= 288K, CA0=CB0=0.0313 mol/L, k=176 L2/mol2·min at 320K, DH°RX=-40000 cal/mol, E/R =3600K, CPA=CPB=20cal/mol·K & CPC=CPD=30 cal/mol·K
Energy balance for adiabatic operation:
E(t)= 0.0889237*t -0.0157181*t2 + 0.0007926*t3 – 8.63E-6*t4
Not zero!

## Slide 38
Segregation model, adiabatic operation, nonelementary reaction kinetics
A+B→C+D
-rA=kCACB2

## Slide 39
The following slides show how the same problem would be solved and the solutions would differ if the reaction rate was still -rA=kCACB2 but the reaction was instead elementary: A+2B→C+D
These slides may be provided as an extra example problem that the students may study on there own if time does not permit doing it in class.

## Slide 40
t min | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 12 | 14
C g/m3 | 0 | 1 | 5 | 8 | 10 | 8 | 6 | 4 | 3 | 2.2 | 1.5 | 0.6 | 0
E(t) | 0 | 0.02 | 0.1 | 0.16 | 0.2 | 0.16 | 0.12 | 0.08 | 0.06 | 0.044 | 0.03 | 0.012 | 0
Start with PFR design eq & see how far can we get:
For a pulse tracer expt, the effluent concentration C(t) & RTD function E(t) are given
in the table below. The irreversible, liquid-phase, elementary rxn A+2B→C+D, -rA=kCACB2 will be carried out isothermally at 320K in this reactor. Calculate the conversion for an ideal PFR, the complete segregation model and maximum mixedness model. CA0=CB0=0.0313 mol/L & k=176 L2/mol2·min at 320K
Could solve with Polymath if we knew the value of t
CB0 = 0.0313
k = 0.0313

## Slide 41
t min | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 12 | 14
C g/m3 | 0 | 1 | 5 | 8 | 10 | 8 | 6 | 4 | 3 | 2.2 | 1.5 | 0.6 | 0
E(t) | 0 | 0.02 | 0.1 | 0.16 | 0.2 | 0.16 | 0.12 | 0.08 | 0.06 | 0.044 | 0.03 | 0.012 | 0
For a pulse tracer expt, the effluent concentration C(t) & RTD function E(t) are given
in the table below. The irreversible, liquid-phase, elementary rxn A+2B→C+D, -rA=kCACB2 will be carried out isothermally at 320K in this reactor. Calculate the conversion for an ideal PFR, the complete segregation model and maximum mixedness model. CA0=CB0=0.0313 mol/L & k=176 L2/mol2·min at 320K
How do we determine t?
For an ideal reactor, t = tm
Use numerical method to determine tm:
t min | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 12 | 14
C g/m3 | 0 | 1 | 5 | 8 | 10 | 8 | 6 | 4 | 3 | 2.2 | 1.5 | 0.6 | 0
E(t) | 0 | 0.02 | 0.1 | 0.16 | 0.2 | 0.16 | 0.12 | 0.08 | 0.06 | 0.044 | 0.03 | 0.012 | 0
t*E(t) | 0 | 0.02 | 0.2 | 0.48 | 0.8 | 0.8 | 0.72 | 0.56 | 0.48 | 0.396 | 0.3 | 0.144 | 0

## Slide 42
t min | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 12 | 14
C g/m3 | 0 | 1 | 5 | 8 | 10 | 8 | 6 | 4 | 3 | 2.2 | 1.5 | 0.6 | 0
E(t) | 0 | 0.02 | 0.1 | 0.16 | 0.2 | 0.16 | 0.12 | 0.08 | 0.06 | 0.044 | 0.03 | 0.012 | 0
For a pulse tracer expt, the effluent concentration C(t) & RTD function E(t) are given
in the table below. The irreversible, liquid-phase, elementary rxn A+2B→C+D, -rA=kCACB2 will be carried out isothermally at 320K in this reactor. Calculate the conversion for an ideal PFR, the complete segregation model and maximum mixedness model. CA0=CB0=0.0313 mol/L & k=176 L2/mol2·min at 320K
t min | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 12 | 14
C g/m3 | 0 | 1 | 5 | 8 | 10 | 8 | 6 | 4 | 3 | 2.2 | 1.5 | 0.6 | 0
E(t) | 0 | 0.02 | 0.1 | 0.16 | 0.2 | 0.16 | 0.12 | 0.08 | 0.06 | 0.044 | 0.03 | 0.012 | 0
t*E(t) | 0 | 0.02 | 0.2 | 0.48 | 0.8 | 0.8 | 0.72 | 0.56 | 0.48 | 0.396 | 0.3 | 0.144 | 0
For an ideal reactor, t = tm
Final XA corresponds to t=5.15 min

## Slide 43
t min | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 12 | 14
C g/m3 | 0 | 1 | 5 | 8 | 10 | 8 | 6 | 4 | 3 | 2.2 | 1.5 | 0.6 | 0
E(t) | 0 | 0.02 | 0.1 | 0.16 | 0.2 | 0.16 | 0.12 | 0.08 | 0.06 | 0.044 | 0.03 | 0.012 | 0
XA(t) is from batch reactor design eq
Batch reactor design eq:
Stoichiometry:
For a pulse tracer expt, the effluent concentration C(t) & RTD function E(t) are given
in the table below. The irreversible, liquid-phase, elementary rxn A+2B→C+D, -rA=kCACB2 will be carried out isothermally at 320K in this reactor. Calculate the conversion for an ideal PFR, the complete segregation model and maximum mixedness model. CA0=CB0=0.0313 mol/L & k=176 L2/mol2·min at 320K
CB0=0.0313
k=176
Best-fit polynomial line for E(t) vs t calculated by Polymath (slide 19)
Segregation model with Polymath:
E(t)= 0.0889237*t -0.0157181*t2 + 0.0007926*t3 – 8.63E-6*t4

## Slide 44
Segregation model, isothermal operation, elementary rxn: A+2B→C+D

## Slide 45
t min | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 12 | 14
C g/m3 | 0 | 1 | 5 | 8 | 10 | 8 | 6 | 4 | 3 | 2.2 | 1.5 | 0.6 | 0
E(t) | 0 | 0.02 | 0.1 | 0.16 | 0.2 | 0.16 | 0.12 | 0.08 | 0.06 | 0.044 | 0.03 | 0.012 | 0
Maximum mixedness model:
For a pulse tracer expt, the effluent concentration C(t) & RTD function E(t) are given
in the table below. The irreversible, liquid-phase, elementary rxn A+2B→C+D, -rA=kCACB2 will be carried out isothermally at 320K in this reactor. Calculate the conversion for an ideal PFR, the complete segregation model and maximum mixedness model. CA0=CB0=0.0313 mol/L & k=176 L2/mol2·min at 320K
l=time
Polymath cannot solve because l→0 (must increase)
Substitute l for z, where z=T̅-l where T̅=longest time interval (14 min)
E must be in terms of T̅-z. Since T̅-z=l & l=t, simply substitute l for t
E(l)= 0.0889237*l-0.0157181*l2 + 0.0007926*l3 – 8.63E-6*l4

## Slide 46
Maximum Mixedness Model, elementary reaction A+2B→C+D, -rA=kCACB2
Eq for E describes RTD function only on interval t= 0 to 14 minutes, otherwise E=0
Denominator cannot = 0
XA, maximum mixedness = 0.25

## Slide 47
t min | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 12 | 14
C g/m3 | 0 | 1 | 5 | 8 | 10 | 8 | 6 | 4 | 3 | 2.2 | 1.5 | 0.6 | 0
E(t) | 0 | 0.02 | 0.1 | 0.16 | 0.2 | 0.16 | 0.12 | 0.08 | 0.06 | 0.044 | 0.03 | 0.012 | 0
For a pulse tracer expt, C(t) & E(t) are given in the table below. The irreversible, liquid-phase, elementary rxn A+2B→C+D, -rA=kCACB2 will be carried out in this reactor. Calculate the conversion for the complete segregation model under adiabatic conditions with T0= 288K, CA0=CB0=0.0313 mol/L, k=176 L2/mol2·min at 320K, DH°RX=-40000 cal/mol, E/R =3600K, CPA=CPB=20cal/mol·K & CPC=CPD=30 cal/mol·K
Polymath eqs for segregation model:
E(t)= 0.0889237*t -0.0157181*t2 + 0.0007926*t3 – 8.63E-6*t4
Express k as function of T:
Need equations from energy balance. For adiabatic operation:

## Slide 48
t min | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 12 | 14
C g/m3 | 0 | 1 | 5 | 8 | 10 | 8 | 6 | 4 | 3 | 2.2 | 1.5 | 0.6 | 0
E(t) | 0 | 0.02 | 0.1 | 0.16 | 0.2 | 0.16 | 0.12 | 0.08 | 0.06 | 0.044 | 0.03 | 0.012 | 0
For a pulse tracer expt, C(t) & E(t) are given in the table below. The irreversible, liquid-phase, elementary rxn A+2B→C+D, -rA=kCACB2 will be carried out in this reactor. Calculate the conversion for the complete segregation model under adiabatic conditions with T0= 288K, CA0=CB0=0.0313 mol/L, k=176 L2/mol2·min at 320K, DH°RX=-40000 cal/mol, E/R =3600K, CPA=CPB=20cal/mol·K & CPC=CPD=30 cal/mol·K
Adiabatic EB:
E(t)= 0.0889237*t -0.0157181*t2 + 0.0007926*t3 – 8.63E-6*t4

## Slide 49
Segregation model, adiabatic operation, elementary reaction kinetics
A+2B→C+D
-rA=kCACB2
X̅A = 0.50
Why so much lower than before?
Because B is completely consumed by XA=0.5