## Slide 1: Review: Nonisothermal Reactor Design
Steady–state total energy balance (TEB):
For a SS nonisotherm flow reactor:
“Simplified” TEB:
Constant (average) heat capacities :
Can rearrange this equation to solve for T
T = reaction temp Ti0 = initial (feed) temperature TR= reference temp

## Slide 2: Review: Solve TEB for Conversion
Solve for XA:
Plug in Q for the specific type of reactor
T = reaction temp Ti0 = initial (feed) temperature TR= reference temp
For an adiabatic reaction (Q=0) and shaft work can be neglected (ẆS=0)

## Slide 3: Review: Application to CSTR
Solve TEB for T at the exit (Texit = Tinside reactor)
Calculate k = Ae-E/RT where T was calculated in step a
Plug the k calculated in step b into the design equation to calculate VCSTR
Case 1: Given FA0, CA0, A, E, Cpi, H°I, and XA, calculate T & V
Solve TEB for T as a function of XA (make a table of T vs XA using EB)
Solve CSTR design equation for XA as a function of T (plug in k = Ae-E/RT ) (use design eq to make a table of XA vs T)
Plot XA,EB vs T & XA,MB vs T on the same graph. The intersection of these 2 lines is the conditions (T and XA) that satisfies the energy & mass balance
Case 2: Given FA0, CA0, A, E, Cpi, H°I, and V, calculate T & XA
XA,EB = conversion determined from the TEB equation
XA,MB = conversion determined using the design equation
XA
T
XA,EB
XA,MB
XA,exit
Texit
Intersection is T and XA that satisfies both equations

## Slide 4: Review: Application to a SS PFR
PFR
FA0
FA
distance
T
XA
Negligible shaft work (ẆS=0) and adiabatic (Q=0)
Use TEB to construct a table of T as a function of XA
Use k = Ae-E/RT to obtain k as a function of XA
Use stoichiometry to obtain –rA as a function of XA
Calculate:
May use numerical methods

## Slide 5: L13: Equilibrium Conversion in Nonisothermal Reactor Design
The highest conversion that can be achieved in reversible reactions is the equilibrium conversion
  For reversible reactions, the equilibrium conversion is usually calculated first
The equilibrium conversion increases with increasing temperature for endothermic reactions
The equilibrium conversion decreases with increasing temperature for exothermic reactions

## Slide 6: Review of Equilibrium Kinetics
KC: equilibrium constant (capital K):
Gas-phase reaction:
If KC is given at a single temperature T2, & DCP can be neglected then:
KP: equilibrium constant in terms of partial pressures Pi:
For ideal gases, KP = KC(RT)Δn where
Temp dependence of KP is given by van’t Hoff’s equation:
If DCP can be neglected then:

## Slide 7: Equilibrium Conversion XAe
T
XA,e
0
1
exothermic
endothermic
Example) A⇌B CA0=1 CB0=0
Rearrange to solve in terms of XAe
This equation enables us to express Xae as a function of T

## Slide 8: XAe and Temperature
Substitute for KC:
Divide numerator & denominator by KC
Changed sign

## Slide 9: XAe and Temperature
Makes sense from Le Chatelier’s principle
Exothermic rxn produces heat→
increasing temp adds heat (product) & pushes rxn to left (lower conversion)
Makes sense from Le Chatelier’s principle
Heat is a reactant in an endothermic rxn→
increasing temp adds reactant (heat) & pushes rxn to right (higher conversion)

## Slide 10: Adiabatic Equilibrium T Example
For the elementary solid-catalyzed liquid-phase reaction
Make a plot of equilibrium conversion as a function of temperature.
Determine the adiabatic equilibrium temperature and conversion when pure A is fed to the reactor at a temperature of 298 K.

## Slide 11
Rate law:
equilibrium
-rA = 0
The Van’t Hoff equation:
Xe = f (T)
Xe only depends on thermodynamics!
Nothing to do with the energy balance!

## Slide 12
Reaction is carried out adiabatically with an inlet temp of 298 K, CPA = 50 cal/mol∙K, & the heat of reaction = 20,000 cal/mol. The energy balance is:
From thermodynamics
X
T
From energy balance
0
0
How to increase the conversion?

## Slide 13
Does increasing the entering temperature increase XA?
XAe
XA
T (K)
XA,EB for adiabatic operation (slants up for exothermic rxn)
Equilibrium curve
for exothermic rxn
Higher T moves XA,EB curve to the right
Adiabatic op, XA,EB at Ti0,2
XA,e (Tadiabatic) decreases for an exothermic reaction
XA,e at Ti0,1
XA,e at Ti0,2

## Slide 14: Optimum Feed Temperature
For a reversible and exothermic reaction, the feed temperature should be optimized to maximize the conversion
From thermodynamics
XEB
T
600
500
350
0.15
0.33
0.75
XA
W
T0 = 600
T0 = 500
T0 = 350
There is an optimum inlet temperature!
High T0: reaction reaches equilibrium fast, but XA is low
Low T0 would give high XA,e but the specific reaction rate k is so small that most of the reactant passes through the reactor without reacting (never reach XA,e)

## Slide 15: How does one increase XA for adiabatic operation of an exothermic reaction?
with interstage cooling!
XEB
T
final conversion
XA,EB1
cooling process
XA,EB2
XA,EB3
XA,EB4
T0
Reactor 4
Reactor 1
Cooling, C1
C2
C3
Reactor 3
Reactor 2
Each reactor operates adiabatically
Endothermic reactions are similar, but with heating instead of cooling

## Slide 16: Endothermic Reactions
The equilibrium conversion increases with increasing temperature, so use interstage heating to increase the conversion
XEB
T
heating process
final conversion
Red lines are from the energy balance, slant backwards because DH°RX >0 for endothermic reaction

## Slide 17
Suppose pure A enters a reactor at 298K . What is the maximum XA achievable in an adiabatic reactor? Assume ẆS=0, and DCP = 0, CP.A=60 J/molK, DH°RX(TR)= 20,000 J/mol, KC=10 exp[2405T-7.2]
Solve TEB for XA:
0
0
Plot XEB vs T and XA,e vs T to compute the maximum XA graphically

## Slide 18
Suppose pure A enters a reactor at 298K . What is the maximum XA achievable in an adiabatic reactor? Assume ẆS=0, and DCP = 0, CP.A=60 J/molK, DH°RX(TR)= 20,000 J/mol, KC=10 exp[2405T-7.2]
T | XA,EB
200 | 0.294
250 | 0.144
298 | 0
325 | -0.081
350 | -0.156
375 | -0.231
400 | -0.306
425 | -0.381
450 | -0.456
500 | -0.606
550 | -0.756
600 | -0.906
T | XAe
200 | 0.000149
250 | 0.001634
298 | 0.007612
325 | 0.014746
350 | 0.024722
375 | 0.038481
400 | 0.056318
425 | 0.078262
450 | 0.10407
500 | 0.165203
550 | 0.234315
600 | 0.305584

## Slide 19
Chart: T (K)
| 200 | 250 | 298 | 325 | 350 | 375 | 400 | 425 | 450 | 500 | 550 | 600
Energy balance conversion | 0.294 | 0.144 | 0 | -0.081 | -0.156 | -0.231 | -0.306 | -0.381 | -0.456 | -0.606 | -0.756 | -0.906
Equilibrium conversion | 0.00014883 | 0.0016341 | 0.0076124 | 0.014746 | 0.024722 | 0.038481 | 0.056318 | 0.078262 | 0.10407 | 0.1652 | 0.23431 | 0.30558
Suppose pure A enters a reactor at 298K . What is the maximum XA achievable in an adiabatic reactor? Assume ẆS=0, and DCP = 0, CP.A=60 J/molK, DH°RX(TR)= 20,000 J/mol (endothermic), KC=10 exp[2504T-7.2]
XAe
EB for adiabatic operation,
(slants down for endothermic rxn)
Tadiabatic
Nearly 0 conversion, not good!
Tadiabatic: Outlet T if reactor had an infinite volume
XA,e at Tadiabatic is max achievable XA in adiabatic reactor

## Slide 20
Chart: T (K)
| 200 | 250 | 298 | 325 | 350 | 375 | 400 | 425 | 450 | 500 | 550 | 600
Energy balance conversion | 0.294 | 0.144 | 0 | -0.081 | -0.156 | -0.231 | -0.306 | -0.381 | -0.456 | -0.606 | -0.756 | -0.906
Equilibrium conversion | 0.00014883 | 0.0016341 | 0.0076124 | 0.014746 | 0.024722 | 0.038481 | 0.056318 | 0.078262 | 0.10407 | 0.1652 | 0.23431 | 0.30558
Does increasing the inlet temperature to 600K improve the conversion of this reaction? ẆS=0, and DCP = 0, CP.A=60 J/molK, DH°RX(TR)= 20,000 J/mol (endothermic), & KC=10 exp[2504T-7.2]
XAe
Tadiabatic: Outlet T if reactor had an infinite volume
EB for adiabatic operation (endothermic) T0=298K
Tadiabatic
XA,e at Tadiabatic is max achievable XA in adiabatic reactor
Nearly 0 conversion

## Slide 21
Chart: T (K)
| 200 | 250 | 298 | 325 | 350 | 375 | 400 | 425 | 450 | 500 | 550 | 600
Energy balance conversion T0=298 | 0.294 | 0.144 | 0 | -0.081 | -0.156 | -0.231 | -0.306 | -0.381 | -0.456 | -0.606 | -0.756 | -0.906
Equilibrium conversion | 0.00014883 | 0.0016341 | 0.0076124 | 0.014746 | 0.024722 | 0.038481 | 0.056318 | 0.078262 | 0.10407 | 0.1652 | 0.23431 | 0.30558
Energy balance conversion, T0=600K | 1.2 | 1.05 | 0.906 | 0.825 | 0.75 | 0.675 | 0.6 | 0.525 | 0.45 | 0.3 | 0.15 | 0
Does increasing the inlet temperature to 600K improve the conversion of this reaction? ẆS=0, and DCP = 0, CP.A=60 J/molK, DH°RX(TR)= 20,000 J/mol (endothermic), & KC=10 exp[2504T-7.2]
XAe ≈ 0
at T0 = 298K
EB for adiabatic operation (endothermic) T0=298K
Tadiabatic
EB for adiabatic operation T0=600K
XAe ≈ 0.2 when T0 = 600K
Tadiabatic
(T0=600K)
Yes, higher conversion is achieved