## Slide 1: L15: Nonisothermal Reactor Example Problems

## Slide 2: Review: Multiple Steady States in CSTR
Plot of XA,EB vs T and XA,MB vs T
Intersections are the T and XA that satisfy both mass balance (MB) & energy balance (EB) equations
Each intersection is a steady state (temperature & conversion)
Multiple sets of conditions are possible for the same reaction in the same reactor with the same inlet conditions!
Chart: T (K)
| 50 | 100 | 125 | 150 | 175 | 200 | 225 | 250 | 275 | 298 | 325 | 350 | 375 | 400 | 425 | 450 | 500 | 550 | 600
EB conversion | -1.235 | -0.91 | -0.7475 | -0.585 | -0.4225 | -0.26 | -0.0975 | 0.065 | 0.2275 | 0.377 | 0.5525 | 0.715 | 0.8775 | 1.04 | 1.2025 | 1.365 | 1.69 | 2.015 | 2.34
Equilibrium conversion | 5.9222e-30 | 1.5069e-12 | 4.5627e-09 | 9.5492e-07 | 4.3414e-05 | 0.00075958 | 0.0069957 | 0.040148 | 0.15228 | 0.35618 | 0.62839 | 0.80316 | 0.89748 | 0.94467 | 0.96853 | 0.98112 | 0.99217 | 0.9962 | 0.99793
XA,MB

## Slide 3: Review: Heat Removal Term R(T) & T0
T
R(T)
Increase T0
T
R(T)
Increase 
T0
Ta
 = 0
 = ∞
For Ta < T0
Heat removed: R(T)
Heat generated G(T)
When T0 increases, slope stays same & line shifts to right
R(T) line has slope of CP0(1+k)
When k increases from lowering FA0 or increasing heat exchange, slope and x-intercept moves
Ta<T0: x-intercept shifts left as k↑
Ta>T0: x-intercept shifts right as k↑
k=0, then TC=T0
k=∞, then TC=Ta

## Slide 4: Review: CSTR Stability
Chart: T
1
2
3
R(T) > G(T) → T falls to T=SS1
G(T) > R(T) → T rises to T=SS3
G(T) > R(T) → T rises to T=SS1
R(T) > G(T)
→T falls to T=SS3
Magnitude of G(T) to R(T) curve determines if reactor T will rise or fall
G(T) = R(T) intersection, equal rate of heat generation & removal, no change in T
G(T) > R(T) (G(T) line above R(T) on graph): rate of heat generation > heat removal, so reactor heats up until a steady state is reached
R(T) > G(T) (R(T) line above G(T) on graph): rate of heat generation < heat removal, so reactor cools off until a steady state is reached
Heat generated G(T)
Heat removed: R(T)

## Slide 5
The elementary irreversible reaction A + B →C is carried out adiabatically in a flow reactor with ẆS=0. An equal molar feed of A & B enters at 300K with u0 = 2 dm3/s and CA0 = 0.1 mol/dm3. What is the PFR & CSTR volume required to achieve XA=0.85?
Extra info: liquid phase rxn CpA=CpB=15 cal/mol•K CpC= 30 cal/mol E = 10,000 cal/mol
DHA°(273K)= -20 kcal/mol DHB°(273K)= -15 kcal/mol DHC°(273K)= -41 kcal/mol
Mole balance
Rate Law
Stoichiometry
Combine rate law & stoichiometry
Energy balance
Solve
Strategy:
6a. Solve CSTR
Use EB to find T as a function of XA
Calculate V using the CSTR design eq with k calculated at that T
6b. Solve PFR
Use EB to construct table of T as a function of XA
Use k = Ae-E/RT to construct table of k as function of T & therefore XA
Calculate -rA as a function of T & XA
Calculate FA0/-rA for each T
Use numeric technique to calculate V

## Slide 6
The elementary irreversible reaction A + B →C is carried out adiabatically in a flow reactor with ẆS=0. An equal molar feed of A & B enters at 300K with u0 = 2 dm3/s and CA0 = 0.1 mol/dm3. What is the PFR & CSTR volume required to achieve XA=0.85?
Mole balance
CSTR
PFR
Rate law
Extra info: CpA=CpB=15 cal/mol•K CpC= 30 cal/mol E = 10,000 cal/mol
DHA°(273K)= -20 kcal/mol DHB°(273K)= -15 kcal/mol DHC°(273K)= -41 kcal/mol
Stoichiometry
Combine:

## Slide 7
The elementary irreversible reaction A + B →C is carried out adiabatically in a flow reactor with ẆS=0. An equal molar feed of A & B enters at 300K with u0 = 2 dm3/s and CA0 = 0.1 mol/dm3. What is the PFR & CSTR volume required to achieve XA=0.85?
Combine MB, rate law & stoichiometry for CSTR:
CSTR
Extra info: CpA=CpB=15 cal/mol•K CpC= 30 cal/mol E = 10,000 cal/mol
DHA°(273K)= -20 kcal/mol DHB°(273K)= -15 kcal/mol DHC°(273K)= -41 kcal/mol

## Slide 8
The elementary irreversible reaction A + B →C is carried out adiabatically in a flow reactor with ẆS=0. An equal molar feed of A & B enters at 300K with u0 = 2 dm3/s and CA0 = 0.1 mol/dm3. What is the PFR & CSTR volume required to achieve XA=0.85?
Energy balance
Extra info: CpA=CpB=15 cal/mol•K CpC= 30 cal/mol E = 10,000 cal/mol
DHA°(273K)= -20 kcal/mol DHB°(273K)= -15 kcal/mol DHC°(273K)= -41 kcal/mol
0
0
Solve for T:
Substitute:
Multiply out quantities in brackets, bring T to 1 side of equation, factor out T, divide by quantity in bracket:
Evaluate DCp:

## Slide 9
The elementary irreversible reaction A + B →C is carried out adiabatically in a flow reactor with ẆS=0. An equal molar feed of A & B enters at 300K with u0 = 2 dm3/s and CA0 = 0.1 mol/dm3. What is the PFR & CSTR volume required to achieve XA=0.85?
Energy balance
Extra info: CpA=CpB=15 cal/mol•K CpC= 30 cal/mol E = 10,000 cal/mol
DHA°(273K)= -20 kcal/mol DHB°(273K)= -15 kcal/mol DHC°(273K)= -41 kcal/mol
Evaluate SQiCp:
Evaluate DH°RX(TR):
Simplify EB:

## Slide 10
The elementary irreversible reaction A + B →C is carried out adiabatically in a flow reactor with ẆS=0. An equal molar feed of A & B enters at 300K with u0 = 2 dm3/s and CA0 = 0.1 mol/dm3. What is the PFR & CSTR volume required to achieve XA=0.85?
Solve for CSTR volume: use EB to find T when XA=0.85
Extra info: CpA=CpB=15 cal/mol•K CpC= 30 cal/mol E = 10,000 cal/mol
DHA°(273K)= -20 kcal/mol DHB°(273K)= -15 kcal/mol DHC°(273K)= -41 kcal/mol

## Slide 11
XA | T (K) | k (dm3/mol·s) | -rA (mol/dm3·s) | FA0/-rA (dm3)
0 |  |  |  | 
0.2 |  |  |  | 
0.4 |  |  |  | 
0.6 |  |  |  | 
0.8 |  |  |  | 
0.85 |  |  |  | 
The elementary irreversible reaction A + B →C is carried out adiabatically in a flow reactor with ẆS=0. An equal molar feed of A & B enters at 300K with u0 = 2 dm3/s and CA0 = 0.1 mol/dm3. What is the PFR & CSTR volume required to achieve XA=0.85?
Solve for PFR:
Use EB to construct table of T as a function of XA (We’re interested in range where XA = 0 to XA = 0.85)
300

## Slide 12
XA | T (K) | k (dm3/mol·s) | -rA (mol/dm3·s) | FA0/-rA (dm3)
0 | 300 |  |  | 
0.2 | 340 |  |  | 
0.4 | 380 |  |  | 
0.6 | 420 |  |  | 
0.8 | 460 |  |  | 
0.85 | 470 |  |  | 
The elementary irreversible reaction A + B →C is carried out adiabatically in a flow reactor with ẆS=0. An equal molar feed of A & B enters at 300K with u0 2 dm3/s and CA0 = 0.1 mol/dm3. What is the PFR & CSTR volume required to achieve XA=0.85?
Solve for PFR:
Use EB to construct table of T as a function of XA -Temperature range should cover XA = 0 to XA = 0.85
Calculate k(T) for each T in the table

## Slide 13
The elementary irreversible reaction A + B →C is carried out adiabatically in a flow reactor with ẆS=0. An equal molar feed of A & B enters at 300K with u0 = 2 dm3/s and CA0 = 0.1 mol/dm3. What is the PFR & CSTR volume required to achieve XA=0.85?
Solve for PFR:
Use EB to construct table of T as a function of XA -Temperature range should cover XA = 0 to XA = 0.85
Calculate k(T) for each T in the table
XA | T (K) | k (dm3/mol·s) | -rA (mol/dm3·s) | FA0/-rA (dm3)
0 | 300 | 0.01 |  | 
0.2 | 340 | 0.072 |  | 
0.4 | 380 | 0.34 |  | 
0.6 | 420 | 1.21 |  | 
0.8 | 460 | 3.42 |  | 
0.85 | 470 | 4.31 |  | 

## Slide 14
The elementary irreversible reaction A + B →C is carried out adiabatically in a flow reactor with ẆS=0. An equal molar feed of A & B enters at 300K with u0 = 2 dm3/s and CA0 = 0.1 mol/dm3. What is the PFR & CSTR volume required to achieve XA=0.85?
Solve for PFR:
Use EB to construct table of T as a function of XA -Temperature range should cover XA = 0 to XA = 0.85
XA | T (K) | k (dm3/mol·s) | -rA (mol/dm3·s) | FA0/-rA (dm3)
0 | 300 | 0.01 |  | 
0.2 | 340 | 0.072 |  | 
0.4 | 380 | 0.34 |  | 
0.6 | 420 | 1.21 |  | 
0.8 | 460 | 3.42 |  | 
0.85 | 470 | 4.31 |  | 
Calculate –rA each XA and k in the table
Calculate k(T)

## Slide 15
The elementary irreversible reaction A + B →C is carried out adiabatically in a flow reactor with ẆS=0. An equal molar feed of A & B enters at 300K with u0 = 2 dm3/s and CA0 = 0.1 mol/dm3. What is the PFR & CSTR volume required to achieve XA=0.85?
Solve for PFR:
Use EB to construct table of T as a function of XA -Temperature range should cover XA = 0 to XA = 0.85
XA | T (K) | k (dm3/mol·s) | -rA (mol/dm3·s) | FA0/-rA (dm3)
0 | 300 | 0.01 | 0.0001 | 
0.2 | 340 | 0.072 | 0.00046 | 
0.4 | 380 | 0.34 | 0.00122 | 
0.6 | 420 | 1.21 | 0.00194 | 
0.8 | 460 | 3.42 | 0.0014 | 
0.85 | 470 | 4.31 | 0.00097 | 
Calculate k(T)
Calculate –rA each XA and k in the table

## Slide 16
The elementary irreversible reaction A + B →C is carried out adiabatically in a flow reactor with ẆS=0. An equal molar feed of A & B enters at 300K with u0 2 dm3/s and CA0 = 0.1 mol/dm3. What is the PFR & CSTR volume required to achieve XA=0.85?
Solve for PFR:
Use EB to construct table of T as a function of XA -Temperature range should cover XA = 0 to XA = 0.85
XA | T (K) | k (dm3/mol·s) | -rA (mol/dm3·s) | FA0/-rA (dm3)
0 | 300 | 0.01 | 0.0001 | 
0.2 | 340 | 0.072 | 0.00046 | 
0.4 | 380 | 0.34 | 0.00122 | 
0.6 | 420 | 1.21 | 0.00194 | 
0.8 | 460 | 3.42 | 0.0014 | 
0.85 | 470 | 4.31 | 0.00097 | 
Calculate k(T)
Calculate FA0/–rA for each XA in the table
Calculate –rA each XA and k in the table

## Slide 17
The elementary irreversible reaction A + B →C is carried out adiabatically in a flow reactor with ẆS=0. An equal molar feed of A & B enters at 300K with u0 = 2 dm3/s and CA0 = 0.1 mol/dm3. What is the PFR & CSTR volume required to achieve XA=0.85?
Solve for PFR:
Use EB to construct table of T as a function of XA -Temperature range should cover XA = 0 to XA = 0.85
XA | T (K) | k (dm3/mol·s) | -rA (mol/dm3·s) | FA0/-rA (dm3)
0 | 300 | 0.01 | 0.0001 | 2000
0.2 | 340 | 0.072 | 0.00046 | 434.8
0.4 | 380 | 0.34 | 0.00122 | 163.9
0.6 | 420 | 1.21 | 0.00194 | 103.1
0.8 | 460 | 3.42 | 0.0014 | 142.9
0.85 | 470 | 4.31 | 0.00097 | 206.2
Calculate k(T)
Calculate FA0/–rA for each XA in the table
Calculate –rA each XA and k in the table

## Slide 18
The elementary irreversible reaction A + B →C is carried out adiabatically in a flow reactor with ẆS=0. An equal molar feed of A & B enters at 300K with u0 = 2 dm3/s and CA0 = 0.1 mol/dm3. What is the PFR & CSTR volume required to achieve XA=0.85?
Solve for PFR:
XA | T (K) | k (dm3/mol·s) | -rA (mol/dm3·s) | FA0/-rA (dm3)
0 | 300 | 0.01 | 0.0001 | 2000
0.2 | 340 | 0.072 | 0.00046 | 434.8
0.4 | 380 | 0.34 | 0.00122 | 163.9
0.6 | 420 | 1.21 | 0.00194 | 103.1
0.8 | 460 | 3.42 | 0.00137 | 146
0.85 | 470 | 4.31 | 0.00097 | 206.2
Numeric evaluation by parts: 5-point rule for XA interval 0 to 0.8, 2-point rule for XA interval from 0.8 to 0.85:

## Slide 19
For these conditions, what is the max T0 that would keep T≤ 550K at complete conversion?
T≤ 550K at complete conversion, XA=1:
Max T0 is 350K

## Slide 20
The first order irreversible reaction A(l) → B(l) is carried out in a jacketed CSTR. The feed contains A and an inert liquid in equimolar amounts, where FA0 = 80 mol/min. What is the reactor temp when the inlet temp T0 is 450K?
UA= 8000 cal/min·K Ta= 300K DHRX=-7500 cal/mol CpA = CpB =20 cal/mol·K
Cpi =30 cal/mol·K t=100 min E=40,000 cal/mol k=6.6 x 10-3 min-1 at 350K
Need to find where G(T)=R(T) for T0 = 450K
Put R(T) & G(T) in terms of constants in the problem statement
Plot R(T) vs T and G(T) vs T on the same graph & find where they intersect

## Slide 21
The first order irreversible reaction A(l) → B(l) is carried out in a jacketed CSTR. The feed contains A and an inert liquid in equimolar amounts, where FA0 = 80 mol/min. What is the reactor temp when the inlet temp T0 is 450K?
UA= 8000 cal/min·K Ta= 300K DHRX=-7500 cal/mol CpA = CpB =20 cal/mol·K
Cpi =30 cal/mol·K t=100 min E=40,000 cal/mol k=6.6 x 10-3 min-1 at 350K
Put k in terms of constants from the problem statement:
I = inert
Put R(T) in terms of constants in the problem statement, starting with CP0:
Put TC in terms of constants in the problem statement:

## Slide 22
The first order irreversible reaction A(l) → B(l) is carried out in a jacketed CSTR. The feed contains A and an inert liquid in equimolar amounts, where FA0 = 80 mol/min. What is the reactor temp when the inlet temp T0 is 450K?
UA= 8000 cal/min·K Ta= 300K DHRX=-7500 cal/mol CpA = CpB =20 cal/mol·K
Cpi =30 cal/mol·K t=100 min E=40,000 cal/mol k=6.6 x 10-3 min-1 at 350K
Find steady state temp [G(T)=R(T) ] for T0 = 450K
I = inert
Plug k and Tc into R(T):

## Slide 23
The first order irreversible reaction A(l) → B(l) is carried out in a jacketed CSTR. The feed contains A and an inert liquid in equimolar amounts, where FA0 = 80 mol/min. What is the reactor temp when the inlet temp T0 is 450K?
UA= 8000 cal/min·K Ta= 300K DHRX=-7500 cal/mol CpA = CpB =20 cal/mol·K
Cpi =30 cal/mol·K t=100 min E=40,000 cal/mol k=6.6 x 10-3 min-1 at 350K
Find steady state temp [G(T)=R(T) ] for T0 = 450K
I = inert
Now put G(T) in terms of constants from the problem statement:
Rate law:
Stoichiometry:
Combine:

## Slide 24
The first order irreversible reaction A(l) → B(l) is carried out in a jacketed CSTR. The feed contains A and an inert liquid in equimolar amounts, where FA0 = 80 mol/min. What is the reactor temp when the inlet temp T0 is 450K?
UA= 8000 cal/min·K Ta= 300K DHRX=-7500 cal/mol CpA = CpB =20 cal/mol·K
Cpi =30 cal/mol·K t=100 min E=40,000 cal/mol k=6.6 x 10-3 min-1 at 350K
Find steady state temp [G(T)=R(T) ] for T0 = 450K
I = inert
Plug rate law into G(T) & simplify:

## Slide 25
The first order irreversible reaction A(l) → B(l) is carried out in a jacketed CSTR. The feed contains A and an inert liquid in equimolar amounts, where FA0 = 80 mol/min. What is the reactor temp when the inlet temp T0 is 450K?
UA= 8000 cal/min·K Ta= 300K DHRX=-7500 cal/mol CpA = CpB =20 cal/mol·K
Cpi =30 cal/mol·K t=100 min E=40,000 cal/mol k=6.6 x 10-3 min-1 at 350K
Steady state temp [G(T)=R(T) ] for T0 = 450K
I = inert
Rearrange so can be solved with Polymath nonlinear equation solver:
Use design equation to get XA as an explicit equation:
Explicit equation for Polymath

## Slide 26
Enter in Polymath:
 | Variable | Value | f(x) | Initial Guess
1 | T | 399.9425 | -4.547E-12 | 400. ( 300. < T < 500. )
Calculated values of NLE variables
If you want to see this graphically, click the Graph button above
Select graph

## Slide 27
Format the graph
Create a table, save it as a text file, import into Excel, & make a graph with correct labels

## Slide 28
Plot reactor temperature as a function of feed temperature, with T0 between 350 and 450K
CP0 and k do not depend on T0, but TC does
Do we need to change G(T) or R(T) when T0 changes?
G(T) does not depend on T0
Need to re-run the Polymath program using various T0 between 350 and 450K to find the new steady state reactor temperatures
Enter equations into Polymath so that R(T) varies according to T0, & run program with varied values of T0
Run over and over again, varying T0 from 350 K to 450 K
In Excel, create a table of T vs T0, and make a graph

## Slide 29
T0 (K) | T1 (K) | T2 (K) | T3 (K)
350 | 316.7 |  | 
360 | 320.15 |  | 
370 | 323.6 | 357.16 | 370.3
380 | 327.3 | 353.4 | 375.1
390 | 331.2 | 350.1 | 379.1
400 | 336.3 | 346 | 382.8
410 | 386 |  | 
420 | 389.8 |  | 
430 | 393.2 |  | 
440 | 396.6 |  | 
450 | 399.9 |  | 
Chart: T0
| 350 | 360 | 370 | 380 | 390 | 400 | 410 | 420 | 430 | 440 | 450
T0 vs T | 316.7 | 320.15 | 323.6 | 327.3 | 331.2 | 336.3 | 386 | 389.8 | 393.2 | 396.6 | 399.9
 | 357.16 | 353.4 | 350.1 | 346
 | 370.3 | 375.1 | 379.1 | 382.8
Steady state temperature as a function of T0

## Slide 30
The elementary, irreversible reaction A(l) → B(l) is carried out in a jacketed CSTR. The feed contains pure A, & it enters the reactor at 310 K, where FA0 = 60 mol/min and u0 = 300 L/min. Extra info: UA= 3200 cal/min•K Ta= 340 K ∆HRX(TR) = -10,000 cal/mol CpA=15 cal/mol·K CpB=15 cal/mol·K t =120 min E =20,000 cal/mol k(400K) = 1 min-1
What is the value of the heat generated term (with units) when a disturbance causes the temperature in the reactor to drift to 360 K if –rA = 0.0015 mol/L•min at 360K? (The reactor is NOT at the steady state.)

## Slide 31
The elementary, irreversible reaction A(l) → B(l) is carried out in a jacketed CSTR. The feed contains pure A, & it enters the reactor at 310 K, where FA0 = 60 mol/min and u0 = 300 L/min. Extra info: UA= 3200 cal/min•K Ta= 340 K ∆HRX(TR) = -10,000 cal/mol CpA=15 cal/mol·K CpB=15 cal/mol·K t =120 min E =20,000 cal/mol k(400K) = 1 min-1
What is the value of the heat generated term (with units) when a disturbance causes the temperature in the reactor to drift to 360 K if –rA = 0.0015 mol/L•min at 360K? (The reactor is NOT at the steady state.)

## Slide 32
The elementary, irreversible reaction A(l) → B(l) is carried out in a jacketed CSTR. The feed contains pure A, & it enters the reactor at 310 K, where FA0 = 60 mol/min and u0 = 300 L/min. Extra info: UA= 3200 cal/min•K Ta= 340 K ∆HRX(TR) = -10,000 cal/mol CpA=15 cal/mol·K CpB=15 cal/mol·K t =120 min E =20,000 cal/mol k(400K) = 1 min-1
What is the value of the heat generated term (with units) when a disturbance causes the temperature in the reactor to drift to 360 K if –rA = 0.0015 mol/L•min at 360K? (The reactor is NOT at the steady state.)

## Slide 33
The elementary, irreversible reaction A(l) → B(l) is carried out in a jacketed CSTR. The feed contains pure A, & it enters the reactor at 310 K, where FA0 = 60 mol/min and u0 = 300 L/min. Extra info: UA= 3200 cal/min•K Ta= 340 K ∆HRX(TR) = -10,000 cal/mol CpA=15 cal/mol·K CpB=15 cal/mol·K t =120 min E =20,000 cal/mol k(400K) = 1 min-1
What is the value of the heat removal term (with units) when a disturbance causes the temperature in the reactor to drift to 360 K if –rA = 0.0015 mol/L•min at 360K? (The reactor is NOT at the steady state.)

## Slide 34
The elementary, irreversible reaction A(l) → B(l) is carried out in a jacketed CSTR. The feed contains pure A, & it enters the reactor at 310 K, where FA0 = 60 mol/min and u0 = 300 L/min. Extra info: UA= 3200 cal/min•K Ta= 340 K ∆HRX(TR) = -10,000 cal/mol CpA=15 cal/mol·K CpB=15 cal/mol·K t =120 min E =20,000 cal/mol k(400K) = 1 min-1
What is the value of the heat removal term (with units) when a disturbance causes the temperature in the reactor to drift to 360 K if –rA = 0.0015 mol/L•min at 360K? (The reactor is NOT at the steady state.)

## Slide 35
The elementary, irreversible reaction A(l) → B(l) is carried out in a jacketed CSTR. The feed contains pure A, & it enters the reactor at 310 K, where FA0 = 60 mol/min and u0 = 300 L/min. Extra info: UA= 3200 cal/min•K Ta= 340 K ∆HRX(TR) = -10,000 cal/mol CpA=15 cal/mol·K CpB=15 cal/mol·K t =120 min E =20,000 cal/mol k(400K) = 1 min-1
What is the value of the heat removal term (with units) when a disturbance causes the temperature in the reactor to drift to 360 K if –rA = 0.0015 mol/L•min at 360K? (The reactor is NOT at the steady state.)

## Slide 36
The elementary, irreversible reaction A(l) → B(l) is carried out in a jacketed CSTR. The feed contains pure A, & it enters the reactor at 310 K, where FA0 = 60 mol/min and u0 = 300 L/min. Extra info: UA= 3200 cal/min•K Ta= 340 K ∆HRX(TR) = -10,000 cal/mol CpA=15 cal/mol·K CpB=15 cal/mol·K t =120 min E =20,000 cal/mol k(400K) = 1 min-1
When a disturbance causes the temperature in the reactor to drift to 360 K if –rA = 0.0015 mol/L•min at 360K,
Will the reactor temperature heat up, cool down, or stay at 360 K?
G(T) > R(T) so the reactor will heat up