## Slide 1: Review: Multiple Steady States in CSTR
Plot of XA,EB vs T and XA,MB vs T
Intersections are the T and XA that satisfy both mass balance (MB) & energy balance (EB) equations
Each intersection is a steady state (temperature & conversion)
Multiple sets of conditions are possible for the same reaction in the same reactor with the same inlet conditions!
Chart: T (K)
| 50 | 100 | 125 | 150 | 175 | 200 | 225 | 250 | 275 | 298 | 325 | 350 | 375 | 400 | 425 | 450 | 500 | 550 | 600
EB conversion | -1.235 | -0.91 | -0.7475 | -0.585 | -0.4225 | -0.26 | -0.0975 | 0.065 | 0.2275 | 0.377 | 0.5525 | 0.715 | 0.8775 | 1.04 | 1.2025 | 1.365 | 1.69 | 2.015 | 2.34
Equilibrium conversion | 5.9222e-30 | 1.5069e-12 | 4.5627e-09 | 9.5492e-07 | 4.3414e-05 | 0.00075958 | 0.0069957 | 0.040148 | 0.15228 | 0.35618 | 0.62839 | 0.80316 | 0.89748 | 0.94467 | 0.96853 | 0.98112 | 0.99217 | 0.9962 | 0.99793
XA,MB

## Slide 2: Review: Heat Removal Term R(T) & T0
T
R(T)
Increase T0
T
R(T)
Increase 
T0
Ta
 = 0
 = ∞
For Ta < T0
Heat removed: R(T)
Heat generated G(T)
When T0 increases, slope stays same & line shifts to right
R(T) line has slope of CP0(1+k)
When k increases from lowering FA0 or increasing heat exchange, slope and x-intercept moves
Ta<T0: x-intercept shifts left as k↑
Ta>T0: x-intercept shifts right as k↑
k=0, then TC=T0
k=∞, then TC=Ta

## Slide 3: Review: CSTR Stability
Chart: T
1
2
3
R(T) > G(T) → T falls to T=SS1
G(T) > R(T) → T rises to T=SS3
G(T) > R(T) → T rises to T=SS1
R(T) > G(T)
→T falls to T=SS3
Magnitude of G(T) to R(T) curve determines if reactor T will rise or fall
G(T) = R(T) intersection, equal rate of heat generation & removal, no change in T
G(T) > R(T) (G(T) line above R(T) on graph): rate of heat generation > heat removal, so reactor heats up until a steady state is reached
R(T) > G(T) (R(T) line above G(T) on graph): rate of heat generation < heat removal, so reactor cools off until a steady state is reached
Heat generated G(T)
Heat removed: R(T)

## Slide 4: L16: Unsteady State Nonisothermal Reactor Design
An open system (for example, CSTR)
Q
W
Fin
Hin
Fout
Hout
rate of heat flow from surroundings to system
Rate of accumulation of energy in system
=
Rate of work done by system on surroundings
-
+
Rate of energy added to system by mass flow in
-
Rate of energy leaving system by mass flow out
Goal: develop EB for unsteady state reactor

## Slide 5: Change in System Energy with Time
Energy of system is the sum of products of each species specific energy Ei & the moles of each species:
Differentiate wrt time
Total V
Total Energy Balance for unsteady state, constant PV
For well-mixed reactor
with constant PV- variation
0

## Slide 6: Well-Mixed Reactors, Constant PV
Special case: well-mixed reactors (e.g., batch, CSTR or semibatch) with constant PV- variation in total P or V can be neglected
Total Energy Balance for unsteady state, constant PV
= 0
Total Energy Balance for unsteady state
Need to put dNi/dt into terms that can be measured

## Slide 7: EB for Well-Mixed Reactors, DPV=0
From the mass balance:
In
Out
-
+
Gen
Accumulation =
Substitute
Add SFiHi to both sides of equation:
Substitute ΣniHi =DH°RX(T):
DH°RX(T)

## Slide 8: Simplified EB for Well-Mixed Reactors
Bring SFi0Hi and DH°RX(T) terms to other side of equation:
Solve for dT/dt:
Factor SFi0Hi0 and SFi0Hi terms and divide by SNiCpi :
Energy balance for unsteady state reactor with phase change:
Energy balance for unsteady state reactor without phase change:

## Slide 9: Unsteady State EB, Liquid-Phase Rxns
For liquid-phase reactions, often DCp = SniCpi is so small it can be neglected
When DCp can be neglected, then:
If the feed is well-mixed, it is convenient to use:
Plug these equations and Ti0 = T0 into the EB gives:
This equation for the EB is simultaneously solved with the mass balance (design eq) for unsteady state, nonisothermal reactor design

## Slide 10: Nonisothermal Batch Reactor Design
No flow, so:
0
Put the energy balance in terms of XA:
Solve with the batch reactor design equation using an ODE solver (Polymath)

## Slide 11: Adiabatic Nonisothermal Batch Reactor Design
In the case of no stirring work and adiabatic operation,
Substitute:
Rearrange:
Substitute:
0
0

## Slide 12
Get like terms together:
Solving for T:
Solve with the batch reactor design equation using an ODE solver (Polymath)
Integrate & solve for XA:
Heat capacity of soln (calculate Cps if not given)
Solve for how XA changes with T

## Slide 13
A 1st order, liquid-phase, exothermic reaction A→B is run in a batch reactor. The reactor is well-insulated, so no heat is lost to the surroundings. To control the temperature, an inert liquid C is added to the reaction. The flow rate of C is adjusted to keep T constant at 100 °F. What is the flow rate of C after 2h?
This is essentially a semi-batch reactor since only C is fed into the reactor
Design eq:
Rate eq: -rA = kCA
Note, using
would complicate
the calculation because V depends on t
Combine:
Rearrange and integrate for NA
TC0 = 80 °F V0= 50 ft3 DH°RX=-25000 Btu/lb mol
k(100 °F)= 1.2 x 10-4 s-1 Cp, (all components)= 0.5 Btu/lb mol °F
CA0= 0.5 lb mol/ft3
Solve design eq for comp as function of t
Solve EB for FC0 using that info & T=100 °F

## Slide 14
Use EB to find how the flow rate of C depends on the rxn (solve EB for FC0)
A 1st order, liquid-phase, exothermic reaction A→B is run in a batch reactor. The reactor is well-insulated, so no heat is lost to the surroundings. To control the temperature, an inert liquid C is added to the reaction. The flow rate of C is adjusted to keep T constant at 100 °F. What is the flow rate of C after 2h?
C is the only species that flows, so:
rAV = -kCAV = -kNA
0
0
0
Isolate FC0:

## Slide 15
A 1st order, liquid-phase, exothermic reaction A→B is run in a batch reactor. The reactor is well-insulated, so no heat is lost to the surroundings. To control the temperature, an inert liquid C is added to the reaction. The flow rate of C is adjusted to keep T constant at 100 °F. What is the flow rate of C after 2h?
TC0 = 80 °F V0= 50 ft3 DH°RX=-25000 Btu/lb mol
k(100 °F)= 1.2 x 10-4 s-1 Cp, (all components)= 0.5 Btu/lb mol °F
CA0= 0.5 lb mol/ft3
At 2h (7200s):

## Slide 16
Instead of feeding coolant to the reactor, a solvent with a low boiling point is added (component D). The solvent has a heat of vaporization of 1000 Btu/lb mol, and initially 25 lb mol of A are placed in the tank. The reactor is well-insulated. What is the rate of solvent evaporation after 2 h if T is constant at 100 °F?
Still a semibatch reactor, where D is removed from the reactor
Use EB that accounts for a phase change:
Q˙ =0
ẆS=0
0
0
0
Additional info: k(100 °F)= 1.2 x 10-4 s-1 DH°RX=-25000 Btu/lb mol
Clicker Question: Does dT/dt = 0?
Yes
No

## Slide 17
Instead of feeding coolant to the reactor, a solvent with a low boiling point is added (component D). The solvent has a heat of vaporization of 1000 Btu/lb mol, and initially 25 lb mol of A are placed in the tank. What is the rate of solvent evaporation after 2 h?
Still a semibatch reactor, where D is removed from the reactor
Use EB that accounts for a phase change:
Q˙ =0
ẆS=0
dT/dt = 0
D is the only species that ‘flows’, and rAV = -kNA0(exp[-kt]), so:
Hi0-Hi = heat of vap
0
0
0
Additional info: k(100 °F)= 1.2 x 10-4 s-1 DH°RX=-25000 Btu/lb mol

## Slide 18
A liquid phase exothermic reaction A →B is carried out at 358K in a 0.2 m3 CSTR. The coolant temperature is 273K and the heat transfer coefficient (U) is 7200 J/min·m2·K. What is the heat exchange area required for steady state operation? Using this heat exchange area, plot T vs t for reactor start-up.
CPA =CPS=20 J/g•K ẆS=0 CA0= 180 g/dm3 u0= 500 dm3/min T0= 313 K
r= 900 g/dm3 DH°RX(T) = -2500 J/g E=94852 J/mol·K k(313K)= 1.1 min-1
a) Heat exchange area for steady state operation:
SS operation means that T is constant, so:
Q˙ =UA(Ta-T), ẆS=0, and A is only species that flows
Plug in rA = -kCA and solve for A

## Slide 19
A liquid phase exothermic reaction A →B is carried out at 358K in a 0.2 m3 CSTR. The coolant temperature is 273K and the heat transfer coefficient (U) is 7200 J/min·m2·K. What is the heat exchange area required for steady state operation? Using this heat exchange area, plot T vs t for reactor start-up.
CPA =CPS=20 J/g•K ẆS=0 CA0= 180 g/dm3 u0= 500 dm3/min T0= 313 K
r= 900 g/dm3 DH°RX(T) = -2500 J/g E=94852 J/mol·K k(313K)= 1.1 min-1
Use material balance to determine steady state value of CA

## Slide 20
A liquid phase exothermic reaction A →B is carried out at 358K in a 0.2 m3 CSTR. The coolant temperature is 273K and the heat transfer coefficient (U) is 7200 J/min·m2·K. What is the heat exchange area required for steady state operation? Using this heat exchange area, plot T vs t for reactor start-up.
CPA =CPS=20 J/g•K ẆS=0 CA0= 180 g/dm3 u0= 500 dm3/min T0= 313 K
r= 900 g/dm3 DH°RX(T) = -2500 J/g E=94852 J/mol·K k(313K)= 1.1 min-1
Solve for heat exchange area at SS:
A=227.4 m2
FA0=90,000 g/min V=200 dm3
DH°RX(T) = -2500 J/g k= 107.4 min-1 CA= 4.1 g/dm3 CPA =20 J/g•K
U= 7200 J/min·m2·K TA0= 313 K T= 358K Ta=273K

## Slide 21
Will use Polymath to plot T vs t for CSTR start-up (unsteady-state). Need equations for dCA/dt, dT/dt, and k.
U= 7200 J/min·m2·K A=227.4m2 CA0=180g/dm3 t=V/u0 Ta=273K
DHRX=-2500 J/g Ni0=mi0 V=200 dm3 CPs=20 J/g˙K u0=500 dm3 T0=313
Mass balance:
CPs is in terms of mass (J/g·K), so FA0 & Ni0 must also be in terms of mass
rA=-kCA
FA0=90,000 g/min
Substitute ṁi0 for Ni0, & use r for the solution to calculate:
Amount of gas leaving reactor (L7)

## Slide 22
Will use Polymath to plot T vs t for CSTR start-up (unsteady-state). Need equations for dCA/dt, dT/dt, and k.
U= 7200 J/min·m2·K A=227.4m2 CA0=180g/dm3 t=V/u0 Ta=273K
DHRX=-2500 J/g Ni0=mi0 V=200 dm3 CPs=20 J/g˙K u0=500 dm3 T0=313
rA=-kCA
FA0=90,000 g/min

## Slide 23
T (K)
t (min)
Reaches steady state at ~12 minutes

## Slide 24
The elementary, liquid phase, exothermic reaction A →B is carried out in a 2 m3
CSTR that is equipped with a heat jacket. Pure A enters the reactor at 60 mol/min and a temperature of 310K. The coolant in the heat jacket is kept at 280 K. Provide all equations, all constants, the initial time, and the final time that must be entered into Polymath in order to plot temperature vs time for the first 20 min of reactor start-up. ΔHRX(TR) = -10,000 cal/mol CPA = CPS =15 cal/mol·K CpB=15 cal/mol·K ẆS=0
E = 20,000 cal/mol k = 1 min-1 at 400 K UA= 3200 cal/min•K u0= 300 L/min
Need equations for how T changes with time, CA changes with time, & k changes with T.
Combine with EB:

## Slide 25
The elementary, liquid phase, exothermic reaction A →B is carried out in a 2 m3
CSTR that is equipped with a heat jacket. Pure A enters the reactor at 60 mol/min and a temperature of 310K. The coolant in the heat jacket is kept at 280 K. Provide all equations, all constants, the initial time, and the final time that must be entered into Polymath in order to plot temperature vs time for the first 20 min of reactor start-up. ΔHRX(TR) = -10,000 cal/mol CPA = CPS =15 cal/mol·K CpB=15 cal/mol·K ẆS=0
E = 20,000 cal/mol k = 1 min-1 at 400 K UA= 3200 cal/min•K u0= 300 L/min
Need equations for how T changes with time, CA changes with time, & k changes with T.
Use the mass balance to get eq for CA(t)