## Slide 1: Review: What size reactor(s) to use?
Answers to this questions are based on the desired conversion, selectivity and kinetics
Reactor type &
size
Conversion
&
selectivity
Kinetics
Material &
energy
balances

## Slide 2: Review: Rate Law for rj
rA: the rate of formation of species A per unit volume [e.g., mol/m3•s]
-rA: the rate of a consumption of species A per unit volume
rj depends on concentration and temperature:
1st order in A, 1st order in B, 2nd order overall
nth order in A
Michaelis-Menton: common in enzymatic reactions

## Slide 3
Review: Basic Molar Balance (BMB)
Rate of flow of j into system
-
Rate of flow of j out of system
+
Rate of generation of j by chemical rxn
-
Rate of decomposition of j
=
Rate of
accumulation
If the system is uniform throughout its entire volume, then:
Moles j generated per unit time (mol/s)
=
Moles generated per unit time and volume (mol/s•m3)
Volume
(m3)
System volume
Fj0
Fj
Gj

## Slide 4: Review: BMB Equations
In
Out
-
+
Generation
=
Accumulation
Next: Apply BME to ideal batch, CSTR, & PFR reactors
System volume
Fj0
Fj
Gj

## Slide 5: L2: Reactor Molar Balances & Considerations
reactor
Fj0
Fj
Gj
Today we will use BMB to derive reactor design equations. Your goal is to learn this process, not to memorize the equations!

## Slide 6: Batch Reactors Properties
Reactants are placed in the reactor, and the reaction is allowed to proceed for some amount of time
Closed system- no addition of reactants or removal of products during the reaction
Unsteady-state conditions- the composition changes with time
Ideal batch reactor- vessel is perfectly mixed
Concentration and temperature are spatially constant, but NOT constant in TIME

## Slide 7: Examples of Batch Reactor
Lab-Scale Batch Reactor
Typical Commercial Batch Reactor
Motor for agitation

## Slide 8: Basic Mole Balance for Batch Reactor
In
Out
-
+
Generation
=
Accumulation
No flow in or out!
Fj0
Fj
X
X
0
0
Batch Reactor Design Equation
If the reactor is perfectly mixed, the temperature, concentration, & therefore the reaction rate are spatially constant:
Ideal Batch Reactor Design Equation

## Slide 9: Continuous Stirred Tank Reactor (CSTR) Properties
Continuously add reactants and remove products (open system)
  Inlet stream instantaneously mixes with bulk of reactor volume
Ideal batch reactor- assume perfect mixing occurs in vessel
  Temperature and concentration are uniform throughout space
  Composition of the exit stream is the same as that inside reactor (CA,outlet = CA, tank)
Steady-state conditions- the reaction rate is the same at every point and does not change with time

## Slide 10: Examples of CSTRs
Laboratory-Scale Bioreactor
Pfaudler Inc.

## Slide 11: Basic Mole Balance for CSTR
In
Out
-
+
Generation
=
Accumulation
0
Steady State CSTR Design Equation
A perfectly mixed CSTR has no spatial variations in reaction rate
Fj0
Fj
CSTR is at steady state (SS), so no change in moles j with time!
Ideal Steady State CSTR Design Equation
Rearrange to put in terms of V
rj is measured at the outlet because Cj,exit = Cj,tank

## Slide 12: Ideal SS CSTR Design Equation
Reactor volume required to reduce the entering flow rate of species j from Fj0 to Fj at the outlet (and in the tank)
How do we determine the molar flow rate, Fj (units = mol/time)?
Cj: concentration of j : volumetric flow rate
Ideal SS CSTR design equation in terms of concentration:

## Slide 13: Plugged Flow Reactor (PFR) Properties
Also called a tubular reactor
Cylindrical pipe with openings at both ends
Steady movement of material down length of reactor
Reactants are consumed as they flow down the length of the reactor
Operated at steady state:
  No radial variation in temperature, concentration, or reaction rate
  All fluid/gas elements have the same residence time

## Slide 14: Industrial PFRs
Polyethylene reactor:
16 inch inner diameter
Operates at 35,000 psi & 600 °F
Has a vertical orientation when in use
Courtesy of Autoclave Engineers of Snap-tite, Inc.

## Slide 15: Mole Balance – PFR
ΔV
FA0
FA
In a plug flow reactor the composition of the fluid varies from point to point along a flow path. Consequently, the material balance for a reaction component must be made for a differential element of volume ΔV
Fj0
Fj
+
-
=
0
Divide by DV
lim
DV→0
Ideal SS PFR Design Eq.
If we assume the PFR is ideal, the degree of completion is not affected by PFR shape, only by PFR volume

## Slide 16: Packed Bed Reactors (PBR)
Cylindrical shell, vertically oriented
Often gravity-driven flow
Heterogeneous reaction: fixed bed of catalyst inside
Reactants enter top and flow through the packed bed of catalyst
Concentration gradient of reactant and product down the length of the reactor
Reaction occurs on the surface of the catalyst pellets
Reaction rate is based on the mass of the solid catalyst, W, not reactor volume V

## Slide 17: Mole Balance- Packed Bed Reactor (PBR)
Similar to PFR, but we want to express it in terms of catalyst weight instead of reactor volume
Units for the rate of a homogeneous rxn (rj) :
Units for the rate of a catalytic rxn (rj’) :
So rewriting the PFR design equation in terms of catalyst weight instead of reactor volume:

## Slide 18: Mole Balances on Common Reactors

## Slide 19: Selection of Reactors
Batch
    small scale
    production of expensive products (e.g. pharmacy)
    high labor costs per batch
    difficult for large-scale production
CSTR: most homogeneous liquid-phase flow reactors
    when intense agitation is required
    relatively easy to maintain good temperature control
    the conversion of reactant per volume of reactor is the smallest of the flow reactors - very large reactors are necessary to obtain high conversions
PFR: most homogeneous gas-phase flow reactors
    relatively easy to maintain
    usually produces the highest conversion per reactor volume (weight of catalyst if it is a packed-bed catalyze gas reaction) of any of the flow reactors
    difficult to control temperature within the reactor
    hot spots can occur

## Slide 20: Uses for Various Reactors
Noncatalytic homogeneous gas reactor
Homogeneous liquid reactor
Liquid-liquid reactor
Gas-liquid reactor
Non-catalytic gas-solid reactor
  Fixed bed
  Fluidized bed
Fixed bed catalytic reactor
Fluid bed catalytic reactor
Gas-liquid-solid reactor
Ethylene polymerization
(high pressure)
Mass polymerization of styrene
Saponification of fats
Nitric acid production
Iron production
Chlorination of metals
Ammonia synthesis
Catalytic cracking (petroleum)
Hydrodesulphurization of oils