## Slide 1: Review: Design Eq & Conversion
Ideal CSTR Design Eq with XA:
BATCH
SYSTEM:
FLOW
SYSTEM:
Ideal Batch Reactor Design Eq with XA:
Ideal SS PFR Design Eq with XA:
Ideal SS PBR Design Eq with XA:
nj≡ stoichiometric coefficient; positive for products, negative for reactants

## Slide 2: Review: Sizing CSTRs
We can determine the volume of the CSTR required to achieve a specific conversion if we know how the reaction rate rj depends on the conversion Xj
Ideal SS CSTR design eq.
Volume is product of FA0/-rA and XA
Plot FA0/-rA vs XA (Levenspiel plot)
VCSTR is the rectangle with a base of XA,exit and a height of FA0/-rA at XA,exit

## Slide 3: Review: Sizing PFRs & PBRs
Area = VPFR or Wcatalyst, PBR
We can determine the volume (catalyst weight) of a PFR (PBR) required to achieve a specific Xj if we know how the reaction rate rj depends on Xj
Ideal PFR design eq.
Plot FA0/-rA vs XA (Experimentally determined numerical values)
VPFR (WPBR) is the area under the curve FA0/-rA vs XA,exit
Ideal PBR design eq.

## Slide 4: Numerical Evaluation of Integrals (A.4)
Simpson’s one-third rule (3-point):
Trapezoidal rule (2-point):
Simpson’s three-eights rule (4-point):
Simpson’s five-point quadrature :

## Slide 5: Review: Reactors in Series
2 CSTRs
2 PFRs
CSTR→PFR
VCSTR1
VPFR2
VPFR2
VCSTR1
VCSTR2
VPFR1
VPFR1
VCSTR2
VCSTR1 + VPFR2
≠
VPFR1 + CCSTR2
PFR→CSTR
If is monotonically
increasing then:

## Slide 6: Chapter 2 Examples

## Slide 7
XA | 0 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.85
-rA | 0.0053 | 0.0052 | 0.0050 | 0.0045 | 0.0040 | 0.0033 | 0.0025 | 0.0018 | 0.00125 | 0.001
1. Calculate FA0/-rA for each conversion value in the table
FA0/-rA
Calculate the reactor volumes for each configuration shown below for the reaction data in the table when the molar flow rate is 52 mol/min.
FA0, X0
X1=0.3
X2=0.8
Config 1
X1=0.3
FA0, X0
X2=0.8
Config 2
←Use numerical methods to solve
XA,out and XA,in respectively, are the conversion at the outlet and inlet of reactor n
Convert to seconds→
-rA is in terms of mol/dm3∙s

## Slide 8
164
1. Calculate FA0/-rA for each conversion value in the table
XA | 0 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.85
-rA | 0.0053 | 0.0052 | 0.0050 | 0.0045 | 0.0040 | 0.0033 | 0.0025 | 0.0018 | 0.00125 | 0.001
FA0/-rA | 164 |  |  |  |  |  |  |  |  | 
Calculate the reactor volumes for each configuration shown below for the reaction data in the table when the molar flow rate is 52 mol/min.
FA0, X0
X1=0.3
X2=0.8
Config 1
X1=0.3
FA0, X0
X2=0.8
Config 2
←Use numerical methods to solve
-rA is in terms of mol/dm3∙s
164
XA,out and XA,in respectively, are the conversion at the outlet and inlet of reactor n
Convert to seconds→

## Slide 9
164
1. Calculate FA0/-rA for each conversion value in the table
XA | 0 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.85
-rA | 0.0053 | 0.0052 | 0.0050 | 0.0045 | 0.0040 | 0.0033 | 0.0025 | 0.0018 | 0.00125 | 0.001
FA0/-rA |  |  |  |  |  |  |  |  |  | 
Calculate the reactor volumes for each configuration shown below for the reaction data in the table when the molar flow rate is 52 mol/min.
FA0, X0
X1=0.3
X2=0.8
Config 1
X1=0.3
FA0, X0
X2=0.8
Config 2
←Use numerical methods to solve
-rA is in terms of mol/dm3∙s
164
XA,out and XA,in respectively, are the conversion at the outlet and inlet of reactor n
Convert to seconds→
For each –rA that corresponds to a XA value, use FA0 to calculate FA0/-rA & fill in the table

## Slide 10
X1=0.3
FA0, X0
1. Calculate FA0/-rA for each conversion value in the table
XA | 0 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.85
-rA | 0.0053 | 0.0052 | 0.0050 | 0.0045 | 0.0040 | 0.0033 | 0.0025 | 0.0018 | 0.00125 | 0.001
FA0/-rA | 164 | 167 | 173 | 193 | 217 | 263 | 347 | 482 | 694 | 867
Calculate the reactor volumes for each configuration shown below for the reaction data in the table when the molar flow rate is 52 mol/min.
FA0, X0
X1=0.3
X2=0.8
Config 1
X2=0.8
Config 2
←Use numerical methods to solve
Convert to seconds→
-rA is in terms of mol/dm3∙s
XA,out and XA,in respectively, are the conversion at the outlet and inlet of reactor n

## Slide 11
XA | 0 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.85
-rA | 0.0053 | 0.0052 | 0.0050 | 0.0045 | 0.0040 | 0.0033 | 0.0025 | 0.0018 | 0.00125 | 0.001
FA0/-rA | 164 | 167 | 173 | 193 | 217 | 263 | 347 | 482 | 694 | 867
FA0, X0
X1=0.3
X2=0.8
Config 1
Reactor 1, PFR from XA0=0 to XA=0.3:
4-pt rule:
Total volume for configuration 1: 51.6 dm3 + 347 dm3 = 398.6 dm3 = 399 dm3
←Use numerical methods to solve
PFR1
CSTR2

## Slide 12
XA | 0 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.85
-rA | 0.0053 | 0.0052 | 0.0050 | 0.0045 | 0.0040 | 0.0033 | 0.0025 | 0.0018 | 0.00125 | 0.001
FA0/-rA | 164 | 167 | 173 | 193 | 217 | 263 | 347 | 482 | 694 | 867
Reactor 1, CSTR from XA0=0 to XA=0.3:
Need to evaluate at 6 pts, but since there is no 6-pt rule, break it up
Total volume for configuration 2: 58 dm3 + 173 dm3 = 231 dm3
X1=0.3
FA0, X0
X2=0.8
Config 2
3 point rule
4 point rule
PFR2
CSTR1
Must evaluate as many pts as possible when the curve isn’t flat

## Slide 13
For a given CA0, the space time t needed to achieve 80% conversion in a CSTR is 5 h. Determine (if possible) the CSTR volume required to process 2 ft3/min and achieve 80% conversion for the same reaction using the same CA0. What is the space velocity (SV) for this system?
t=5 h
u0=2 ft3/min
Space velocity:
Notice that we did not need to solve the CSTR design equation to solve this problem.
Also, this answer does not depend on the type of flow reactor used.
XA=0.8

## Slide 14
A product is produced by a nonisothermal, nonelementary, multiple-reaction mechanism. Assume the volumetric flow rate is constant & the same in both reactors. Data for this reaction is shown in the graph below. Use this graph to determine which of the 2 configurations that follow give the smaller total reactor volume.
FA0, X0
X1=0.3
X2=0.7
Config 2
X1=0.3
FA0, X0
X2=0.7
Config 1
Shown on graph
Since u0 is the same in both reactors, we can use this graph to compare the 2 configurations
PFR- volume is u0 multiplied by the area under the curve between XA,in & XA,out
CSTR- volume is u0 multiplied by the product of CA0/-rA,outlet times (XA,out - XA,in)

## Slide 15
A product is produced by a nonisothermal, nonelementary, multiple-reaction mechanism. Assume the volumetric flow rate is constant & the same in both reactors. Data for this reaction is shown in the graph below. Use this graph to determine which of the 2 configurations that follow give the smaller total reactor volume.
FA0, X0
X1=0.3
X2=0.7
Config 2
X1=0.3
FA0, X0
X2=0.7
Config 1
PFR- V is u0 multiplied by the area under the curve between XA,in & XA,out
CSTR- V is u0 multiplied by the product of CA0/-rA,outlet times (XA,out - XA,in)
Config 1
Config 2
Less shaded area
Config 2 (PFRXA,out=0.3 first, and CSTRXA,out=0.7 second) has the smaller VTotal
XA = 0.3
XA = 0.7
XA = 0.3
XA = 0.7