## Slide 1: Review: Logic of Isothermal Reactor Design
In
Out
-
+
Generation
=
Accumulation
1. Set up mole balance for specific reactor
2. Derive design eq. in terms of XA for each reactor
Batch
CSTR
PFR
3. Put Cj is in terms of XA and plug into rA
4. Plug rA into design eq and solve for the time (batch) or volume (flow) required for a specific XA
(We will always look conditions where Z0=Z)
Examples of combining rates & design eqs follow!

## Slide 2: Review: Batch Reactor Operation
Batch Volume is constant, V=V0
Mole balance
Rate law
Stoichiometry (put CA in terms of X)
Combine
A → B -rA = kCA2
2nd order reaction rate
Calculate the time required for a conversion of XA in a constant V batch reactor
Integrate this equation in order to solve for time, t
Be able to do these 4 steps, and then integrate to solve for time for ANY REACTION

## Slide 3: Review: CSTR Operation
A → B -rA = kCA
Calculate the CSTR volume required to get a conversion of XA
Mole balance
Rate law
Stoichiometry (put CA in terms of X)
Combine
1st order reaction rate
Put FA0 in terms of CA0
Volume required to achieve XA for 1st order rxn
Be able to do these steps for any order reaction!

## Slide 4: Review: Scaling CSTRs
Space time t (residence time) required to achieve XA for 1st order irreversible rxn
If one knows the volume of the pilot-scale reactor required to achieve XA, how is this information used to achieve XA in a larger reactor?
k in the small reactor is the same as k in the bigger reactor
Want XA in the small reactor to be the same as XA in the bigger reactor
u0 in the small reactor must be different from u0 in the bigger reactor
Suppose for a 1st order irreversible rxn:
Separate variables we will
vary from those held constant
So the reactor volume must be proportional to the volumetric flow rate u0
Be able to do this for any order rxn!
Eq is for a 1st order rxn only!

## Slide 5: Review: Damköhler Number, Da
Estimates the degree of conversion that can be obtained in a flow reactor
First order irreversible reaction:
1st order irreversible reaction
Second order irreversible reaction:
2nd order irreversible reaction
How is XA related to Da in a first order irreversible reaction in a flow reactor?
If Da < 0.1, then XA < 0.1
If Da > 10, then XA > 0.9
Substitute
From slide L6-7:

## Slide 6: Review: Sizing CSTRs for 2nd Order Rxn
Mole balance
Rate laws
Stoichiometry
Combine
or
Calculate the CSTR volume required to get a conversion of XA
A → B -rA = kCA2
Liquid-phase 2nd order reaction rate
In terms of conversion?
In terms of space time?
In terms of XA as a function of Da?
Eq is for a 2nd order liquid irreversible rxn
Be able to do these steps!

## Slide 7: Review: n CSTRs in Series
CA0u0
CA1u
CA2u
u0 = u
For n identical CSTRs, then:
How is conversion related to the # of CSTRs in series?
Put CAn in terms of XA (XA at the last CSTR):
1st order irreversible liquid phase rxn run in n CSTRs with identical V, t and k
1st order irreversible liquid-phase rxn run in n CSTRs with identical V, t and k
Rate of disappearance of A in the nth reactor:

## Slide 8: Review: Isothermal CSTRs in Parallel
FA0
FA01
FA02
same T, V, u
Subscript i denotes reactor i
FA01 = FA02 = … FA0n
Volume of each CSTR
Molar flow rate of each CSTR
Mole Balance
Conversion achieved by any one of the reactors in parallel is the same as if all the reactant were fed into one big reactor of volume V

## Slide 9: Liquid Phase Reaction in PFR
LIQUID PHASE: Ci ≠ f(P) → no pressure drop
Calculate volume required to get a conversion of XA in a PFR
2A → B -rA = kCA2
2nd order reaction rate
Mole balance
Rate law
Stoichiometry (put CA in terms of X)
Combine
Liquid-phase 2nd order reaction in PFR
Be able to do these 4 steps, integrate & solve for V for ANY ORDER RXN
See Appendix A for integrals frequently used in reactor design

## Slide 10: Liquid Phase Reaction in PBR
LIQUID PHASE: Ci ≠ f(P) → no pressure drop
Calculate catalyst weight required to get a conversion of XA in a PBR
2A → B -r’A = kCA2
2nd order reaction rate
Mole balance
Rate law
Stoichiometry (put CA in terms of X)
Combine
Liquid-phase 2nd order reaction in PBR
Be able to do these 4 steps, integrate & solve for V for ANY ORDER RXN

## Slide 11: Isobaric, Isothermal, Ideal Rxns in Tubular Reactors
GAS PHASE:
1
1
1
Gas-phase reactions are usually carried out in tubular reactors (PFRs & PBRs)
  Plug flow: no radial variations in concentration, temperature, & ∴ -rA
  No stirring element, so flow must be turbulent
FA0
FA
Stoichiometry for basis species A:

## Slide 12: Isobaric, Isothermal, Ideal Rxn in PFR
GAS PHASE: Ci = f(e) → no DP, DT, or DZ
Calculate PFR volume required to get a conversion of XA
2A → B -rA = kCA2
2nd order reaction rate
Mole balance
Rate law
Stoichiometry (put CA in terms of X)
Combine
Gas-phase 2nd order rxn in PFR no DP, DT, or DZ
Integral A-7 in appendix

## Slide 13: Effect of e on u and XA
e: expansion factor, the fraction of change in V per mol A reacted
u0: volumetric flow rate
u varies if gas phase & moles product ≠ moles reactant, or if a DP, DT, or DZ occurs
No DP, DT, or DZ occurs, but moles product ≠ moles reactant →
e = 0 (mol product = mol reactants): u = u0: constant volumetric flow rate as XA increases
  e < 0 (mol product < mol reactants): u < u0 volumetric flow rate decreases as XA increases
  Longer residence time than when u = u0
  Higher conversion per volume of reactor (weight of catalyst) than if u = u0
  e > 0 (mol product > mol reactants): u > u0 with increasing XA
  Shorter residence time than when u = u0
  Lower conversion per volume of reactor (weight of catalyst) than if u = u0

## Slide 14: Pressure Drop in PFRs & PBRs
GAS PHASE:
Considering ideal gas phase behavior (Z0=Z)
Concentration is a function of P so pressure drop is important in gas phase rxns
Why?
Take a 1st order reaction A → B in a PBR with –r’A = kCA
Substitute concentration of A into the rate law:
If P drops during the reaction, P/P0 is less than one, so CA ↓ & the rxn rate ↓
For tubular reactors:
PFR
PBR
Use the differential forms of the design equations to address pressure drop
Pressure drops are especially common in reactions run in PBRs
→ we will focus on PBR applications

## Slide 15: Pressure Drop in PBRs
GAS PHASE: A → B -r’A = kCA2
Calculate dXA/dW for an isothermal ideal gas phase reaction with DP
2nd order reaction rate
Mole balance
Rate law
Stoichiometry (put CA in terms of X)
Combine
We need to relate P/P0 to W
This eq. is solved simultaneously with an eq. that describes how the pressure drops as the reactant moves down the reactor
Function of XA and pressure

## Slide 16: Ergun Equation relates P to W
Differential form of Ergun equation for pressure drop in PBR:
AC: cross-sectional area rC: particle density
b: constant for each reactor, calculated using a complex equation that depends on properties of bed (gas density, particle size, gas viscosity, void volume in bed, etc)
a: constant dependant on the packing in the bed
This equation can be simplified to:

## Slide 17: Gas Phase Reaction in PBR with ΔP
GAS PHASE: A → B -r’A = kCA2
Calculate dXA/dW for an isothermal ideal gas phase reaction with DP
2nd order reaction rate
Mole balance
Combine with rate law and stoichiometry
Relate P/P0 to W
Ergun Equation can be simplified by using y=P/P0 and T=T0:
Simultaneously solve dXA/dW and dP/dW (or dy/dW) using Polymath

## Slide 18: Analytical Solutions to P/P0
Sometimes P/P0 can be calculated analytically. When T is constant and e = 0:
1
0
1
Evaluate
Only for isothermal rxn where e=0
From no pressure change
To pressure change

## Slide 19: Pressure Drop Example
GAS PHASE: A → B
2nd order reaction rate
This gas phase reaction is carried out isothermally in a PBR. Relate the catalyst weight to XA
1
0
e = 0 and isothermal, so:
Plug into CA
Plug into PBR design eq:
-r’A = kCA2
Simplify, integrate, and solve for XA in terms of W or W in terms of XA:

## Slide 20: Pressure Drop Example
A → B -r’A = kCA2
2nd order gas phase rxn non-elementary rate
This gas phase reaction is carried out isothermally in a PBR. Relate the catalyst weight to XA
Solve for XA
Rearrange eq. for W:

## Slide 21: Next Time
Startup of a CSTR under isothermal conditions
Semi-batch reactor