## Slide 1: Review: Liquid Phase Reaction in PFR
LIQUID PHASE: Ci ≠ f(P) → no pressure drop
Calculate volume required to get a conversion of XA in a PFR
2A → B -rA = kCA2
2nd order reaction rate
Mole balance
Rate law
Stoichiometry (put CA in terms of X)
Combine
Liquid-phase 2nd order reaction in PFR
Be able to do these 4 steps, integrate & solve for V for ANY ORDER RXN
See Appendix A for integrals frequently used in reactor design

## Slide 2: Review: Liquid Phase Reaction in PBR
LIQUID PHASE: Ci ≠ f(P) → no pressure drop
Calculate catalyst weight required to get a conversion of XA in a PBR
2A → B -r’A = kCA2
2nd order reaction rate
Mole balance
Rate law
Stoichiometry (put CA in terms of X)
Combine
Liquid-phase 2nd order reaction in PBR
Be able to do these 4 steps, integrate & solve for V for ANY ORDER RXN

## Slide 3: Review: Isobaric, Isothermal, Ideal Gas-Phase Rxns in Tubular Reactors
GAS PHASE:
1
1
1
Gas-phase reactions are usually carried out in tubular reactors (PFRs & PBRs)
  Plug flow: no radial variations in concentration, temperature, & ∴ -rA
  No stirring element, so flow must be turbulent
FA0
FA
Stoichiometry for basis species A:

## Slide 4: Review: Effect of e on u and XA
e: expansion factor, the fraction of change in V per mol A reacted
u0: volumetric flow rate
u varies if gas phase & moles product ≠ moles reactant, or if a DP, DT, or DZ occurs
No DP, DT, or DZ occurs, but moles product ≠ moles reactant →
e = 0 (mol product = mol reactants): u = u0: constant volumetric flow rate as XA ↑e < 0 (mol product < mol reactants): u < u0 volumetric flow rate ↓ as XA ↑
Q1: For an irreversible gas-phase reaction, how does the residence time and XA change when  < 0?
They don’t
The residence time is longer & XA increases
The residence time is longer & XA decreases
The residence time is shorter, & XA decreases
The residence time is shorter & XA increases

## Slide 5: Review: Effect of e on u and XA
e: expansion factor, the fraction of change in V per mol A reacted
u0: volumetric flow rate
u varies if gas phase & moles product ≠ moles reactant, or if a DP, DT, or DZ occurs
No DP, DT, or DZ occurs, but moles product ≠ moles reactant →
e = 0 (mol product = mol reactants): u = u0: constant volumetric flow rate as XA increases
  e < 0 (mol product < mol reactants): u < u0 volumetric flow rate decreases as XA increases
  Longer residence time than when u = u0
  Higher conversion per volume of reactor (weight of catalyst) than if u = u0
  e > 0 (mol product > mol reactants): u > u0 with increasing XA
  Shorter residence time than when u = u0
  Lower conversion per volume of reactor (weight of catalyst) than if u = u0

## Slide 6: Review: Isobaric, Isothermal, Ideal Rxn in PFR
GAS PHASE:
Ci = f(e) → no DP, DT, or DZ
Calculate PFR volume required to get a conversion of XA
2A → B -rA = kCA2
2nd order reaction rate
Mole balance
Rate law
Stoichiometry (put CA in terms of X)
Combine
Gas-phase 2nd order rxn in PFR no DP, DT, or DZ
Integral A-7 in appendix
Be able to do these 5 steps, & solve for V for ANY ORDER RXN

## Slide 7: Review: Pressure Drop in PBRs
GAS PHASE: A → B -r’A = kCA2
Calculate dXA/dW for an isothermal ideal gas phase reaction with DP
2nd order reaction rate
Mole balance
Rate law
Stoichiometry (put CA in terms of X)
Combine
Relate P/P0 to W (Ergun equation)
Ergun Equation can be simplified by using y=P/P0 and T=T0:
Simultaneously solve dXA/dW and dP/dW (or dy/dW) using Polymath

## Slide 8: Review: Ergun Equation
Differential form of Ergun equation for pressure drop in PBR:
AC: cross-sectional area rC: particle density
b: constant for each reactor, calculated using a complex equation that depends on properties of bed (gas density, particle size, gas viscosity, void volume in bed, etc)
a: constant dependant on the packing in the bed
Calculates pressure drop in a packed bed.
This equation can be simplified to:

## Slide 9: L7: Unsteady-State Isothermal Reactor Operation: CSTR Start-Up and Semi-Batch Reactors
V0
Vf
start
CBu0
V0 + u0t
time t
end
Semi-batch
Time required to reach steady-state after CSTR start-up
Predicting concentration and conversion as a function of time
A+B
A

## Slide 10: Start-Up of a Fixed-Volume CSTR
Isothermal (unusual, but simple case), well-mixed CSTR
Unsteady state: concentrations vary with time & accumulation is non-zero
Goal: Determine the time necessary to reach steady-state operation
moles A in CSTR changes with time until steady state is reached
In
Out
-
+
Generation
=
Accumulation
CA0u0
u0CA
Use concentration rather than conversion in the balance eqs
Divide by V to convert dNA to dCA
Multiply by t

## Slide 11: CSTR Start-Up: 1st Order Reaction
Integrate this eq to find CA (t) while 1st order rxn in CSTR is at unsteady-state:
Combine
Bring variables to one side & factor
Put like variables with their integrals

## Slide 12: CSTR Start-Up: 1st Order Reaction
We integrated this eq to find CA (t) while CSTR of 1st order rxn is in unsteady-state:
At steady state, t is large and:
0
Is this consistent with steady state balance eq for CSTR?
No accumulation at steady state
0
In the unsteady state, when CA = 0.99CAS:
time to reach 99% of steady-state concentration in terms of tk
Solve for ts to determine time to reach 99% of steady-state concentration
Goal: combine start-up and SS eqs to estimate time to reach SS (ts)
Yes, same!

## Slide 13: CSTR Start-Up: 1st Order Reaction
99% of the steady-state concentration is achieved at:
When k is very small (slow rxn), 1>>kt:
When k is very big (fast rxn), 1<<kt
63% of the steady-state concentration is achieved at:
CA = 0.63CAS
In the unsteady state, the time to reach CA = 0.99CAS is:

## Slide 14: Better Selectivity in a Semi-Batch Reactor
To enhance selectivity of desired product over side product
Desired product P
Undesired side product S
Instantaneous selectivity, SP/S, is the ratio of the relative rates*:
Higher concentrations of A favor formation of the desired product P
Higher concentrations of B favor formation of the undesired side product S
Slowly feed B into the reactor containing A
Commonly used in bioreactors, when the enzyme is inhibited by excess substrate
To maximize the formation of the desired product:
*We’ll look at this concept of instantaneous selectivity in more detail in L9
Notes: We’ll look at this concept of instantaneous selectivity in more detail in L9

## Slide 15: Semi-Batch Reactor Design Equation
CBu0
V0 + u0t
Do a mole balance on A since it does not enter or leave the reactor (assume the reactor is well-mixed)
In
Out
-
+
Generation
=
Accumulation
Use whatever units are most convenient (NA, CA, XA, etc)
2 parts: how CA changes with t and how V changes with t
Convert NA to CA using:

## Slide 16: Semi-Batch Reactor Design Equation
CBu0
V0 + u0t
Do a mole balance on A since it does not enter or leave the reactor (assume the reactor is well-mixed)
In
Out
-
+
Generation
=
Accumulation
2 parts: how CA changes with t and how V changes with t
Reactor volume at any time can be found with a mole balance
In
Out
-
+
Generation
=
Accumulation
= u0
r = r0
Substitute:
Rearrange to get in terms of dCA/dt
Balance on A

## Slide 17: Semi-Batch Reactor Design Equation
CBu0
V0 + u0t
Mole Balance on B
In
Out
-
+
Generation
=
Accumulation
Substitute
Rearrange to get in terms of dCB/dt
Balance on B

## Slide 18: Semi-Batch Reactor Design Equation: in Terms of NA
CBu0
V0 + u0t
In
Out
-
+
Generation
=
Accumulation
Reactor design eq. provided that rA is a function of NA
NB comes from BMB:
The design eq in terms of XA can be messy. Sometimes it gives a single equation when using Nj or Cj gives multiple reactor design equations.
-rA = kACACB

## Slide 19: Improving Yields of Reversible Rxns with Semi-Batch Reactors
+ H2O
V0
Vf
FD
V0 - u0t
Semi-batch
To improve product yield in a reversible reaction:
Start with A(l) and B(l) in the reactor
D(g) bubbles out of the liquid phase, pushing the equilibrium to the right and forcing the reaction to go to completion
Common industrial reaction:
n
+ n
Boil off water to produce high MW polymer
nylon
A+B⇌C+D
A+B

## Slide 20: Improving Yields of Reversible Rxns with Semi-Batch Reactors
How do we account for the loss of product D in the material balance?
V0
Vf
FD
V0 - u0t
Semi-batch
To improve product yield in a reversible reaction:
Start with A(l) and B(l) in the reactor
D(g) bubbles out of the liquid phase, pushing the equilibrium to the right and forcing the reaction to go to completion
A+B⇌C+D
A+B

## Slide 21: Loss of Mass in Semi-Batch Reactor
In
Out
-
+
Generation
=
Accumulation
Overall Mass balance:
↑want in terms of dV/dt
V0 + u0t
D(g)
= u0 r = r0
Divide mass balance by r
Relate ṁ to a rate:
From stoichiometry, rD = -rA
Next, convert units to:
Substitute for ṁ
One of the diff. eq. that are simultaneously solved (by Polymath)
Conversion 1:
Conversion 2: