## Slide 1: Review: Isothermal Reactor Design
In
Out
-
+
Generation
=
Accumulation
1. Set up mole balance for specific reactor
2. Derive design eq. in terms of XA for each reactor
Batch
CSTR
PFR
3. Put Cj is in terms of XA and plug into rA
4. Plug rA into design eq & solve for the time (batch) or V (flow) required for a specific XA or the XA obtained for given V , 0, time, etc
(We will always look conditions where Z0=Z)
Be able to rearrange equations & integrate for Q2
Reaction order needs to be determined.

## Slide 2: Review: Analysis of Rate Data
Constant-volume batch reactor for homogeneous reactions: make concentration vs time measurements during unsteady-state operation
Differential reactor for solid-fluid reactions: monitor product concentration for different feed conditions during steady state operation
  Goal: determine reaction order, a, and specific reaction rate constant, k
Data collection is done in the lab so we can simplify BMB, stoichiometry, and fluid dynamic considerations
Want ideal conditions → well-mixed (data is easiest to interpret)
Method of Excess
Differential method
Integral method
Half-lives method
Initial rate method
Differential reactor
More complex kinetics

## Slide 3: Review: Method of Excess
A + B → products Suspect rate eq. -rA = kCAaCBb
Run reaction with an excess of B so CB ≈ CB0
Rate equation simplifies to –rA = k’CAa where k’=kACBb ≈ k’=kACB0b and a can be determined
Repeat, but with an excess of A so that CA ≈ CA0
With excess A, rate simplifies to –rA = k’’CBb where k’’=kACAa ≈ k’’=kACA0a
Determine kA by measuring –rA at known concentrations of A and B, where

## Slide 4: Review: Differential Method
Plot DCA/Dt vs t
Determine dCA/dt from plot by graphical or numerical methods
  Draw rectangles on the graph. Then draw a curved line so that the area above the curve that is cut off of each rectangle approximately fills the unfilled area under the curve
  -dCA/dt is read using the value where the curve crosses a specified time
Plot ln(-dCA/dt) vs ln CA
0
0
Where –rA = kCAa
alpha power
Average slope
Curved line represents –dCA/dt
Slope of line = α
Insert α, –dCA,p/dt, & corresponding CA,p

## Slide 5: Review: Integral Method
A trial-and-error procedure to find reaction order
Guess the reaction order → integrate the differential equation
Method is used most often when reaction order is known and it is desired to evaluate the specific reaction rate constants (k) at different temps to determine the activation energy
Looking for the appropriate function of concentration corresponding to a particular rate law that is linear with time

## Slide 6
For the reaction A  products
For a first-order reaction - rA = k CA
ln (CA0/CA)
t
For a second-order reaction - rA = k CA2
1/CA
t
For a zero-order reaction -rA = k
CA
t
Plot of CA vs t is a straight line
Plot of ln(CA0/CA) vs t is a straight line
Plot of 1/CA vs t is a straight line

## Slide 7: Review: Method of Half-lives
A  products
ln (t1/2)
ln CA0
Slope = 1- 
Plot ln(t1/2) vs ln CA0. Get a straight line with a slope of 1-α
Half-life of a reaction (t1/2): time it takes for the concentration of the reactant to drop to half of its initial value

## Slide 8: Review: Method of Initial Rates
When the reaction is reversible, the method of initial rates can be used to determine the reaction order and the specific rate constant
Very little product is initially present, so rate of reverse reaction is negligible
  A series of experiments is carried out at different initial concentrations
  Initial rate of reaction is determined for each run
  Initial rate can be found by differentiating the data and extrapolating to zero time
  By various plotting or numerical analysis techniques relating -rA0 to CA0, we can obtain the appropriate rate law:

## Slide 9: Review: Differential Catalyst Bed
Conversion of reactants & change in reactant concentration in the bed is extremely small
FA0
Cp
CA0
FAe
Fp
W
L
r’A: rate of reaction per unit mass of catalyst
flow in - flow out + rate of gen = rate of accum.
When constant flow rate, u0 = u:
Product concentration
The reaction rate is determined by measuring product concentration, Cp

## Slide 10: L9: Reactor Design for Multiple Reactions
Usually, more than one reaction occurs within a chemical reactor
Minimization of undesired side reactions that occur with the desired reaction contributes to the economic success of a chemical plant
Goal: determine the reactor conditions and configuration that maximizes product formation
Reactor design for multiple reactions
  Parallel reactions
  Series reactions
  Independent reactions
  More complex reactions
  Use of selectivity factor to select the proper reactor that minimizes unwanted side reactions

## Slide 11: Classification of Multiple Reactions
A
B
C
k1
k2
A
C
B
k2
k1
A
B
k1
C
D
k2
2) Series reactions
Desired product
3) Independent reactions
Crude oil cracking
Desired product
4) Complex reactions
1) Parallel or competing reactions

## Slide 12: Parallel Reactions
Purpose: maximizing the desired product in parallel reactions
D
kD
A+B
U
kU
(desired)
(undesired)
Rate of disappearance of A:
Define the instantaneous rate selectivity, SD/U
Goal: Maximize SD/U to maximize production of the desired product

## Slide 13: Maximizing SD/U for Parallel Reactions: Temperature Control
What reactor conditions and configuration maximizes the selectivity?
Start with temperature (affects k):
a) If ED > EU
Specific rate of desired reaction kD increases more rapidly with increasing T
Use higher temperature to favor desired product formation
b) If ED < EU
Specific rate of desired reaction kD increases less rapidly with increasing T
Use lower T to favor desired product formation (not so low that the reaction rate is tiny)

## Slide 14: Maximize SD/U for Parallel Reactions using Temperature
What reactor temperature maximizes the selectivity?
ED = 20 kcal/mol, EU = 10 kcal/mol, T = 25 ◦C (298K) or 100 ◦C (373K)
SD/U is greater at 373K, higher temperature to favors desired product formation
A
U
D
kU
kD
kD/U
a) ED > EU
T = 25 ◦C
(298K):
T = 100 ◦C
(373K):

## Slide 15: Maximizing SD/U for Parallel Reactions: Concentration
What reactor conditions and configuration maximizes the selectivity?
Now evaluate concentration:
→ Use large CA
→ Use small CA
→ Use large CB
→ Use small CB
How do these concentration requirements affect reactor selection?
D
kD
A+B
U
kU

## Slide 16: Concentration Requirements & Reactor Selection
CA0u0
CB0u0
CAu0
CBu0
How do concentration requirements play into reactor selection?
CSTR: concentration is always at its lowest value (that at outlet)
PFR
PFR (or PBR): concentration is high at the inlet & progressively drops to the outlet concentration
CA(t)
CB(t)
D
kD
A+B
U
kU
Batch: concentration is high at t=0 & progressively drops with increasing time
Semi-batch: concentration of one reactant (A as shown) is high at t=0 & progressively drops with increasing time, whereas concentration of B can be kept low at all times
CBu0
CA

## Slide 17
D
kD
A+B
U
kU
b1 > b2
High CB favors desired product formation
b1 < b2
High CB favors undesired product formation
(keep CB low)
a1 > a2
High CA favors desired product formation
a1 < a2
High CA favors undesired product formation
(keep CA low)
PFR/PBR
Batch reactor
When CA & CB are low (end time or position), all rxns will be slow
High P for gas-phase rxn, do not add inert gas (dilutes reactants)
PFR/PBR w/ side streams feeding low CB
CB
←High CA
Semi-batch reactor, slowly
feed B to large amount of A
CB
CB
CB
CSTRs in series
B consumed before leaving CSTRn
CA0u0
CB0u0
CAu0
CBu0
CSTR
PFR/PBR
PFR/PBR w/ high recycle
Dilute feed with inerts that are easily separated from product
Low P if gas phase
PFR/PBR
Side streams feed low CA
←High CB
CA
Semi-batch reactor slowly feed A to large amt of B
CA
CA
CA
CSTRs in series

## Slide 18: Different Types of Selectivity
instantaneous rate selectivity, SD/U
overall rate selectivity,
instantaneous yield, YD
(at any point or time in reactor)
overall yield,
flow
batch
Evaluated at outlet
Evaluated at tfinal

## Slide 19: Series (Consecutive) Reactions
(desired)
(undesired)
A
D
U
k1
k2
Time is the key factor here!!!
Spacetime t for a flow reactor Real time t for a batch reactor
To maximize the production of D, use:
Batch
or
PFR/PBR
or
n
CSTRs in series
and carefully select the time (batch) or spacetime (flow)

## Slide 20: Concentrations in Series Reactions
A
B
C
k1
k2
-rA = k1CA
rB,net = k1CA – k2CB
How does CA depend on t?
How does CB depend on t?
Substitute
Use integrating factor (reviewed on Compass)

## Slide 21: Reactions in Series: Cj & Yield
The reactor V (for a given u0) and t that maximizes CB occurs when dCB/dt=0
so
A
B
C
topt