## Slide 1: Review: Analysis of Rate Data
Constant-volume batch reactor for homogeneous reactions: make concentration vs time measurements during unsteady-state operation
Differential reactor for solid-fluid reactions: monitor product concentration for different feed conditions during steady state operation
  Goal: determine reaction order, a, and specific reaction rate constant, k
Data collection is done in the lab so we can simplify BMB, stoichiometry, and fluid dynamic considerations
Want ideal conditions → well-mixed (data is easiest to interpret)
Method of Excess
Differential method
Integral method
Half-lives method
Initial rate method
Differential reactor
More complex kinetics

## Slide 2: Review: Method of Half-lives
A  products
ln (t1/2)
ln CA0
Slope = 1- 
Plot ln(t1/2) vs ln CA0. Get a straight line with a slope of 1-α
Half-life of a reaction (t1/2): time it takes for the concentration of the reactant to drop to half of its initial value

## Slide 3: Review: Method of Initial Rates
When the reaction is reversible, the method of initial rates can be used to determine the reaction order and the specific rate constant
Very little product is initially present, so rate of reverse reaction is negligible
  A series of experiments is carried out at different initial concentrations
  Initial rate of reaction is determined for each run
  Initial rate can be found by differentiating the data and extrapolating to zero time
  By various plotting or numerical analysis techniques relating -rA0 to CA0, we can obtain the appropriate rate law:

## Slide 4: Review: Differential Catalyst Bed
Conversion of reactants & change in reactant concentration in the bed is extremely small
FA0
Cp
CA0
FAe
Fp
W
L
r’A: rate of reaction per unit mass of catalyst
flow in - flow out + rate of gen = rate of accum.
When constant flow rate, u0 = u:
Product concentration
The reaction rate is determined by measuring product concentration, Cp

## Slide 5: Review: Multiple Rxns & Selectivity
A
B
C
k1
k2
A
C
B
k2
k1
2) Series rxns
3) Complex rxns
1) Parallel / competing rxns
Desired product
A+B C+D A+C E
k1
k2
instantaneous rate selectivity, SD/U
overall rate selectivity,
instantaneous yield, YD
(at any point or time in reactor)
overall yield,
flow
batch
at exit
at tfinal
Maximize selectivity / yield to maximize production of desired product

## Slide 6: Review: Maximizing SD/U for Parallel Rxns
What reactor conditions and configuration maximize selectivity?
a) If ED > EU
Specific rate of desired reaction kD increases:
Use higher temperature
b) If ED < EU
less rapidly with increasing T
Use lower temperature(not so low that the reaction rate is tiny)
more rapidly with increasing T
To favor production of the desired product
Now evaluate concentration:
→ Use large CA
→ Use small CA
→ Use large CB
→ Use small CB

## Slide 7: Concentration Requirements & Reactor Selection
CA0u0
CB0u0
CAu0
CBu0
How do concentration requirements play into reactor selection?
CSTR: concentration is always at its lowest value (that at outlet)
PFR
PFR (or PBR): concentration is high at the inlet & progressively drops to the outlet concentration
CA(t)
CB(t)
D
kD
A+B
U
kU
Batch: concentration is high at t=0 & progressively drops with increasing time
Semi-batch: concentration of one reactant (A as shown) is high at t=0 & progressively drops with increasing time, whereas concentration of B can be kept low at all times
CBu0
CA

## Slide 8
D
kD
A+B
U
kU
b1 > b2
High CB favors desired product formation
b1 < b2
High CB favors undesired product formation
(keep CB low)
a1 > a2
High CA favors desired product formation
a1 < a2
High CA favors undesired product formation
(keep CA low)
PFR/PBR
Batch reactor
When CA & CB are low (end time or position), all rxns will be slow
High P for gas-phase rxn, do not add inert gas (dilutes reactants)
PFR/PBR w/ side streams feeding low CB
CB
←High CA
Semi-batch reactor, slowly
feed B to large amount of A
CB
CB
CB
CSTRs in series
B consumed before leaving CSTRn
CA0u0
CB0u0
CAu0
CBu0
CSTR
PFR/PBR
PFR/PBR w/ high recycle
Dilute feed with inerts that are easily separated from product
Low P if gas phase
PFR/PBR
Side streams feed low CA
←High CB
CA
Semi-batch reactor slowly feed A to large amt of B
CA
CA
CA
CSTRs in series

## Slide 9: Different Types of Selectivity
instantaneous rate selectivity, SD/U
overall rate selectivity,
instantaneous yield, YD
(at any point or time in reactor)
overall yield,
flow
batch
Evaluated at outlet
Evaluated at tfinal

## Slide 10: Series (Consecutive) Reactions
(desired)
(undesired)
A
D
U
k1
k2
Time is the key factor here!!!
Spacetime t for a flow reactor Real time t for a batch reactor
To maximize the production of D, use:
Batch
or
PFR/PBR
or
n
CSTRs in series
and carefully select the time (batch) or spacetime (flow)

## Slide 11: Concentrations in Series Reactions
A
B
C
k1
k2
-rA = k1CA
rB,net = k1CA – k2CB
How does CA depend on t?
How does CB depend on t?
Substitute
Use integrating factor (reviewed on Compass)

## Slide 12: Reactions in Series: Cj & Yield
The reactor V (for a given u0) and t that maximizes CB occurs when dCB/dt=0
so
A
B
C
topt

## Slide 13
What reactor/reactors scheme and conditions would you use to maximize the selectivity parameters for the following parallel reaction?
Need to maximize SD/U1
Plug in numbers:
A+C D desired
kD
A+C U1 undesired
kU1
To maximize the production of the desired product, the temperature should be
  As high as possible (without decomposing the reactant or product)
  Neither very high or very low
  As low as possible (but not so low the rate = 0)
  Doesn’t matter, T doesn’t affect the selectivity
  Not enough info to answer the question
E/R
ED > EU, so use higher T

## Slide 14
What reactor/reactors scheme and conditions would you use to maximize the selectivity parameters for the following parallel reaction?
Need to maximize SD/U1
Plug in numbers:
A+C D desired
kD
A+C U1 undesired
kU1
To maximize the production of the desired product, CA should be
  As high as possible
  Neither very high or very low
  As low as possible
  Doesn’t matter, CA doesn’t affect the selectivity
  Not enough info to answer the question
αD < αU1, so high CA favors undesired product formation (keep CA low)

## Slide 15
What reactor/reactors scheme and conditions would you use to maximize the selectivity parameters for the following parallel reaction?
Need to maximize SD/U1
Plug in numbers:
Since ED>EU1, kD increases faster than kU1 as the temperature increases
aD<aU1, keep CA low to maximize CD with respect to CU1
rD and rU1 are 1st order in CC, so changing CC does not influence selectivity
A+C D desired
kD
A+C U1 undesired
kU1
Operate at a high temperature to maximize CD with respect to CU1
HOWEVER, high CC will increase the reaction rate and offset the slow reaction rate that is caused by low CA (that’s a good thing)
What reactor should we use?

## Slide 16
What reactor/reactors scheme and conditions would you use to maximize the selectivity parameters for the following parallel reaction?
Need to maximize SD/U1
aD<aU1, keep CA low to maximize CD with respect to CU1
rD and rU1 are 1st order in CC, so changing CC does not influence selectivity
A+C D desired
kD
A+C U1 undesired
kU1
ED>EU1, operate at a high temperature to maximize CD with respect to CU1
HOWEVER, high CC will increase the reaction rate and offset the slow reaction rate that is caused by low CA (that’s a good thing)
What reactor should we use?
←High CC
Semi-batch reactor slowly feed A to large amount of C
CA
PFR/PBR w/ side streams feeding low CA
A
C
PFR

## Slide 17
How does the selection of reactor/reactors scheme and conditions change if D can react with C and form another undesired product?
Need to maximize SD/U1 and SD/U2
A+C D desired
kD
A+C U1 undesired
kU1
D+C U2 undesired
kU2
aD<aU1, keep CA low
ED>EU1, operate at a high T
High CC increases rxn rate & offsets slow rxn from low CA
Since ED<EU21, kD increases slower than kU2 as T increases ⇨ operate at low T to maximize CD
aD>aU2, keep CA high to maximize CD
rD, rU1 & rU2 are all 1st order in CC, so changing CC does not influence selectivity, but high CC will offset the rate decrease due to low CA
Low CD reduces the production of U2
Conflicts with maximizing SD/U1!
Conflicts with maximizing SD/U1!
Conflicts with producing the product D!!!

## Slide 18
A
C
PFR, high T
Maximize SD/U1 & SD/U2
A+C D desired
kD
A+C U1 undesired
kU1
D+C U2 undesired
kU2
aD<aU1, keep CA low
ED>EU1, operate at a high T
Want to maximize CD
ED<EU2, operate at low T
aD>aU2, keep CA high
Low CD reduces production of U2
High CC increases rxn rate & offsets slow rate caused by low CA
Consider relative magnitude of SD/U1 and DD/U2 as a function of position in PFR
PFR w/ side streams feeding low CA
High T, CC is initially high, CA is low
→ high SD/U1
Initially CD=0 → rU2=0. Both gradually increase down reactor
Initially high SD/U2 (because CD is low), but SD/U2 gradually decreases down reactor
At some distance down the reactor, significant amounts of D have formed
SD/U2 becomes significant with respect to SD/U1
At this point, want low T, high CA & low CC
PFR 2, low T

## Slide 19
If a CSTR were used with CA = 1 mol/L and CD= 1 mol/L, at what temperature should the reactor be operated?
Need to maximize SD/(U1+U2)
A+C D desired
kD
A+C U1 undesired
kU1
D+C U2 undesired
kU2
CA=1
CD=1
Plot SD/(U1+U2) vs temperature to find the temperature that maximizes SD/(U1+U2)

## Slide 20
Chart: Temperature (K)
| 1 | 50 | 100 | 150 | 200 | 250 | 300 | 350 | 400 | 450 | 500 | 550 | 600 | 650 | 700 | 750 | 800 | 850 | 900 | 950 | 1000
Selectivity | 0 | 1.3711e-13 | 3.312e-06 | 0.00095738 | 0.016277 | 0.089102 | 0.27675 | 0.6218 | 1.1406 | 1.8231 | 2.6162 | 3.3577 | 3.7137 | 3.4086 | 2.6414 | 1.8521 | 1.2563 | 0.85682 | 0.59757 | 0.4284 | 0.31577
If a CSTR were used with CA = 1 mol/L and CD= 1 mol/L, at what temperature should the reactor be operated?
Need to maximize SD/(U1+U2)
A+C D desired
kD
A+C U1 undesired
kU1
D+C U2 undesired
kU2
SD/(U1+U2)
600K

## Slide 21
Calculate the yield of forming B in a CSTR and PFR when the conversion
of A is 90% and CA0 = 4 mol/L. The following reactions occur in the reactor:
A B
kB
A C
kC
What is the expression for the yield of B for a CSTR?
(overall yield)
We know CA0 and CA when XA=0.9. How do we get CB?
In - Out + Gen. = Accum.
0
0
Use the mole balance on A to find t (at 90% conversion)
In - Out + Gen. = Accum.
0

## Slide 22
A B
kB
A C
kC
What is –rA?
CA0 = 4 mol/L, and at XA=0.9, CA= 0.4 mol/L
Plug -rA back into expression for t
Residence time for XA = 0.9
Calculate the yield of forming B in a CSTR and PFR when the conversion
of A is 90% and CA0 = 4 mol/L. The following reactions occur in the reactor:

## Slide 23
Calculate the yield of forming B in a CSTR and PFR when the conversion
of A is 90% and CA0 = 4 mol/L. The following reactions occur in the reactor:
A B
kB
A C
kC
What is the expression for the yield of B for a PFR?
(overall yield)
Use the mass balance to get CB
Use the mole balance on A to find t (at 90% conversion)
0

## Slide 24
Calculate the yield of forming B in a CSTR and PFR when the conversion
of A is 90% and CA0 = 4 mol/L. The following reactions occur in the reactor:
A B
kB
A C
kC
Use mole balance on A to find t (at XA = 0.9)
CA0 = 4 mol/L
CA = 0.4 mol/L
Yield was better in the CSTR, but the residence time was longer